## Slide 1: TCP/IP: Concepts and IP Routing
Modernized 2026 edition (US English) | Rodolfo Nützmann
Based on the "TCP/IP Concepts" course presented at Technology Week, March 1999
Notes: Opening slide. This course is the modernized version of the "TCP/IP Concepts" material I presented in March 1999 (Technology Week), when I was a Field Network Engineer at Cabletron Systems. The original material derived from the "Level II Routing Student Guide" (J.P. Gorsky, 1995). What changed in this edition: 16:9 format; diagrams redrawn as native, editable objects; content updated for 2026 (CIDR, IPv6, EIGRP, BGP-4, PIM-SM, MPLS, VRRPv3); RFC references revised; example addresses moved to documentation or private ranges (RFC 5737, RFC 1918, RFC 7042). Suggested duration: two days (8 hours each), with subnetting exercises and a packet-capture lab between the modules.

## Slide 2: Course agenda
Module 1: General routing concepts
Heterogeneity and the components of an internetwork
Bridges and Layer 2 switches versus routers
Routable and nonroutable protocols (historical view)
Network-layer versus data-link addressing
Encapsulation and packet transmission
Static and dynamic routing
Distance vector: metrics, slow convergence and its fixes
Link state: principles, advantages and protocols
Autonomous systems
Module 2: TCP/IP
TCP/IP stack, IPv4 datagram, protocol and port numbers
IPv4 addressing: classes (legacy), CIDR, subnetting and VLSM
Host behavior: route determination and ARP (local, remote, proxy)
Complete transfer example across a routed internetwork
RIP, EIGRP, administrative distance and redistribution
OSPF in detail; IS-IS; BGP-4
ACLs, broadcasts, secondary addresses, unnumbered interfaces
IPv6: header, addressing, ND, routing, transition
IP multicast (IGMP, PIM), RSVP, MPLS and VRRP
Notes: Present the two modules and the selection criterion: Module 1 covers internetworking fundamentals and routing algorithms, independent of any protocol; Module 2 applies those concepts to the TCP/IP stack (IPv4 and IPv6), to the routing protocols and to the complementary technologies (multicast, MPLS, VRRP). Topics tagged LEGACY throughout the deck are kept for their teaching value or because they still show up in certification exams, but they do not represent current practice.

## Slide 3: From 1999 to 2026: what changed in this course
Topic | In 1999 | In 2026
LAN links | Ethernet 10/100, Token Ring, FDDI | Ethernet 1G to 400G, Wi-Fi 6/7; Token Ring and FDDI extinct
Network protocols | TCP/IP, IPX, AppleTalk, DECnet, SNA | IP only (IPv4 and IPv6); the rest is legacy
IPv4 addressing | Classes A/B/C, contiguous subnets | CIDR/VLSM (RFC 4632); IPv4 exhaustion (IANA 2011, LACNIC 2020); NAT and CGNAT
IPv6 | "IPng" in draft (RFC 1883) | RFC 8200 (2017); > 50% of Google access (Mar 2026); Brazil ≈ 59% (APNIC, Oct 2026)
IGP | RIP, IGRP, OSPF | OSPFv2/v3, IS-IS, EIGRP (RFC 7868); RIP only in small networks
EGP | EGP on the way out, BGP-4 arriving | BGP-4 (RFC 4271) universal; 32-bit ASNs (RFC 6793)
Multicast | DVMRP, MOSPF, MBone | PIM-SM/SSM (RFC 7761, RFC 4607), IGMPv3/MLDv2
Gateway redundancy | VRRP just published (RFC 2338) | VRRPv3 (RFC 5798) for IPv4 and IPv6; HSRP
Layer 2 interconnection | Bridges, STP 802.1D | Multilayer switches, RSTP/MSTP, 802.1Q VLANs, EVPN
Notes: This slide is new. It calibrates expectations: almost every concept from 1999 is still valid, but the technology context changed radically. Use it to explain why some topics (Token Ring, NetWare/IPX, EGP, IGRP, MBone) now appear only as history. Data verified in October 2026: native IPv6 access to Google exceeded 50% for the first time on March 28, 2026 (50.10%, per Internet Society Pulse using Google data); in Brazil, the APNIC Labs measurement on October 5, 2026 showed about 59% of users as IPv6 capable. References: Internet Society Pulse, "18 years later, IPv6 reaches majority" (2026); APNIC Labs, IPv6 Capability Metrics, Brazil (BR).

## Slide 4: General routing concepts
MODULE 1
Internetworking, bridges and switches, routers, logical addressing, static and dynamic routing, distance vector, link state and autonomous systems
Notes: Module 1 divider. In the original, this module included objectives about the Cabletron router product line and basic Cisco router operations; both were removed as product-specific and dated. The module is now vendor neutral.

## Slide 5: Module 1 objectives
1
Internetworking vocabulary
Recognize the basic internetworking terms and concepts: LAN and WAN links, interconnection devices, broadcast and collision domains.
2
Bridges and switches versus routers
Compare the operation of bridges/Layer 2 switches and routers, and understand Layer 2 and Layer 3 switching.
3
Routable protocols
Describe the properties of a routable protocol and put nonroutable protocols in historical context.
4
Distance vector
Explain the principle of operation, the inherent instability (slow convergence) and the techniques that correct it.
5
Link state
Explain SPF (Dijkstra) algorithms, their advantages over distance vector and the protocols that implement them.
6
Autonomous systems
Define autonomous system and distinguish interior from exterior routing protocols.
Notes: Read the objectives with the class. By the end of the module the student should be able to explain, in their own words, why a switch and a router make decisions at different layers and why link-state algorithms converge faster than distance-vector ones. 2026 update: the original objectives 'recall the router products in the Cabletron product line' and 'basic Cisco router operations' were replaced by 'recognize Layer 2 and Layer 3 switching' and 'describe autonomous systems', topics the 1999 course already covered but did not list.

## Slide 6: Heterogeneity: the reason internetworks exist
WAN / Internet
(IPv4 + IPv6)
R1
R2
R3
Campus: 1G Ethernet
PC
PC
SW
Campus: Wi-Fi 6 (802.11ax)
Lap
Cel
AP
Data center: 25/100G Ethernet
Srv
Srv
ToR
Public cloud
(VPC)
In 1999 the challenge was making TCP/IP and NetWare coexist on Token Ring and Ethernet; in 2026 the challenge is connecting campus, Wi-Fi, data center and cloud under a single protocol: IP.
Notes: In the 1999 slide the heterogeneity was in the protocols: Token Ring and Ethernet segments carrying TCP/IP and NetWare at the same time. Today the heterogeneity is in the links (Ethernet, Wi-Fi, fiber, 5G, WAN) and in the administrative domains (campus, data center, public clouds), while the network layer converged on IP. The role of the interconnection devices is still the same: let stations on different links communicate as if they were on a single logical network. 2026 update: Token Ring (IEEE 802.5) and FDDI stopped being manufactured in the 2000s; NetWare/IPX was discontinued by Novell. Both appear in the original diagram and were replaced.

## Slide 7: Components of an internetwork
LAN links
IEEE 802.3 Ethernet: 1G, 10G, 25G, 100G, 400G
IEEE 802.11 Wi-Fi (ax, be)
One broadcast domain per VLAN
Legacy: Token Ring, FDDI, ARCnet
WAN links
Leased circuits, dark fiber, Metro Ethernet
Carrier MPLS (L3VPN, L2VPN)
Public Internet with tunnels (IPsec, SD-WAN)
4G/5G, LEO satellite
Legacy: serial lines, Frame Relay, X.25, ATM
Interconnection devices
Bridge / Layer 2 switch (forwards by MAC)
Router (forwards by IP address)
Layer 3 switch (routing in ASIC)
Legacy: repeaters and hubs (Layer 1)
TCP/IP internetworks are connectionless: every packet is forwarded independently, hop by hop.
Notes: Three elements build any connectionless internetwork: local links, long-distance links and the devices that interconnect them. The original listed only bridges and routers as interconnection devices; today we add Layer 2 switches (which are multiport bridges) and Layer 3 switches (routers implemented in ASIC hardware). Note that firewalls, load balancers and VPN gateways also interconnect networks, but they operate at higher layers and will be mentioned only when needed.

## Slide 8: Interconnection devices and the OSI model
7 Application
6 Presentation
5 Session
4 Transport
3 Network
2 Data link
1 Physical
Hub / repeater
LEGACY
7 Application
6 Presentation
5 Session
4 Transport
3 Network
2 Data link
1 Physical
Bridge / L2 switch
7 Application
6 Presentation
5 Session
4 Transport
3 Network
2 Data link
1 Physical
Router
7 Application
6 Presentation
5 Session
4 Transport
3 Network
2 Data link
1 Physical
L3 switch
The highlighted layer is the one that decides forwarding: destination MAC (Layer 2) or destination IP address (Layer 3). An L3 switch routes between VLANs with the same logic as a router, but in ASIC.
Notes: Use the diagram to fix the rule: each device decides based on the highest layer it understands. The hub repeats bits (Layer 1); the bridge/switch learns and forwards by MAC address (Layer 2); the router forwards by IP address (Layer 3). Layer 3 switches combine the last two functions in hardware. 2026 update: hubs and repeaters disappeared with switched full-duplex Ethernet; they are kept only as a Layer 1 reference.

## Slide 9: Bridges and Layer 2 switches
Application
Presentation
Session
Transport
Network
Data link
Physical
Source system
Application
Presentation
Session
Transport
Network
Data link
Physical
Destination system
Bridge function (MAC table)
Bridge / L2 switch
Physical
Physical
LAN link A
LAN link B
Operates at the data link layer: decides by destination MAC
Transparent to the stations: does not alter frames
An Ethernet switch = a multiport bridge in hardware
Standard: IEEE 802.1D (now folded into IEEE 802.1Q)
Notes: The transparent bridge (IEEE 802.1D, 1990) is the direct ancestor of the Ethernet switch: a switch is a multiport bridge with hardware forwarding. The diagram shows the bridge operating only up to the data link layer: it neither reads nor changes the IP header. Key point: the bridge is 'transparent' because the stations do not know it exists; frames reach the destination with the same source and destination MAC addresses they left with.

## Slide 10: Frame flow through a bridge or switch
1
Learn
Record the source MAC (SA) and the arrival port in the MAC table; refresh the aging timer.
2
Look up
Search for the destination MAC (DA). Found on another port: forward. Found on the same port: filter (discard).
3
Flood
Unknown DA, broadcast or multicast: send the frame out every port except the one it arrived on (flooding).
4
Age out
Entries without traffic are removed after the aging time (default 300 s), letting stations move between ports.
MAC | Port | Age (s)
00-00-5E-00-53-01 | 1 | 12
00-00-5E-00-53-02 | 1 | 40
00-00-5E-00-53-0A | 2 | 3
00-00-5E-00-53-0B | 3 | 275
MAC table (SAT / CAM) of a switch
SW1
port 1
port 2
port 3
01
0A
0B
Notes: Describe the learning-bridge algorithm: (1) for every frame received, the bridge records the source MAC and the arrival port in the address table (SAT, Source Address Table, today called the MAC table or CAM); (2) it looks up the destination MAC; if present in the table, it forwards out the learned port (or filters, if it is the arrival port); if absent, or if it is broadcast/multicast, it floods out all other ports; (3) every entry has an aging timer (300 s by default in IEEE 802.1D) refreshed by each frame received from that source. This is exactly the behavior of any modern Ethernet switch, just executed in ASIC with per-VLAN tables.

## Slide 11: Switched network: broadcast domain and Spanning Tree
SW1
SW2
SW3
active (forwarding)
blocked (STP)
A
User A
B
User B
C
User C
The initial communication from A to B is a broadcast (e.g., ARP Request): every switch floods it, every station examines it
After B replies, the switches know the MACs and forward only along the learned path
Redundant links are held in standby by Spanning Tree (IEEE 802.1D/802.1w): with no TTL in the frame, an L2 loop would be permanent
The whole set forms a single broadcast domain (one VLAN)
Modern segmentation
VLANs (802.1Q) create several broadcast domains on the same switch
RSTP/MSTP converge in seconds; EVPN/VXLAN replaces STP in data centers
Notes: Example: user A wants to talk to user B through two switches. The initial communication (ARP, for instance) is a broadcast, which every switch floods. So every segment and every station receives and examines the broadcast. Once B answers, the switches have learned the MACs of A and B and forward the unicast frames only along the needed path. Redundant paths (the dashed links) are blocked by Spanning Tree to avoid Layer 2 loops, which would be catastrophic because the Ethernet frame has no TTL. 2026 update: the original STP (802.1D) took 30 to 50 s to converge; RSTP (802.1w, 2001) converges in seconds and MSTP (802.1s) handles groups of VLANs. In data centers STP was replaced by IP fabrics with EVPN/VXLAN.

## Slide 12: Layer 2 switching: advantages and limitations
Advantages
Cost: lower price per port than routers
Performance: does not parse the network-layer header; line-rate forwarding in ASIC
Plug and play: learns addresses by itself; little configuration
Protocol independence: carries any Layer 2 payload (IP, ARP, LLDP, legacy protocols)
Limitations
Broadcast: no protection against broadcast storms; the failure domain grows with the network
Topology: uses only a subset of the links (spanning tree); classic STP converges in 30 to 50 s (RSTP: seconds)
MTU: does not fragment; frames larger than the MTU of the egress link are dropped
No congestion feedback to the stations (Ethernet frame flow is not end to end)
Scale: 802.1D recommended a maximum diameter of 7 bridges; today the limit is a design choice (size of the broadcast domain)
Notes: The advantages listed in 1999 are still valid: cost per port, performance and simplicity. 'Protocol independence' lost importance once IP became the only network protocol, but it is still the reason Layer 2 protocols (LLDP, STP, ARP) work across switches and not across routers. Among the limitations, broadcast storms and the failure scope remain the main argument for segmenting with routing (VLANs plus inter-VLAN routing). The old '7 bridges and 8 networks' rule was the maximum diameter 802.1D recommended so that the STP timers would work; with RSTP and star topologies that rule is no longer applied as a hard limit, but the principle (keep the broadcast domain small) stands. 2026 update: 'bridges drop oversized packets' referred to the different MTUs of Token Ring (up to 17,914 bytes) and Ethernet (1,500); with universal Ethernet and jumbo frames the problem practically disappeared.

## Slide 13: Routers
Operate at the network layer of the OSI model (the Internet layer of TCP/IP)
Forward packets from end station to end station, allowing multiple paths between them (ECMP)
Routing decision based on the network address (IP), not the data-link (MAC) address
Bound broadcast domains: traffic isolation and the natural place for policy and security
Take part in a distributed algorithm (routing protocol) to choose the optimal path
Rewrite the data-link header at every hop and decrement the TTL (IPv4) / Hop Limit (IPv6)
Application
Presentation
Session
Transport
Network
Data link
Physical
Source
Application
Presentation
Session
Transport
Network
Data link
Physical
Destination
Routing function
Data link
Physical
Data link
Physical
Router
Link A
Link B
Notes: The router performs its function at the network layer. Unlike the bridge, it makes the forwarding decision from the destination network (IP) address, rewrites the data-link headers at every hop and takes part in a distributed algorithm to compute the paths. Explain the phrase 'allows multiple paths': unlike STP, which blocks redundant links, IP routing uses all the links and can even load-balance across equal-cost paths (ECMP).

## Slide 14: End systems and intermediate systems
Transport
Network
Data link
Physical
End system A
Transport
Network
Data link
Physical
End system B
Network
Intermediate system 1
Data link
Physical
Data link
Physical
Network
Intermediate system 2
Data link
Physical
Data link
Physical
End-to-end transport connection (TCP)
End systems (hosts) implement every layer; the transport connection is end to end
Intermediate systems (routers) implement up to the network layer and treat every packet independently
Reliability, ordering and flow control belong to TCP at the endpoints; the router may drop packets
Notes: ISO terminology: end systems (the hosts) implement all the layers; intermediate systems (the routers) implement only up to the network layer. The transport connection (TCP) is end to end and crosses the routers without being interpreted by them. This explains why reliability (retransmission, flow control) is the hosts' responsibility, and why a router may drop packets under congestion: TCP at the endpoints will notice and react.

## Slide 15: Data flow inside a router
Control plane (CPU, software)
Routing protocols
(OSPF, BGP, ...)
RIB: routing table
(every learned route)
ARP / ND
(neighbor resolution)
Management, ACLs,
policies
programs
Data plane (ASIC or software forwarding)
Ingress
interface
(buffer)
Strip data-link
header; validate
IP, checksum, TTL
FIB: longest
prefix match
lookup
Adjacency:
new data-link
header; TTL-1
Egress queues
(QoS)
Egress
interface
RIB (Routing Information Base) = what the router knows; FIB (Forwarding Information Base) = what it uses to forward. Packets addressed to the router itself go up to the control plane.
Notes: The original diagram showed a 1999 router: a hardware buffer per interface, a software buffer, the routing table, the ARP cache and a hold queue. The 2026 version separates control plane and data plane: the control plane (CPU) runs the routing protocols and builds the RIB (routing table); from it derives the FIB, the compact table the data plane (ASIC or optimized software) uses to forward at line rate. The adjacency table (ARP/ND) supplies ready-made data-link headers. Step by step: the frame arrives, the data-link header is removed, the IP packet is validated (checksum, TTL), the FIB is consulted by longest prefix, the TTL is decremented, a new data-link header is built and the frame is queued on the egress interface (where QoS policies act).

## Slide 16: Routers: advantages and limitations
Advantages
Broadcast isolation: every interface (or VLAN) is a separate broadcast domain
Path selection: uses the best physical path available; load-balances across equal-cost paths (ECMP)
Flexibility: any topology, including redundant meshes with no blocked links
Practically unlimited scale: the Internet is a routed network
Policy point: ACLs, QoS, NAT, tunnels
Limitations
Protocol dependence: only forwards what it is configured to route (today: IPv4 and IPv6)
Throughput: in 1999, software routing was slower than bridging; in 2026, L3 switches and ASIC routers forward at line rate
Configuration complexity: addressing, protocols, policies; hosts need an address, mask and gateway (automated by DHCP/SLAAC)
Cost: more complex and more expensive devices per port
Notes: Compare with the switch slide. The router's main advantage is bounding the broadcast and failure domain; its main historical disadvantage was performance, because in 1999 routing was done in software on a general-purpose CPU. Today Layer 3 switches and core routers forward in ASIC at line rate, so the throughput argument has practically vanished; what remains is configuration complexity and cost. 'Protocol dependence' also stopped being a practical problem: a modern router only needs to handle IPv4 and IPv6 (dual stack).

## Slide 17: Routable and nonroutable protocols
LEGACY
Routable protocols
Use a layered structure close to the OSI model, with a network layer and a hierarchical logical address (network + node)
Designed for internetworks with several LAN/WAN links joined by routers
In use (2026): IPv4 (RFC 791) and IPv6 (RFC 8200)
Legacy: XNS, Novell IPX, AppleTalk, DECnet Phase IV and DECnet/OSI, Banyan VINES, ISO CLNP, Xerox PUP
Nonroutable protocols
Do not implement a network layer, or use a flat addressing scheme (no 'network' part)
Designed for a single link or an extended LAN (with bridges)
Legacy: NetBIOS/NetBEUI, SNA (subarea and APPN), DEC LAT, DEC MOP
Still today, by design: ARP, STP, LLDP and other Layer 2 protocols stay confined to the link
How to 'route' the nonroutable: encapsulation over IP. NetBIOS moved to TCP/UDP (RFC 1001/1002, ports 137 to 139); SNA was carried by DLSw (RFC 2166) and later by Enterprise Extender; in general, tunnels and Layer 2 VPNs (EVPN/VXLAN, L2TPv3) extend a link across a routed network.
Bottom line for 2026: 'routable protocol' means IP. The criterion is still useful to explain why ARP, STP and LLDP do not cross routers.
Notes: A protocol is 'routable' when it has a network layer with hierarchical logical addressing (network + node), letting routers forward its packets between different links. In 1999 this mattered because corporate networks carried several protocols at once; the routers of the day (Cabletron, Cisco) routed IP, IPX, AppleTalk and DECnet simultaneously. In 2026 the list shrank to IPv4 and IPv6. The nonroutable protocols (NetBIOS/NetBEUI, SNA, LAT, MOP) either disappeared or were encapsulated over IP (NetBIOS over TCP/IP, RFC 1001/1002; SNA over DLSw or Enterprise Extender). The concept, however, is still useful: Layer 2 protocols such as ARP, STP and LLDP stay confined to the link and do not cross routers.

## Slide 18: Addressing: network layer versus data link layer
Data-link address (MAC)
48 bits (EUI-48): 24-bit manufacturer OUI + 24-bit serial
Flat: says nothing about where the interface is in the internetwork
Scope: valid only within the link (broadcast domain)
Example (RFC 7042 documentation range): 00-00-5E-00-53-1A
Network address (IP)
Logical and hierarchical: network (prefix) + node (host)
Scope: unique across the whole internetwork (the Internet, when public)
Assigned by the administrator, DHCP (IPv4/IPv6) or SLAAC (IPv6)
Examples: 172.16.20.10/24 (IPv4), 2001:db8:20::10/64 (IPv6)
General structure of a network-layer address
Network (prefix): which link?
Node (host): which interface on the link?
IPv4: 172.16.20 | .10 IPv6: 2001:db8:20:: | :10 (the boundary is set by the mask or the prefix length)
In 1999 every routable protocol had its own scheme (IPX: 32-bit network + node = MAC; AppleTalk: 16-bit network + 8-bit node). Today, only IPv4 and IPv6.
Notes: Two address spaces coexist in every internetwork: the data-link address (MAC, 48 bits on Ethernet and Wi-Fi), which identifies the interface within a link and comes burned in by the manufacturer (or is locally assigned), and the network address (IP), logical and hierarchical, which identifies the system across the whole internetwork and is assigned by the administrator or by DHCP/SLAAC. The network address has two components: the network part (prefix), which the router uses to decide the next hop, and the node (host) part, which identifies the interface within that network. The mapping between the two spaces is done by ARP (IPv4) or Neighbor Discovery (IPv6).

## Slide 19: Packet transmission: down the stack
Transport
Network
Data link (MAC)
Physical
Sender
Transport
Network
Data link (MAC)
Physical
Receiver
Data unit at each layer (PDU)
TCP/UDP header
Data
Segment
IP header
TCP/UDP header
Data
Packet
Ethernet hdr
IP header
TCP/UDP header
Data
FCS
Frame
bits on the physical medium
Each layer adds its header on the way out and removes it on the way in (encapsulation)
The frame's EtherType (0x0800 IPv4, 0x86DD IPv6, 0x0806 ARP) identifies the network protocol
Legacy: the IEEE 802.3 format with LLC/SNAP (LLC-PDU) was common in 1999; today IP over Ethernet uses Ethernet II; Wi-Fi still uses LLC/SNAP
Notes: Follow the diagram top to bottom on the sender and bottom to top on the receiver: the transport layer hands a segment to the network layer, which adds the IP header and forms the packet (datagram); the data-link layer encapsulates the packet in a frame with a header (MACs and EtherType) and a trailer (FCS); the physical layer transmits the bits. In the original Ethernet and in IEEE 802.3 with LLC/SNAP there was an LLC sublayer between the network and MAC layers (the 1999 slide showed LLC-PDU and MAC-PDU). Today practically all IP over Ethernet uses the Ethernet II (DIX) format with an EtherType field (0x0800 for IPv4, 0x86DD for IPv6), without LLC; the LLC sublayer survives in Wi-Fi (802.11 uses LLC/SNAP).

## Slide 20: Encapsulation: an IPv4 packet inside an Ethernet frame
Ethernet II frame (IEEE 802.3 with EtherType)
Preamble
7 B
SFD
1 B
Destination MAC
6 B
Source MAC
6 B
EtherType
2 B (0x0800)
Data: IP packet
46 to 1,500 B
FCS
4 B
IPv4 packet (datagram), RFC 791
bit 0
bit 31
Version
IHL
DSCP
ECN
Total length
Identification
Flags
Fragment offset
Time to live (TTL)
Protocol
Header checksum
Source IP address
Destination IP address
Options (rare)
Padding
Transport-layer data (TCP/UDP segment), up to 65,515 bytes
Minimum IPv4 header: 20 bytes (IHL = 5). Ethernet MTU of 1,500 bytes: larger packets are fragmented (IPv4) or dropped with ICMP 'Packet Too Big' (IPv6).
Notes: The Ethernet II frame carries: preamble (7 bytes) and start frame delimiter (SFD, 1 byte), destination MAC, source MAC, EtherType (2 bytes) and a data field of 46 to 1,500 bytes, followed by the FCS (CRC-32). Inside the data field goes the IP packet: a 20-byte header (without options) and a payload of up to 65,535 bytes in total, which forces fragmentation whenever the packet exceeds the 1,500-byte MTU. The IPv4 header is detailed in Module 2. Note already that the Type of Service (ToS) field of the original slide was redefined as DSCP + ECN (RFC 2474 and RFC 3168).

## Slide 21: Routing algorithms: how routers learn about networks
Manual configuration: static routes
The administrator enters prefix, mask and next hop
Default route (0.0.0.0/0 or ::/0) as 'everything else'
Predictable, no control traffic, no CPU
Does not react to failures (unless tracked with IP SLA/BFD)
Automatic distribution: dynamic routing
Routers exchange information and compute paths
Distance vector: RIP, EIGRP (advanced distance vector)
Link state: OSPF, IS-IS
Path vector: BGP (between autonomous systems)
Reacts to failures and topology changes (convergence)
Rule of thumb: static at the edges (stubs and default), dynamic in the core. The final routing table combines both sources, arbitrated by administrative distance (Module 2).
Notes: Opening question: how does a router discover every network and subnet in an internetwork? Two methods: manual configuration (static routes) or automatic distribution by a distributed adaptive (dynamic) routing protocol. In practice both are used: static routes for leaf networks and the default route; dynamic protocols for the core. The next slides walk through: static routing, dynamic routing, distance vector (with its problems and fixes) and link state.

## Slide 22: Static routing
All routing information is precomputed and supplied by manual configuration
Must be recomputed and reapplied on every topology change
Unsuitable for large, dynamic internetworks
Ideal for stub networks (a single path) and for the default route
No protocol overhead; fully predictable behavior
Internetwork
(dynamic routing)
R3
R4
R1
R2
single path
Network A (stub): 172.16.40.0/24
! on R2 (default route)
ip route 0.0.0.0 0.0.0.0 R1
! on R1 (route to network A)
ip route 172.16.40.0 /24 R2
Notes: All routing information is precomputed by the administrator and entered manually. If the topology changes, someone must recompute and reconfigure. That is why static routing does not scale to large, dynamic internetworks, yet it is still the right choice for stub (leaf) networks, which have a single way out. Diagram example: network A sits behind R2, with a single link to R1. On R2 a default route pointing to R1 is enough; on R1 a static route to network A via R2 is enough. No dynamic protocol needs to run on that link. 2026 update: static routes can be conditioned on reachability checks (IP SLA, BFD) and are widely used at Internet edges and in public clouds (VPC route tables).

## Slide 23: Distributed adaptive (dynamic) routing
Distance vector
'Routing by rumor': each router advertises to its neighbors the distance (metric) to each destination
Bellman-Ford algorithm
Simple; converges more slowly; subject to transient loops
RIP (RFC 2453), EIGRP (RFC 7868, 'advanced')
Link state
Each router floods a description of its links (LSA); everyone builds the same map
Dijkstra's SPF algorithm
Converges fast; scales with areas; more CPU and memory
OSPF (RFC 2328 / 5340), IS-IS (RFC 1195)
Path vector
Advertises the full path (list of ASs) to each destination; avoids loops by inspecting the path
Policy based, not metric based only
Between autonomous systems (and inside large data centers)
BGP-4 (RFC 4271)
Routers sense the local environment, exchange information with each other and jointly run a distributed algorithm to determine the optimal path.
Notes: Routers dynamically sense their local environment (active interfaces, neighbors) and exchange that information among themselves in a distributed fashion, with no central controller. Together they run a distributed algorithm that determines the optimal route between any two stations. Two families dominate the interior protocols: distance vector (each router tells its neighbors 'how far I am from each destination') and link state (each router tells everyone 'these are my links and their costs', and each one computes the complete map). BGP, used between autonomous systems, is a path vector: it advertises the list of ASs traversed.

## Slide 24: Distance-vector routing
Each router keeps the distance (metric) from itself to every possible destination and the vector (outgoing neighbor)
Learns the topology by exchanging complete tables with direct neighbors at periodic intervals
On receiving a neighbor's update, it updates the table when:
  the destination was unknown
  the advertised route is shorter than the known one
  the current route already goes through that neighbor and the advertised distance changed (accepted even if worse)
Based on the Bellman-Ford algorithm; no view of the full map ('routing by rumor')
R1
R2
Network A
Net | Metric | Via
A | 1 | R1
R2 learns 'A at 1 hop via R1' from R1's periodic advertisement
A: 0
Notes: Each router keeps, for every known destination, the distance (metric) and the neighbor through which it is reached (the vector). Periodically it sends its whole table to its direct neighbors (RIP: every 30 s). On receiving an update from a neighbor, the router updates its table when: (1) the destination was unknown; (2) the new route is shorter than the known one; (3) the current route already goes through that neighbor and the advertised distance changed (up or down), in which case the change is accepted even if it is worse. The third case is what lets the news that a destination got worse or went down propagate, and it is also the entry point of the count-to-infinity problem, shown next.

## Slide 25: Routing metrics
How the 'distance' between source and destination is measured
Hop count (RIP), bandwidth and delay (EIGRP), administrative cost (OSPF, IS-IS), reliability, load
The metric defines what 'best path' means to the protocol
Hops ignore capacity: 1 hop at 2 Mbps may be worse than 2 hops at 1 Gbps
R1
R2
R3
WAN 2 Mbps (1 hop)
1 Gbps
1 Gbps
A
B
Path A → B | Hops (RIP) | Minimum bandwidth | Choice
R1 → R2 | 1 | 2 Mbps | RIP
R1 → R3 → R2 | 2 | 1 Gbps | EIGRP / OSPF
Notes: A metric is the way to measure the 'distance' between source and destination. Hop count (RIP) is the simplest, but it ignores link capacity: in the diagram, the two-hop path over 1 Gbps links is better than one hop over a 2 Mbps link. That is why EIGRP uses bandwidth and delay, and OSPF/IS-IS use an administrative cost derived from bandwidth. 2026 update: the original speeds (56 kbps, 1.544 Mbps T1, 10 Mbps) were replaced by current values, but the lesson is the same.

## Slide 26: The slow convergence problem (count to infinity)
Network A
R1
R2
R3
Net | Metr. | Via
A | 0 | direct
Net | Metr. | Via
A | 1 | R1
Net | Metr. | Via
A | 2 | R2
"A: 0"
"A: 1"
"A: 2" (ignored)
Three routers (R1 to R3), each with a route to network A
Periodic advertisements in every direction: R1 → R2 'A: 0', R2 → R3 'A: 1', and also R3 → R2 'A: 2'
While everything works, R2 ignores R3's advertisement because it already has a better route (1 via R1)
Notes: Initial scenario: three routers in a row; R1 is directly connected to network A (metric 0 or 1, depending on the protocol), R2 reaches A via R1 (metric 1) and R3 via R2 (metric 2). Everyone periodically advertises their tables to their neighbors: R1 says 'A: 0', R2 says 'A: 1', R3 says 'A: 2'. With advertisements in every direction (no split horizon), R2 also receives from R3 that 'A is at 2 via R3', which it ignores for now because its current route (1 via R1) is better.

## Slide 27: Slow convergence: the failure creates a loop
Network A
R1
R2
R3
X failure
Net | Metr. | Via
A | 16 (∞) | -
Net | Metr. | Via
A | 3 | R3
Net | Metr. | Via
A | 2 | R2
"A: 2" accepted!
later: "A: 3"
loop R2 ⇄ R3
The link to A fails; R1 marks A as unreachable (RIP: metric 16 = infinity)
R2 loses the route via R1, but R3 still advertises 'A: 2' (via R2!); R2 accepts: 'A: 3 via R3' → loop
Every cycle the metric climbs by 1 (3, 4, 5...) up to infinity: count to infinity; with advertisements every 30 s, convergence takes minutes
Notes: The link from R1 to network A goes down. R1 marks A as unreachable (infinite metric, 16 in RIP). Before R1 advertises that, R2 receives (or already had) from R3 the advertisement 'A: 2'. Having lost its route via R1 (or receiving 'A: 16' from R1), R2 accepts R3's route: 'A: 3 via R3'. But R3 reached A via R2! A loop has formed: packets for A go R2 → R3 → R2 → R3 until the TTL expires. Worse: in the following updates, R2 advertises 'A: 3' to R3, which moves to 'A: 4 via R2', which advertises 'A: 4' to R2, which goes to 5, and so on until the metric reaches infinity (16 in RIP, which is why the limit is so low). This is count to infinity; with updates every 30 s, it can take minutes.

## Slide 28: Fix 1: split horizon
A
B
C
172.16.10.0
172.16.20.0
172.16.30.0
172.16.40.0
Advertisements from A
→ to the right: 10.0, 20.0
← to the left: (no neighbor)
Advertisements from B
→ to the right: 10.0, 20.0, 30.0
← to the left: 30.0, 40.0
Advertisements from C
→ to the right: (no neighbor)
← to the left: 30.0, 40.0
Rule: a route learned on an interface is never advertised back out that same interface.
B learned 10.0 and 20.0 from A: does not advertise them back to A; learned 40.0 from C: does not advertise it to C
Eliminates the loop between two direct neighbors; does not solve loops in rings of three or more routers
Used by RIP and EIGRP; enabled by default in most implementations
Notes: Rule: never advertise a route back out the interface you learned it from. In the three-routers-in-a-row example, router B learned 10.0 and 20.0 from A, so it does not advertise them back to A; it learned 40.0 from C, so it does not advertise it to C. R3 would therefore never tell R2 'A: 2', and the loop of the previous slide never forms. The diagram shows what each router advertises in each direction with simple split horizon. Note that split horizon solves loops between two direct neighbors, but not loops with three or more routers in a ring; that is why it is combined with hold-down and triggered updates. Addresses updated to the private range 172.16.0.0/12 (RFC 1918); the original used 134.141.x.0, a block that belonged to Cabletron at the time.

## Slide 29: Fix 2: split horizon with poison reverse
A
B
C
172.16.10.0
172.16.20.0
172.16.30.0
172.16.40.0
Advertisements from A
→ right: 10.0, 20.0, 30.0 (∞), 40.0 (∞)
← left: (no neighbor)
Advertisements from B
→ right: 10.0, 20.0, 30.0, 40.0 (∞)
← left: 10.0 (∞), 20.0 (∞), 30.0, 40.0
Advertisements from C
→ right: (no neighbor)
← left: 10.0 (∞), 20.0 (∞), 30.0, 40.0
Rule: the route learned on an interface is advertised back out of it with an infinite metric (∞ = 16 in RIP).
Makes it explicit to the neighbor that it must not use this router for that destination
Breaks loops faster than simple split horizon, at the cost of larger updates
Default in RIP on many implementations; EIGRP uses simple split horizon and route poisoning when withdrawing a destination
Notes: A more aggressive variant: instead of omitting the route learned on an interface, the router advertises it back out that interface with an infinite metric (16 in RIP). B tells A: '10.0 and 20.0 are unreachable through me', making it explicit that A must not use B to reach them, even if A loses its route. The cost is larger updates (every route is advertised on every interface). The benefit is breaking loops faster, including some that simple split horizon does not prevent.

## Slide 30: Fix 3: hold-down timer
1
Network goes down
The router receives (or generates) the 'destination unreachable' advertisement and starts the hold-down timer for that destination (Cisco RIP: 180 s).
2
Waiting period
Ignores any advertisement claiming the destination is back with an equal or worse metric; keeps forwarding on the old route (marked possibly down).
3
Exceptions
Immediately accepts an advertisement with a better metric or one coming from the neighbor that originally reported the route.
4
Expiration
When the timer expires, advertisements are accepted normally again. The news of the failure has reached every router.
Goal
Wait long enough to make sure all routers are notified of the down route and not mistakenly accept an out-of-date message (still circulating) that claims the route exists.
Cost
Delays the convergence of routes that legitimately came back. Modern protocols (EIGRP/DUAL, OSPF) do without long timers.
Notes: On receiving the information that a network became unreachable, the router enters hold-down for that destination: for a fixed time (180 s in Cisco's RIP) it ignores advertisements claiming the network is back with an equal or worse metric, accepting only better advertisements or ones from the original neighbor. The idea is to wait long enough for the news of the failure to reach everyone, avoiding the acceptance of stale information still circulating. Side effect: the convergence of a route that really came back is delayed by the same amount. That is why modern protocols prefer mechanisms that do not depend on long timers (EIGRP with DUAL, link state with SPF).

## Slide 31: Fix 4: triggered updates
The router sends the update immediately on detecting a change in the routing table, without waiting for the period
The triggered update contains only the routes that changed
Speeds up convergence and shrinks the window in which stale information circulates
Typical RIP combination: split horizon + poison reverse + hold-down + triggered updates
EIGRP: only triggered, reliable updates (RTP); no periodic table advertisements
R1
R2
Network A
t = 0: A fails
t ≈ 0: "A: ∞"
Without a triggered update, R2 would only learn of the failure in the next periodic advertisement (up to 30 s later).
Notes: Instead of waiting for the next periodic advertisement (30 s in RIP), the router sends an update immediately whenever its table changes, containing only the routes that changed. This speeds up the propagation of bad news and shrinks the window during which stale information can cause loops. Combined, the four techniques (split horizon, poison reverse, hold-down and triggered updates) make RIP usable in small networks. In EIGRP every update is triggered and there are no periodic table advertisements: the adjacency is kept by Hello packets and information is exchanged reliably (RTP).

## Slide 32: Distance vector, example (1 of 4): initial state
1
A
2
B
3
C
4
D
5
Table of A
Net | Metric | Via
1 | 1 | DC
2 | 1 | DC
Table of B
Net | Metric | Via
2 | 1 | DC
3 | 1 | DC
Table of C
Net | Metric | Via
3 | 1 | DC
4 | 1 | DC
Table of D
Net | Metric | Via
4 | 1 | DC
5 | 1 | DC
Before the exchange of information, each router knows only its directly connected networks (DC).
Notes: Four routers in a row (A, B, C, D) interconnect five networks (1 to 5). Before any exchange of information, each router knows only the directly connected networks (DC, metric 1 by the convention of this example). The next four slides show the tables after each update cycle, with simple split horizon active. Ask the students to predict the contents of the tables before advancing each slide.

## Slide 33: Distance vector, example (2 of 4): first exchange
1
A
2
B
3
C
4
D
5
Table of A
Net | Metric | Via
1 | 1 | DC
2 | 1 | DC
3 | 2 | B
Table of B
Net | Metric | Via
2 | 1 | DC
3 | 1 | DC
1 | 2 | A
4 | 2 | C
Table of C
Net | Metric | Via
3 | 1 | DC
4 | 1 | DC
2 | 2 | B
5 | 2 | D
Table of D
Net | Metric | Via
4 | 1 | DC
5 | 1 | DC
3 | 2 | C
The first exchange of advertisements, with simple split horizon, adds to the tables the networks one neighbor away (highlighted).
Notes: First exchange of advertisements, with simple split horizon. A receives network 3 from B (metric 2 via B); network 2, which both have as directly connected, stays at metric 1 in each. B receives network 1 from A and network 4 from C; C receives network 2 from B and network 5 from D; D receives network 3 from C. Each router now knows the networks one neighbor away. The new entries of each cycle are highlighted (in the 1999 original they were marked in blue).

## Slide 34: Distance vector, example (3 of 4): second exchange
1
A
2
B
3
C
4
D
5
Table of A
Net | Metric | Via
1 | 1 | DC
2 | 1 | DC
3 | 2 | B
4 | 3 | B
Table of B
Net | Metric | Via
2 | 1 | DC
3 | 1 | DC
1 | 2 | A
4 | 2 | C
5 | 3 | C
Table of C
Net | Metric | Via
3 | 1 | DC
4 | 1 | DC
2 | 2 | B
5 | 2 | D
1 | 3 | B
Table of D
Net | Metric | Via
4 | 1 | DC
5 | 1 | DC
3 | 2 | C
2 | 3 | C
The second periodic update adds the networks two neighbors away. A and D still do not know the whole topology.
Notes: In the second periodic update, B advertises networks 3 and 4 to A (A already had 3; it adds 4 at metric 3 via B); C advertises network 5 to B (metric 3 via C); B advertises network 1 to C (metric 3 via B); C advertises network 2 to D (metric 3 via C). Note that A and D, at the ends, still do not know the whole topology: A is missing network 5 and D is missing network 1.

## Slide 35: Distance vector, example (4 of 4): convergence
1
A
2
B
3
C
4
D
5
Table of A
Net | Metric | Via
1 | 1 | DC
2 | 1 | DC
3 | 2 | B
4 | 3 | B
5 | 4 | B
Table of B
Net | Metric | Via
2 | 1 | DC
3 | 1 | DC
1 | 2 | A
4 | 2 | C
5 | 3 | C
Table of C
Net | Metric | Via
3 | 1 | DC
4 | 1 | DC
2 | 2 | B
5 | 2 | D
1 | 3 | B
Table of D
Net | Metric | Via
4 | 1 | DC
5 | 1 | DC
3 | 2 | C
2 | 3 | C
1 | 4 | C
It took three iterations (three update periods) for this network to converge. Diameter of N hops ≈ N-1 cycles.
Notes: In the third exchange, A learns network 5 (metric 4 via B) and D learns network 1 (metric 4 via C). Now every table contains all five networks: the network converged in three iterations. In general, a network with a diameter of N hops needs N-1 update cycles to converge, which, with RIP's 30 s period, can mean minutes. That slowness is the motivation for triggered updates and for link-state protocols.

## Slide 36: Link-state routing: principles (1 of 2)
1
Meet the neighbors
Each router discovers the adjacent routers and learns their identifiers (Hello protocol).
2
Describe the links
Builds a link-state advertisement (LSA) with the list of neighbors and the cost of each link.
3
Flood
Transmits the LSA to all other routers (flooding); each one stores the most recent LSA from each originator in the link-state database (LSDB).
4
Compute
With the complete topology map, each router runs SPF (Dijkstra) and computes the route to each destination with itself as the root.
R1
R2
R3
R4
10
10
100
10
50
LSA of R1: {R2: 10, R3: 10, R4: 50}
LSA of R4: {R1: 50, R2: 100, R3: 10}
Every router has the same LSDB and computes its own SPF tree
Notes: Four responsibilities of each router: (1) discover its neighbors and learn their names (identifiers), usually by Hello packets; (2) build a link-state packet (LSA, Link State Advertisement, or LSP in IS-IS) with the list of neighbors and the cost of each link; (3) flood the LSA to every router in the area, each one keeping the most recent LSA from each originator, forming an identical database everywhere; (4) with the complete map, compute the routes to each destination with the SPF algorithm (Dijkstra), with itself as the root.

## Slide 37: Link-state routing: principles (2 of 2)
What the link-state router does NOT do
Does not send updates with a list of destinations and distances (the whole routing table)
Does not depend on 'rumors': computes everything from primary data
What it does
Actively tests the state of every neighbor (Hello)
Propagates the message describing the state of its links (LSA): periodically (OSPF: 30 min) and immediately on every change
1
On receiving an LSA
Updates the internetwork map, marking the links as up or down (and stores the most recent version, by sequence number).
2
When a link's state changes
Recompiles the routes by running Dijkstra's algorithm (SPF) on the database; the resulting routing table is installed in the RIB/FIB.
Notes: The essential difference from distance vector: a link-state router never sends 'lists of destinations with distances'. It does only two things: actively tests the state of its neighbors (Hello) and propagates periodically (and immediately on every change) the description of its own links. On receiving an LSA, it updates the map by marking links up or down; on every change it recomputes the routes with Dijkstra. In OSPF the LSA is also re-sent every 30 minutes (LSRefreshTime) and expires after 60 minutes (MaxAge), which keeps the database consistent even without changes.

## Slide 38: Link state: advantages over distance vector
Independent computation
Each router computes the routes by itself, from the same original state data (identical LSDB). No accumulation of errors from neighbor to neighbor.
Fast convergence
A router recognizes a new LSA and forwards it before recomputing routes; the news spreads at flooding speed, not at the pace of update periods.
Better scaling
Each LSA carries only one router's direct connections. Areas (OSPF) and levels (IS-IS) limit the scope of flooding and of SPF.
Criterion | Distance vector (RIP) | Link state (OSPF, IS-IS)
What is advertised | Routing table (destination + metric) to neighbors | State of its own links (LSA) to everyone in the area
View of the network | Only the neighbors' 'rumor' | Complete map of the area
Convergence | Slow (30 s cycles, hold-down) | Fast (flooding + SPF; subsecond with BFD)
Notes: Three advantages: (1) each router computes the routes independently from the same raw topology data, instead of trusting the neighbor's arithmetic; (2) it converges faster, because a router can recognize a new LSA and forward it even before recomputing its routes, so the news spreads at flooding speed; (3) it scales better, because each LSA carries only the direct connections of one router (small, stable information), and areas limit the scope of flooding. Costs: more memory (LSDB) and CPU (SPF), and more careful configuration (areas). On 2026 hardware those costs are irrelevant for networks of thousands of routers.

## Slide 39: Link-state protocols in use
UPDATED
Protocol | Origin and standard | Status in 2026
OSPF | IETF; OSPFv2 RFC 2328 (1998, successor of RFC 1247 from 1991); OSPFv3 RFC 5340 (2008) for IPv6 | Most used IGP in enterprise and campus networks; detailed in Module 2
IS-IS | ISO 10589 (designed at Digital for DECnet Phase V); integrated IS-IS for IP: RFC 1195; IPv6: RFC 5308 | De facto standard in large providers and data centers; base of Segment Routing (SR-MPLS, SRv6)
NLSP | Novell Link State Protocol, for IPX routing | Extinct with NetWare/IPX (legacy)
OSPF and IS-IS implement the same algorithm (Dijkstra) with different encapsulations: OSPF runs over IP (protocol 89); IS-IS runs directly over the data link layer (it does not need IP to form adjacencies), which makes it attractive in provider cores and fabrics.
Also link state, outside IP routing
TRILL and SPB (IEEE 802.1aq) used IS-IS for Layer 2 forwarding; today the dominant approach in data centers is BGP + EVPN/VXLAN
SDN controllers and Wi-Fi fabric protocols reuse the idea of a synchronized topology database
Notes: In 1999 there were three interior link-state protocols: OSPF (IETF, for IP; then RFC 1247, today RFC 2328 for OSPFv2 and RFC 5340 for OSPFv3), IS-IS (ISO 10589, designed at Digital for DECnet Phase V and extended to IP by RFC 1195) and NLSP (Novell, for IPX). NLSP died with IPX. OSPF and IS-IS remain the market's two link-state IGPs: OSPF dominates in enterprise networks; IS-IS is widely used by service providers and in large data centers, thanks to its independence from IP and its extensibility (TLVs), which also made it the base of Segment Routing.

## Slide 40: Autonomous system (AS)
AS 64512 (IGP: OSPF)
R1
R2
R3
R4
AS 64513 (IGP: IS-IS)
R5
R6
R7
R8
eBGP between the ASs
Routers under a common administration, with a single routing policy toward the outside (RFC 1930)
Inside the AS: interior protocol (IGP): OSPF, IS-IS, EIGRP, RIP; between ASs: exterior protocol (EGP): BGP-4
AS number (ASN): 16 bits until 2007; 32 bits since RFC 4893 / RFC 6793; private: 64512 to 65534 and 4,200,000,000 to 4,294,967,294 (RFC 6996)
Assigned by the RIRs (ARIN, LACNIC...) and, in Brazil, by Registro.br / NIC.br
Notes: Classic definition (RFC 1930): a set of routers and networks under a common administration, with a single, coherent routing policy toward the outside. Inside the AS runs an IGP (OSPF, IS-IS, EIGRP, RIP); between ASs runs the Internet's de facto EGP, BGP-4. Each public AS receives a number (ASN) assigned by the regional registries (in Brazil, NIC.br/Registro.br together with LACNIC; in the US, ARIN). 2026 update: ASNs were 16 bits (up to 65,535); since RFC 4893 (2007), consolidated in RFC 6793 (2012), they are 32 bits. Private ranges: 64512 to 65534 and 4,200,000,000 to 4,294,967,294 (RFC 6996). Examples: AS 2 (UDEL), AS 15169 (Google), AS 28573 (Claro Brazil).

## Slide 41: Module 1 summary
Internetworking
L2 switch decides by MAC; router decides by IP; L3 switch does both in ASIC
Routers bound broadcast domains and allow multiple paths
Today only IPv4 and IPv6 are 'routable'; ARP, STP and LLDP stay on the link
Addressing and encapsulation
MAC: flat, link scope; IP: hierarchical (prefix + host), global scope
Each layer adds its header; EtherType identifies IPv4/IPv6/ARP
Minimum IPv4 header of 20 bytes; Ethernet MTU of 1,500 bytes
Distance vector
Advertises the table to neighbors; Bellman-Ford; converges in N-1 cycles
Count to infinity mitigated by split horizon, poison reverse, hold-down and triggered updates
RIP (legacy/small networks), EIGRP (advanced)
Link state and AS
Floods LSAs; identical LSDB; Dijkstra; converges fast and scales with areas
OSPF and IS-IS in use; NLSP extinct
AS = common administration; IGP inside, BGP-4 between ASs; 32-bit ASN
Notes: Recap the key points before starting Module 2. Suggested check questions: (1) why is a Layer 2 loop worse than a Layer 3 loop? (TTL); (2) what information does a distance-vector router send to its neighbors, and a link-state one? (3) name the four techniques that mitigate count to infinity; (4) what is an autonomous system and which protocol runs between them?

## Slide 42: TCP/IP
MODULE 2
Protocol stack, IPv4 addressing and subnetting, host behavior (route determination and ARP), routing across an internetwork, routing protocols (RIP, EIGRP, OSPF, BGP), access control, IPv6, multicast, MPLS and VRRP
Notes: Module 2 divider. It is the longest module: about 120 slides. Suggested pacing: addressing and subnetting in the first half of day 1; ARP and the complete transfer example at the end of day 1; routing protocols on the morning of day 2; IPv6, multicast, MPLS and VRRP in the afternoon.

## Slide 43: Module 2 objectives (1 of 2)
1
Characteristics of TCP/IP
Protocol stack, IPv4 datagram, protocol and port numbers, addressing, subnetting and VLSM, host-to-host communication, ARP and Proxy ARP.
2
The IP routing process
Describe in detail, step by step, what happens to a packet between the source station and the destination station in a routed internetwork.
3
RIP and EIGRP
Recall the fundamentals of RIP (v1, v2, RIPng) and of EIGRP (composite metric, DUAL, multipath) and the role of administrative distance.
4
Redistribution and OSPF
Discuss route redistribution between routing processes and recall the principles of OSPF (areas, router types, Hello, DR, LSAs).
Notes: Original objectives kept, with updated terminology: 'IPng' became IPv6; 'IGRP' became EIGRP; and we added IS-IS, BGP-4 and the modern IPv6 mechanisms (Neighbor Discovery, SLAAC).

## Slide 44: Module 2 objectives (2 of 2)
1
BGP-4
Distinguish interior from exterior protocols and describe the fundamentals of BGP-4 (path vector, eBGP/iBGP, attributes).
2
Access control
Recall how access control lists (ACLs) on routers filter IP traffic, and how they evolved into stateful firewalls.
3
Operational topics
Broadcast handling (DHCP relay), secondary addresses, unnumbered interfaces, static and default routes.
4
IPv6 and complementary technologies
Understand IPv6 (header, addressing, ND/SLAAC, routing, transition), IP multicast (IGMP/MLD, PIM), RSVP, MPLS and VRRP.
Notes: Second half of the objectives. Note that the last group, which in 1999 was called 'new IP technologies', includes topics that are production standards today (IPv6, MPLS, VRRP) and one that stayed a niche (RSVP).

## Slide 45: TCP/IP: origin and governance
The most widely used protocol suite in the world: the foundation of the Internet and of enterprise networks
Developed in a project funded by ARPA/DARPA (US); Cerf and Kahn, 1974; IP and TCP specified in 1981 (RFC 791, RFC 793); ARPANET switches over on January 1, 1983
The RFCs (Requests for Comments) define the processing of the protocols and are public; standardized by the IETF; numbers administered by IANA
Includes not only Layers 3 and 4 but also applications (DNS, HTTP, SMTP, SSH, SNMP) and auxiliary protocols (ICMP, ARP, DHCP)
TCP consolidated in 2022 in RFC 9293; IPv4 is still RFC 791; IPv6 is RFC 8200 (2017)
Timeline
1969: first ARPANET nodes
1974: Cerf and Kahn, 'A Protocol for Packet Network Intercommunication'
1981: RFC 791 (IP) and RFC 793 (TCP)
1983: ARPANET 'flag day'; DNS (RFC 882/883)
1985: subnetting (RFC 950); 1986: IETF
1993: CIDR (RFC 1519); 1998: IPv6 (RFC 2460)
2011: IANA runs out of free IPv4
2017: IPv6 Internet Standard (RFC 8200)
2026: > 50% of Google access over IPv6
Notes: TCP/IP came out of a project funded by ARPA/DARPA of the US Department of Defense; the seminal paper by Cerf and Kahn is from 1974, the IP (RFC 791) and TCP (RFC 793) specifications are from September 1981, and the ARPANET switched to TCP/IP on January 1, 1983. The specifications are published as RFCs (Requests for Comments), public documents maintained by the RFC Editor; standardization is done by the IETF (since 1986) and the numbers (ports, protocols, addresses) are administered by IANA. 2026 update: the TCP specification was consolidated in 2022 in RFC 9293, which replaces RFC 793 and dozens of updates. The TCP/IP suite does not define only Layers 3 and 4: it includes applications (DNS, HTTP, SMTP, SSH...) and auxiliary protocols (ICMP, ARP, DHCP).

## Slide 46: The TCP/IP protocol stack and the OSI model
7 Application
6 Presentation
5 Session
4 Transport
3 Network
2 Data link
1 Physical
OSI model
TCP/IP stack (RFC 1122)
Application
Transport
Internet
Network interface
(link + physical)
Examples at each layer
Application: HTTP/HTTPS, DNS, SMTP, IMAP, SSH, SNMP, NTP, DHCP, TLS (security between application and transport)
Transport: TCP, UDP, QUIC (over UDP), SCTP
Internet: IPv4, IPv6, ICMP/ICMPv6, IGMP/MLD, IPsec; routing protocols (OSPF, BGP) run over IP or TCP
Network interface: Ethernet, Wi-Fi, PPP/PPPoE, MPLS (Layer '2.5'), VXLAN (encapsulation over UDP)
Legacy: Token Ring, FDDI, Frame Relay, ATM
The Internet layer (IP) is the 'narrow waist of the hourglass': everything above runs over IP, and IP runs over any link.
Notes: The TCP/IP stack has four layers (RFC 1122): application, transport, Internet and network interface (link). Many courses show five, separating physical from data link. The seven-layer OSI model is useful as vocabulary: OSI Layers 5 to 7 correspond to the TCP/IP application layer; OSI Layer 3 is the Internet layer; Layers 2 and 1 form the network interface. The media access protocols listed in the original (Ethernet, Token Ring, FDDI) were updated: today, Ethernet, Wi-Fi and WAN links of every kind.

## Slide 47: Application layer
Application
Transport
Internet
Network interface
Function | Current protocols (port) | Legacy / replaced
Web and APIs | HTTPS: HTTP/1.1 and HTTP/2 over TLS/TCP 443; HTTP/3 over QUIC/UDP 443 | Cleartext HTTP (80)
Names | DNS (UDP/TCP 53); DNS over TLS (853) and over HTTPS; DNSSEC | hosts file, static tables
Remote access | SSH (TCP 22); RDP (3389) | Telnet (23), rlogin (513)
Files | SFTP/SCP (22), HTTPS, SMB (445), NFSv4 (2049) | FTP (20/21), TFTP (69) still in network boot
E-mail | SMTP submission (587, TLS), IMAPS (993), server-to-server SMTP (25) | POP3 (110), SMTP without TLS
Management and time | SNMPv3 (UDP 161/162), NETCONF/RESTCONF, gNMI, syslog (514), NTP (123) | SNMPv1/v2c (cleartext communities)
Host configuration | DHCP (UDP 67/68), DHCPv6 (546/547), SLAAC (IPv6) | BOOTP, RARP
Notes: The original slide listed WWW, file transfer (TFTP, FTP, NFS), e-mail (SMTP), remote login (Telnet, rlogin) and management (SNMP). In 2026: the Web uses HTTPS (HTTP/1.1, HTTP/2 and HTTP/3 over QUIC) almost exclusively; cleartext Telnet, rlogin and FTP were replaced by SSH, SFTP and HTTPS; DNS gained DNSSEC and encrypted transports (DoT, DoH); e-mail uses submission on port 587 with STARTTLS/TLS and IMAPS. Highlight: TLS is not a formal OSI layer, but it sits between application and transport; most application protocols run over TLS today.

## Slide 48: Transport layer
Application
Transport
Internet
Network interface
TCP: Transmission Control Protocol
Connection oriented (three-way handshake), reliable and ordered byte stream
Flow control (window) and congestion control
Header of 20 bytes or more; RFC 9293 (2022)
UDP: User Datagram Protocol
Connectionless, no delivery or ordering guarantee
8-byte header; minimal latency
DNS, DHCP, SNMP, NTP, voice and video, QUIC; RFC 768
QUIC: the transport of HTTP/3
Runs over UDP (port 443) with integrated TLS 1.3
Multiple streams without head-of-line blocking; connection migration
RFC 9000 (2021); a significant share of web traffic (HTTP/3)
SCTP and others
SCTP (RFC 9260): messages, multihoming; telephony signaling (SIGTRAN), 4G/5G networks
DCCP (RFC 4340): rarely used
16-bit ports identify the application in TCP, UDP, SCTP and QUIC
Notes: TCP (RFC 9293) offers a reliable, ordered byte stream with flow and congestion control, connection oriented (three-way handshake). UDP (RFC 768) offers connectionless datagrams with no guarantees and a minimal 8-byte overhead: ideal for DNS, voice, video, games and for protocols that implement their own control. The relevant newcomer since 1999 is QUIC (RFC 9000, 2021), a transport over UDP with integrated TLS 1.3 encryption, stream multiplexing without head-of-line blocking and connection establishment in 0 or 1 RTT; it is the base of HTTP/3. SCTP (RFC 9260) is used in telephony signaling and mobile networks.

## Slide 49: Internet layer
Application
Transport
Internet
Network interface
Protocol | Function | Reference
IPv4 | 32-bit addressing, forwarding, fragmentation; connectionless, best effort | RFC 791 (1981)
IPv6 | 128-bit addressing, simplified header, extension headers, no fragmentation in routers | RFC 8200 (2017)
ICMP / ICMPv6 | Errors (destination unreachable, TTL expired), diagnostics (echo), MTU (Packet Too Big); ICMPv6 includes ND and MLD | RFC 792 / RFC 4443
ARP | IPv4 → MAC resolution on broadcast links (encapsulated directly in Ethernet, 0x0806) | RFC 826 (1982)
ND (IPv6) | Neighbor and router discovery, address resolution, SLAAC; replaces ARP and part of ICMP | RFC 4861, RFC 4862
IGMP / MLD | Hosts tell routers which multicast groups they want to receive | RFC 3376 / RFC 3810
IPsec (AH, ESP) | Authentication, integrity and confidentiality at the network layer; VPNs | RFC 4301 to 4303
RARP | MAC → IP resolution for diskless stations; replaced by BOOTP and DHCP (legacy) | RFC 903
Notes: The original listed IP, ARP, RARP and ICMP. Update: IPv4 (RFC 791) and IPv6 (RFC 8200) coexist in dual stack; ICMP (RFC 792) and ICMPv6 (RFC 4443) handle diagnostics and error signaling, and ICMPv6 also carries Neighbor Discovery (ND, RFC 4861), which replaces ARP in IPv6; IGMP (RFC 3376) and MLD (RFC 3810) manage multicast groups; IPsec (AH, ESP) protects packets. RARP (RFC 903) was replaced by BOOTP and then DHCP. ARP, although listed in the Internet layer for convenience, operates between Layers 2 and 3: it is encapsulated directly in Ethernet frames (EtherType 0x0806), not in IP.

## Slide 50: The IPv4 datagram in detail
bit 0
bit 31
Version
4
IHL
4
DSCP
6
ECN
2
Total length
16
Identification
16
Flags
3
Fragment offset
13
TTL
8
Protocol
8
Header checksum
16
Source address (32)
Destination address (32)
Options (0 to 40 bytes) + padding
Field | Note
IHL | 32-bit words; 5 = 20 bytes (no options)
DSCP / ECN | Former ToS; QoS (RFC 2474) and congestion (RFC 3168)
Flags | bit 1 DF (don't fragment), bit 2 MF (more fragments)
TTL | Remaining hops; 0 → drop + ICMP; traceroute
Protocol | 6 TCP, 17 UDP, 1 ICMP, 89 OSPF...
Checksum | Header only; recomputed at every hop (TTL changes)
Options | Rare; many networks drop packets with options
Fragmentation: a packet larger than the MTU of the egress link is split by the router (IPv4) using Identification, MF and Offset; with DF set, it is dropped with ICMP 'Fragmentation Needed', the basis of Path MTU Discovery (RFC 1191). In IPv6 only the source fragments.
Notes: Walk through the fields: Version (4); IHL, header length in 32-bit words (5 = 20 bytes, up to 15 = 60 bytes with options); DSCP and ECN, the former 'Type of Service' (RFC 2474 and RFC 3168), used for QoS and congestion notification; Total Length in bytes (maximum 65,535); Identification, Flags (DF: don't fragment; MF: more fragments) and Offset, used in fragmentation; TTL, decremented by every router and which, on reaching zero, causes a drop and an ICMP Time Exceeded (the basis of traceroute); Protocol, which identifies the payload (next slide); Checksum, of the header only; source and destination addresses; options (rare and frequently blocked). Practical note: fragmentation is avoided with Path MTU Discovery (RFC 1191) by setting DF; in IPv6 routers never fragment.

## Slide 51: Protocol numbers: identifying the IP payload
No. | Protocol | Use
1 | ICMP | Errors and diagnostics
2 | IGMP | Multicast group membership
6 | TCP | Reliable transport
17 | UDP | Connectionless transport
41 | IPv6 | IPv6 encapsulated in IPv4 (6in4)
47 | GRE | Generic tunnels
50 / 51 | ESP / AH | IPsec
58 | ICMPv6 | ICMP for IPv6 (includes ND, MLD)
88 | EIGRP | Routing (Cisco, RFC 7868)
89 | OSPF | Link-state routing
103 | PIM | Multicast routing
112 | VRRP | Gateway redundancy
132 | SCTP | Multistream transport
Demultiplexing at the Internet layer
IP
Protocol = ?
ICMP
(1)
TCP
(6)
UDP
(17)
OSPF
(89)
Received packet
Official registry: IANA, 'Assigned Internet Protocol Numbers' (replaces RFC 1700 from 1994).
Notes: The Protocol field (IPv4) or Next Header (IPv6) tells the Internet layer whom to hand the data to: 6 for TCP, 17 for UDP, 1 for ICMP and so on. It is the first stage of demultiplexing; the second is the port, inside the TCP/UDP segment. The values are administered by IANA in the 'Protocol Numbers' registry (RFC 1700 from 1994, cited in the original, was replaced by the online registries, RFC 3232). Draw attention to 41 (IPv6 encapsulated in IPv4, used in 6in4 tunnels), 47 (GRE), 50 and 51 (IPsec), 58 (ICMPv6), 88 (EIGRP), 89 (OSPF), 103 (PIM), 112 (VRRP) and 132 (SCTP), all seen throughout the course.

## Slide 52: Port numbers: identifying the application
Ranges (RFC 6335)
0 to 1023: system ('well-known') ports
1024 to 49151: user (registered) ports
49152 to 65535: dynamic / ephemeral (client side)
Socket = 5-tuple
protocol + source IP + source port + destination IP + destination port. It is what NAT, stateful firewalls and load balancers track.
Port | Transport | Service | Port | Transport | Service
22 | TCP | SSH, SFTP, SCP | 161 / 162 | UDP | SNMP / traps
25 | TCP | SMTP (server to server) | 179 | TCP | BGP
53 | UDP, TCP | DNS | 443 | TCP, UDP | HTTPS; HTTP/3 (QUIC)
67 / 68 | UDP | DHCP server / client | 445 | TCP | SMB
69 | UDP | TFTP (network boot) | 500 / 4500 | UDP | IKE / IPsec NAT-T
80 | TCP | HTTP (cleartext) | 514 | UDP | syslog
123 | UDP | NTP | 520 / 521 | UDP | RIP / RIPng
143 / 993 | TCP | IMAP / IMAPS | 587 | TCP | SMTP submission (TLS)
23 | TCP | Telnet (legacy) | 20 / 21 | TCP | FTP (legacy)
Official registry: IANA Service Name and Transport Protocol Port Number Registry (successor of RFC 1060 / RFC 1700).
Notes: TCP and UDP (and also SCTP and QUIC) use 16-bit ports to tell applications apart on the same host. RFC 6335 defines three ranges: system ports (0 to 1023, the 'well-known' ones), registered user ports (1024 to 49151) and dynamic or ephemeral ports (49152 to 65535), used on the client side. The official registry is IANA's 'Service Name and Transport Protocol Port Number Registry', which replaced RFC 1060 cited in the original (later RFC 1700). A socket is identified by the 5-tuple: protocol, source IP, source port, destination IP, destination port; that is what NAT, firewalls and load balancers track.

## Slide 53: Receiving a frame: demultiplexing at three levels
Ethernet frame (FCS ok, destination MAC = mine or broadcast/multicast)
Data link: EtherType
ARP
0x0806
IPv6
0x86DD
802.1Q
0x8100
MPLS
0x8847
0x0800 = IPv4
Internet: Protocol field
ICMP (1)
OSPF (89)
UDP (17)
ESP (50)
6 = TCP
Transport: destination port
SSH
TCP 22
HTTPS
TCP 443
DNS
UDP 53
NTP
UDP 123
Application (process / socket)
Notes: Follow the frame from the bottom up: (1) the interface checks the FCS and the destination MAC (its own, broadcast or a subscribed multicast) and uses the EtherType to hand the payload to the right protocol (0x0800 IPv4, 0x86DD IPv6, 0x0806 ARP, 0x8100 802.1Q, 0x8847 MPLS); (2) the IP layer validates the header and uses the Protocol field to deliver to TCP, UDP, ICMP, etc.; (3) the transport uses the destination port to deliver to the right application (DNS on 53, SSH on 22). In 1999 the Type/SNAP ID field played the EtherType role; the original diagram showed Telnet 23, FTP 21, DNS 53 and TFTP 69.

## Slide 54: Decimal-to-binary conversion
Position | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Weight | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
172 = | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0
255 = | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Subtraction method
172 - 128 = 44 → bit 128 on
44 - 64 < 0 → bit 64 off
44 - 32 = 12 → bit 32 on
12 - 16 < 0 → bit 16 off
12 - 8 = 4 → bit 8 on
4 - 4 = 0 → bit 4 on; bits 2 and 1 off
Result: 172 = 10101100
Mask (octet) | Binary | 1 bits
0 | 00000000 | 0
128 | 10000000 | 1
192 | 11000000 | 2
224 | 11100000 | 3
240 | 11110000 | 4
248 | 11111000 | 5
252 | 11111100 | 6
254 | 11111110 | 7
255 | 11111111 | 8
Sum of all weights = 255. If a position is 0, nothing is added. The nine values in the table are the only ones that appear in contiguous masks.
Notes: Basic tool for subnetting: each octet has 8 bits with weights 128, 64, 32, 16, 8, 4, 2 and 1. To convert 172 to binary, subtract the largest weights that fit: 172 - 128 = 44; 44 - 32 = 12; 12 - 8 = 4; 4 - 4 = 0, so bits 128, 32, 8 and 4 are on: 10101100. The sum of all weights is 255, the largest value of an octet. Ask the students to convert 192, 224, 240, 248, 252, 254 and 255 (the values that appear in masks) and to memorize that each one adds a 1 bit on the left.

## Slide 55: The IPv4 address
Every IPv4 interface is identified by a 32-bit address
Defined in 1981 (RFC 791) with two parts: network identifier and host number
Network part assigned by the numbering hierarchy: IANA → RIRs (ARIN in the US; LACNIC with NIC.br in Brazil) → providers → organizations
Host part assigned by the network administrator (or by DHCP)
Written as four decimal numbers separated by dots; each number is one octet (0 to 255)
Network
Host
32 bits
10101100
00010000
00010100
00001010
172
16
20
10
172 . 16 . 20 . 10
Where is the network/host boundary?
1981 to 1993: set by the class (first bits)
Since 1993: set by the mask or the prefix length (CIDR), e.g., 172.16.20.10/24
Notes: Every IPv4 interface has a 32-bit address, written as four decimal numbers separated by dots (dotted-decimal notation), each representing one octet. When IP was standardized in 1981 the address had two parts, network and host; the network part was assigned by the numbering authorities (today IANA → RIRs → providers → organizations) and the host part by the network administrator. The original example, 134.141.20.10, was a real Cabletron address; we use 172.16.20.10, from the RFC 1918 private range.

## Slide 56: Classful addressing (1981 to 1993)
LEGACY
Class | Leading bits | 1st octet | Format (N = network, H = host) | Natural mask | Networks × hosts
A | 0xxxxxxx | 1 to 126 | N.H.H.H (8 + 24 bits) | 255.0.0.0 (/8) | 126 × 16,777,214
B | 10xxxxxx | 128 to 191 | N.N.H.H (16 + 16 bits) | 255.255.0.0 (/16) | 16,384 × 65,534
C | 110xxxxx | 192 to 223 | N.N.N.H (24 + 8 bits) | 255.255.255.0 (/24) | 2,097,152 × 254
D | 1110xxxx | 224 to 239 | Multicast (RFC 1112): 28 group bits | n/a | Multicast groups
E | 1111xxxx | 240 to 255 | Reserved / experimental | n/a | Not routed on the Internet
First-octet rule: the value of the first octet reveals the class and therefore the 'natural' mask. 0.0.0.0/8 and 127.0.0.0/8 (loopback) are reserved.
Why it ended
Waste: a class B (65,534 hosts) for a company with 300 machines
Explosion of the Internet routing table with thousands of class Cs
What replaced it
CIDR (RFC 1519, 1993; current RFC 4632) and VLSM: the mask sets the boundary
Private addresses (RFC 1918) + NAT; then IPv6
Notes: Originally there were three classes of networks, A, B and C, recognized by the first bits of the first octet (the first-octet rule): class A, leading bit 0, 7 network bits and 24 host bits (1 to 126; 0 and 127 reserved); class B, bits 10, 14 network bits and 16 host bits (128 to 191); class C, bits 110, 21 network bits and 8 host bits (192 to 223). Class D (1110, 224 to 239) was defined later for multicast (RFC 1112) and class E (1111, 240 to 255) stayed reserved. The scheme was abandoned in 1993 in favor of CIDR (RFC 1519, today RFC 4632) because it wasted addresses (a class B for a company with 300 hosts) and made the Internet routing table explode with class C networks. The terms 'class A/B/C' survive only as jargon and in certification exams; modern equipment is classless by default.

## Slide 57: CIDR: classless routing and prefix notation
UPDATED
Prefix notation
172.16.20.10/24 = mask 255.255.255.0 (24 one bits)
/n: the n leftmost bits identify the network; the remaining 32 - n, the host
Usable hosts = 2^(32-n) - 2 (except /31 and /32)
Aggregation (supernetting)
192.0.2.0/24 + 192.0.3.0/24 → advertised as 192.0.2.0/23
A provider holding 198.51.100.0/22 advertises a single prefix for 1,022 customer hosts
Global IPv4 table ≈ 1 million prefixes (2026); unmanageable without CIDR
Prefix | Mask | Host bits | Addresses | Usable hosts | Typical use
/8 | 255.0.0.0 | 24 | 16,777,216 | 16,777,214 | Former class A; 10.0.0.0/8 private
/16 | 255.255.0.0 | 16 | 65,536 | 65,534 | Former class B; large campus
/24 | 255.255.255.0 | 8 | 256 | 254 | User subnet / VLAN
/26 | 255.255.255.192 | 6 | 64 | 62 | Small subnet
/30 | 255.255.255.252 | 2 | 4 | 2 | Point-to-point link
/31 | 255.255.255.254 | 1 | 2 | 2 (RFC 3021) | Point-to-point link with no waste
/32 | 255.255.255.255 | 0 | 1 | 1 | Router loopback; host route
Notes: With CIDR (Classless Inter-Domain Routing), the boundary between network and host is given explicitly by the prefix length (/n = n network bits), equivalent to a mask of n contiguous 1 bits. This allows allocating blocks of the right size (172.16.20.0/23 for 510 hosts, instead of a class B) and aggregating (summarizing) several prefixes into a single routing advertisement, shrinking the Internet tables (supernetting). In 2026 the global IPv4 table has about one million prefixes; without CIDR it would be unmanageable. VLSM (Variable Length Subnet Mask) is the same principle applied inside an organization: subnets of different sizes according to need. Classful protocols (RIPv1, IGRP) do not carry a mask and do not support VLSM; every modern protocol (RIPv2, EIGRP, OSPF, IS-IS, BGP-4) is classless.

## Slide 58: Special-purpose IPv4 addresses
Block | Meaning | Reference
0.0.0.0/8 (0.0.0.0) | 'This host on this network'; source only (e.g., DHCP client without an address) | RFC 1122
127.0.0.0/8 | Loopback: packets never leave the host (127.0.0.1; IPv6 ::1) | RFC 1122
10/8, 172.16/12, 192.168/16 | Private addresses: not routed on the Internet; used with NAT | RFC 1918
100.64.0.0/10 | Shared address space for provider CGNAT (between the customer and the carrier's NAT) | RFC 6598
169.254.0.0/16 | Link-local (autoconfiguration without DHCP, 'APIPA'); not routed | RFC 3927
192.0.2/24, 198.51.100/24, 203.0.113/24 | Documentation and examples (used in this course) | RFC 5737
224.0.0.0/4 | Multicast (former class D); 224.0.0.0/24 is link local | RFC 5771
240.0.0.0/4 | Reserved (former class E); not usable on the public Internet | RFC 1112
255.255.255.255 | Limited broadcast: destination only; does not cross routers | RFC 919
x.y.z.255 (/24) | Directed broadcast: all host bits set to 1; routers do not forward it by default | RFC 2644
Consolidated registry: RFC 6890 and the IANA IPv4 Special-Purpose Address Registry. Exhaustion: IANA in 2011, LACNIC in 2020 (final phase); hence NAT, CGNAT and IPv6.
Notes: The original listed four cases: 0.0.0.0 ('this host on this network', source only, e.g., a DHCP client), 255.255.255.255 (limited broadcast, destination only, does not cross routers), directed broadcast (all host bits set to 1, e.g., 172.16.20.255/24) and 127.x.y.z (loopback, never leaves the host). The list grew: private addresses (RFC 1918) used with NAT; shared address space 100.64.0.0/10 for provider CGNAT (RFC 6598); link-local 169.254.0.0/16 (APIPA, RFC 3927); documentation blocks (RFC 5737), which we use in this course; multicast 224.0.0.0/4; and the former class E 240.0.0.0/4, still not usable on the Internet. The consolidated registry is RFC 6890 and IANA's 'Special-Purpose Address Registry'.

## Slide 59: Subnets: a third level of hierarchy
Before subnetting (1981)
Network number
Host
With subnetting (RFC 950, 1985): bits borrowed from the host part
Network number
Subnet
Host
Example: 172.16.0.0/16 split with 8 subnet bits → 256 /24 subnets (172.16.0.0/24 to 172.16.255.0/24), 254 hosts each
A subnet is a division of the space reserved for hosts, made by the organization itself; one subnet per link (VLAN, segment, WAN link)
To the outside, the network is still a single prefix (aggregation); only the internal routers know the subnets
The subnet field can have any size; it is specified by a 32-bit mask (or by the prefix length)
With CIDR/VLSM the 'network versus subnet' distinction lost its technical meaning: everything is a prefix; the term subnet remains in everyday use
Notes: In 1984/1985 (RFC 917 and RFC 950, Internet Standard Subnetting Procedure) a third level was added to the address structure: the subnet. The organization receives a prefix (back then, a class network) and borrows bits from the host part to number its internal subnets, one per link. To the rest of the Internet the network is still a single one; internally the routers distinguish the subnets. The subnet field can have any size (RFC 950 asked for at least 2 bits; today, with CIDR, any value), and it is defined by a 32-bit mask.

## Slide 60: The subnet mask and the comparison under mask
Mask: 32 bits, with 1s in the network and subnet positions and 0s in the host positions; always contiguous (e.g., 255.255.255.0 = /24)
Comparison under mask: bitwise AND between address and mask; the host bits are zeroed and the subnet identifier remains
The subnet field can have any size; /n says how many bits are 1
Used by the host (local or remote destination?) and by the router (which route matches the destination? longest prefix)
A | B | A AND B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
AND truth table: only 1 AND 1 gives 1
Practical rules
Mask 255 in an octet: copy the address octet
Mask 0: zero the octet
Intermediate mask (128 to 254): convert to binary and apply the AND bit by bit
Prefix /n ⇔ mask with n leading 1 bits
Notes: The mask is a 32-bit pattern with 1s in the network and subnet positions and 0s in the host positions. The fundamental operation is the comparison under mask: a bitwise AND between the address and the mask; every address bit whose mask bit is 0 is zeroed, and the result is the subnet identifier, which is compared with that of the route or of the host itself. The current specification requires contiguous masks (all 1s on the left); noncontiguous masks were allowed in RFC 950 but were never practical and have been forbidden since RFC 1519. This operation is executed by every host when sending a packet (local or remote?) and by every router when consulting its table (longest prefix match).

## Slide 61: Comparison under mask: example
172.16.128.2
10101100
00010000
10000000
00000010
address
AND
255.255.255.0
11111111
11111111
11111111
00000000
mask /24
result
10101100
00010000
10000000
00000000
= 172.16.128.0
172
16
128
0
Classic reading (1999)
Network (class B): 172.16.0.0
Subnet: 172.16.128.0 (8 borrowed bits)
Host: .2
CIDR reading (2026)
The host belongs to prefix 172.16.128.0/24
Host range: 172.16.128.1 to 172.16.128.254
Directed broadcast: 172.16.128.255
Notes: Host 172.16.128.2 with mask 255.255.255.0 (/24). Write address and mask in binary, AND column by column and convert back: 172.16.128.0. That is the subnet identifier. The 'network' in the old sense (class B) would be 172.16.0.0; the subnet, 172.16.128.0. With CIDR we simply say the host belongs to prefix 172.16.128.0/24. The original used 134.141.128.2; the logic is identical.

## Slide 62: Addressing with subnets in an internetwork
Internet
advertises only 172.16.0.0/16
Autonomous system: 172.16.0.0/16
R1
172.16.10.0/24
R2
R3
172.16.20.0/24
172.16.30.0/24
172.16.40.0/24
172.16.50.0/24
One subnet per link; each router interface gets an address from the subnet of its link
Notes: The diagram shows an autonomous system that received the prefix 172.16.0.0/16 and divided it into /24 subnets, one per link: 172.16.10.0/24, .20.0, .30.0, .40.0 and .50.0. To the Internet only the aggregate 172.16.0.0/16 is advertised (in this example, being private, it would not even be advertised; imagine a public block). Internally, the routers exchange the subnets through the IGP. Every router interface gets an address in the subnet of the link it is attached to; by convention the first or the last usable address.

## Slide 63: Host addressing with subnets
R1
E0
E1
172.16.128.1 /24
172.16.64.1 /24
Subnet 172.16.128.0/24
Subnet 172.16.64.0/24
H
172.16.128.2
H
172.16.128.3
H
172.16.128.4
H
172.16.64.2
H
172.16.64.3
H
172.16.64.4
Breakdown of 172.16.128.2 /24
172
16
128
2
Network (16 bits, historical class B)
Subnet (8 bits)
Host (8 bits)
Every host needs three parameters: address, mask (or prefix) and default gateway (the router's address on its subnet). Today DHCP delivers all three; in IPv6, RA/SLAAC delivers prefix and router and DHCPv6 complements.
Notes: Two links joined by a router: 172.16.128.0/24 on interface E0 (172.16.128.1) and 172.16.64.0/24 on E1 (172.16.64.1). The hosts on each side get addresses in their subnet and use the router's address as default gateway. The breakdown of address 172.16.128.2 shows the three levels: network 172.16, subnet 128, host 2. Question for the class: can host 172.16.128.2 talk directly to 172.16.64.2? No: the comparison under mask yields different subnets, so the packet goes to the gateway (next slides).

## Slide 64: Special addresses in a subnetted environment
In every subnet
All host bits = 1: directed broadcast of the subnet (172.16.128.255 for 172.16.128.0/24)
All host bits = 0: subnet identifier (172.16.128.0)
Neither can be assigned to a host: usable = 2^h - 2
Example: 172.16.128.0/24
Subnet: 172.16.128.0
Hosts: 172.16.128.1 to 172.16.128.254 (254)
Directed broadcast: 172.16.128.255
Gateway (convention): .1 or .254
Old rule (RFC 950, 1985) | Current rule | Reference
Do not use the first subnet ('subnet zero') nor the last ('all-ones') | Both usable; default on all modern equipment | RFC 1878 (1995)
Point-to-point links with /30 (4 addresses, 2 usable) | /31 allowed: 2 addresses, both usable, no broadcast | RFC 3021 (2000)
Router loopback in an ordinary subnet | /32 per loopback; host route | Current practice
Directed broadcast forwarded by routers | Disabled by default ('smurf' attacks) | RFC 2644 (1999)
Notes: Within each subnet, the address with all host bits set to 1 is the directed broadcast of that subnet (172.16.128.255 for 172.16.128.0/24) and the address with all host bits set to 0 identifies the subnet itself; neither can be assigned to a host. That is why the number of usable hosts is 2^(host bits) - 2. Two important updates: (1) RFC 950 recommended not using the first ('subnet zero') and the last ('all-ones') subnets of a block; that fell with CIDR (RFC 1878) and all modern equipment uses them; (2) RFC 3021 (2000) allows /31 on point-to-point links, with two addresses and no broadcast, doubling the efficiency versus /30; and /32 is used for loopbacks.

## Slide 65: Masks off the octet boundary (VLSM)
Example: 203.0.113.77 /29 (mask 255.255.255.248)
203.0.113.77
11001011
00000000
01110001
01001|101
address
AND
255.255.255.248
11111111
11111111
11111111
11111|000
mask /29
subnet
11001011
00000000
01110001
01001|000
= 203.0.113.72
subnet | host
Result
Subnet: 203.0.113.72/29
Hosts: .73 to .78 (6)
Broadcast: .79
The 'step' shortcut
256 - 248 = 8 → subnets every 8: .0, .8, .16 ... .72, .80
77 lies between 72 and 80 → subnet .72
Other masks
/25 step 128; /26 step 64; /27 step 32; /28 step 16; /30 step 4
In the 3rd octet (/17 to /23) the step counts in multiples of 256 addresses
Notes: When the number of subnet bits does not fall on an octet boundary, you must work in binary. Example: 203.0.113.77 with mask 255.255.255.248 (/29): the last octet 77 = 01001101; the mask 248 = 11111000 keeps the first five bits (01001 = 72) and zeroes the three host bits. So the subnet is 203.0.113.72/29, the hosts go from .73 to .78 and the broadcast is .79. The 'step' between /29 subnets is 256 - 248 = 8: .0, .8, .16, ..., .72, .80. The original used 197.129.59.77 with five subnet bits on a class C; the arithmetic is the same. With VLSM, a /24 block can be split into subnets of different sizes, as the next slide shows.

## Slide 66: VLSM in practice: addressing plan for a /24
Need | Hosts | Prefix | Subnet | Host range | Broadcast
Users | 100 | /25 (126) | 172.16.20.0/25 | .1 to .126 | .127
Servers | 50 | /26 (62) | 172.16.20.128/26 | .129 to .190 | .191
Management | 25 | /27 (30) | 172.16.20.192/27 | .193 to .222 | .223
Printers | 10 | /28 (14) | 172.16.20.224/28 | .225 to .238 | .239
WAN link 1 | 2 | /30 (2) | 172.16.20.240/30 | .241 to .242 | .243
WAN link 2 | 2 | /30 (2) | 172.16.20.244/30 | .245 to .246 | .247
WAN link 3 | 2 | /30 (2) | 172.16.20.248/30 | .249 to .250 | .251
Spare | - | /30 | 172.16.20.252/30 | .253 to .254 | .255
VLSM rules: allocate from largest to smallest; each subnet starts at a multiple of its size; no overlap; the IGP must be classless (RIPv2, EIGRP, OSPF, IS-IS).
Modern variant: point-to-point links with /31 (RFC 3021) free up 8 addresses; router loopbacks use /32 in a separate block (e.g., 172.16.255.0/24).
Notes: Model exercise: split 172.16.20.0/24 to serve a network of 100 users, one of 50 servers, one of 25 management devices, one of 10 printers and four point-to-point links. Golden rule of VLSM: allocate from the largest to the smallest subnet, always on boundaries aligned to the block size. 172.16.20.252/30 is left over and, if the links use /31, even more space. Ask the students to redo the plan with /31 on the links (RFC 3021) and to discuss where to place the gateway address in each subnet.

## Slide 67: Internet Protocol behavior
MODULE 2 | PART 2
How a host decides where to send a packet: route determination (local or remote), next-hop lookup and address resolution with ARP
Notes: This part follows the original slide by slide: host communication, route determination, local and remote destinations, gateway lookup, and then ARP in three scenarios (local host, remote host, Proxy ARP). We close with a complete data-transfer example across two routers.

## Slide 68: IP host communication: always two steps
1
Route determination
Is the destination local (same prefix as mine) or remote? If remote, what is the next hop (gateway) for it? Decided from the host's address, mask and route table.
2
Address resolution
What is the data-link (MAC) address of the local destination, or of the next hop? ARP in IPv4; Neighbor Discovery (ND) in IPv6. Result kept in a cache.
Always, on every host
IP hosts perform these steps regardless of configuration or topology. Understanding them is the basis of connectivity troubleshooting.
Verification tools
Linux: ip route get <destination>; ip neigh
Windows: route print; arp -a
macOS: netstat -rn; arp -an
Routers: show ip route; show ip arp
Notes: Every IP communication starts with two steps on the source host: (1) route determination: is the destination local (same link) or remote (behind a router)? If remote, what is the next hop? (2) address resolution: what is the MAC of the destination (if local) or of the next hop (if remote)? These steps always happen, on every operating system and in every topology, even when the administrator never thought about them; they are the basis for troubleshooting 'I can't ping'.

## Slide 69: Route determination: local or remote?
First step: is the destination IP local or remote?
Local: host inside the same network or subnet address space (prefix) as the source
Remote: host outside the source's prefix; reachable only through a router
The source uses its IP, its mask and the destination IP in the decision (comparison under mask of both addresses)
Modern implementation: lookup in the host's route table with longest prefix match (equivalent)
Inputs of the decision
Source IP: 172.16.128.7
Mask: 255.255.255.0 (/24)
Destination IP: 172.16.128.2 (or 172.16.64.2)
Possible outcomes
Local → resolve the destination's MAC (ARP)
Remote → look up the next hop (gateway) and resolve its MAC
No route → 'network unreachable' error on the host itself
Notes: The first step is deciding whether the destination IP is local or remote. Local destination: it is within the same prefix (network or subnet) as the source host; remote destination: it is outside that prefix. The host uses three pieces of information: its own IP address, its mask (prefix) and the destination IP address. It applies the mask to both addresses (comparison under mask) and compares the results. Note for 2026: modern hosts do this by consulting their route table with longest prefix match, which is equivalent to the comparison under mask when there is only the connected-subnet route and the default route.

## Slide 70: Route determination logic
(destination IP AND mask) = (source IP AND mask)?
YES
NO
LOCAL destination
Both stations are on the same link. The source sends directly to the destination.
REMOTE destination
The source consults its route table, picks the next hop (gateway) and sends the packets to it.
Address resolution (ARP / ND)
for the IP of the destination (local) or of the gateway (remote)
Notes: The flowchart from the original: IF (destination IP AND source mask) = (source IP AND source mask) THEN the destination is on the same physical link and the source can send directly; ELSE the source consults its route table to find the next hop (gateway) and sends the packets to it. In both cases, the next step is address resolution (ARP) for the chosen IP: the destination or the gateway.

## Slide 71: Local or remote: example with AND
Destination: 172.16.128.2
172.16.128.2 (destination)
10101100
00010000
10000000
00000010
AND 255.255.255.0
11111111
11111111
11111111
00000000
result
10101100
00010000
10000000
00000000
172.16.128.0
172.16.128.7 (source)
10101100
00010000
10000000
00000111
AND 255.255.255.0
11111111
11111111
11111111
00000000
result
10101100
00010000
10000000
00000000
172.16.128.0
Equal results → LOCAL destination (same link)
What if the destination were 172.16.64.2? AND → 172.16.64.0 ≠ 172.16.128.0 → REMOTE
Check it on the operating system
Linux: ip route get 172.16.128.2 → 'dev eth0' (local); ip route get 172.16.64.2 → 'via 172.16.128.1' (remote, through the gateway)
Notes: Source 172.16.128.7, mask 255.255.255.0, destination 172.16.128.2. AND of the destination with the mask: 172.16.128.0; AND of the source with the mask: 172.16.128.0. Equal results, so the destination is local. Repeat with destination 172.16.64.2: the AND gives 172.16.64.0, different from 172.16.128.0, so remote. The original used 134.141.128.x.

## Slide 72: Local destinations
If the destination subnet is the same as the source's, communication happens without a router
Frames are transmitted directly on the attached link (L2 switches along the way are transparent; 'same link' = same VLAN)
The source moves immediately to address resolution (ARP) to obtain the destination's MAC
Common troubleshooting mistake: a wrong mask makes the host believe a remote destination is local (and the ARP is never answered)
A
172.16.128.7 /24
B
172.16.128.2 /24
SW (VLAN 128)
direct frame: MAC B
Subnet 172.16.128.0/24: no router involved
Notes: If the destination network and the source network are the same, communication happens without a router: the frames are transmitted directly on the link both stations are attached to. The host moves immediately to the address resolution phase to obtain the destination's MAC. Note that 'same link' today means, in practice, 'same VLAN': Layer 2 switches between the stations are transparent.

## Slide 73: Remote destinations
Remote destination: an intermediate step is required before address resolution
Next-hop gateway lookup: which router to use to reach the remote network?
The source then resolves the MAC of the gateway, not of the final destination
The IP packet is still addressed to the final destination; only the Ethernet frame is addressed to the gateway
A
172.16.128.7 /24
R1
gw .128.1
B
172.16.64.2 /24
frame: MAC R1
IP packet: source 172.16.128.7 → destination 172.16.64.2
Ethernet frame: MAC A → MAC R1
Different subnets (128.0/24 and 64.0/24): a router is mandatory
Notes: If the source determines that the destination is remote, there is an intermediate step before address resolution: the next-hop gateway lookup. It determines which router the source will use to forward packets to the remote network. Only then does the source ARP, and it ARPs for the gateway, not for the destination.

## Slide 74: Next-hop gateway lookup
The source consults its route table to find the next hop for the remote network
Sources of a host's table: the connected-subnet route, the default gateway (DHCP or RA), static routes, and on servers/routers, dynamic protocols (RIP, OSPF, BGP)
Selection by longest prefix match: the most specific route wins; /0 (default) matches everything and is used last
Result: the IP of a router on the same link as the source
Destination | Next hop | Interface | Route source
172.16.128.0/24 | connected | eth0 | interface address
172.16.64.0/24 | 172.16.128.1 | eth0 | static
10.0.0.0/8 | 172.16.128.2 | eth0 | static (VPN)
0.0.0.0/0 | 172.16.128.1 | eth0 | DHCP (default gateway)
Route table of a host (ip route / route print)
Lookup examples
172.16.128.9 → matches the connected /24 → local
172.16.64.2 → matches the static /24 → via 172.16.128.1
10.1.2.3 → matches the /8 → via 172.16.128.2
8.8.8.8 → only the /0 → via 172.16.128.1
Notes: The source station consults its route table to determine the next hop for the remote network. A host's table may be built from static routes, from the default gateway (received by DHCP or RA) or, on servers and routers, from dynamic protocols. The result is the IP address of a directly connected router (on the same link) able to forward toward the destination. The lookup follows the longest-prefix rule: among all routes matching the destination, the most specific wins; the default route (/0) matches everything and wins last.

## Slide 75: IP communication: what the host knows at this point
Already determined (network layer)
Whether the destination is local or remote
If remote, the IP address of the next hop (router)
The IP packet can be built: source, destination, TTL, protocol...
Still missing (data link layer)
The MAC address of the destination (if local) or of the next hop (if remote)
Without it, the Ethernet frame cannot be built
Solution: ARP (IPv4) or ND (IPv6), with a cache
Destination MAC = ?
Source MAC = A
0x0800
IP: 172.16.128.7 → 172.16.64.2 | data
FCS
The frame is ready except for the destination MAC: ARP resolves that
Notes: Intermediate summary. The source host has determined (1) whether the destination is local or remote and (2), if remote, the logical address of the next hop. It has all the network-layer information. What is missing is the data-link-layer information: the MAC of the destination or of the gateway. That is where ARP comes in.

## Slide 76: Address resolution: ARP (RFC 826)
Direct transmission or via the gateway, communication on the link is always MAC to MAC
The source must resolve the MAC of the destination or of the next hop before transmitting
ARP (RFC 826): a broadcast question 'who has IP X?'; the owner replies in unicast with its MAC
Every host keeps an ARP cache with the IP → MAC mappings (entries expire: Linux revalidates after ≈ 30 s; Cisco IOS 4 h)
Encapsulated directly in Ethernet (0x0806), never crosses routers; in IPv6 it is replaced by Neighbor Discovery (ND)
A
172.16.10.1
B
172.16.10.200
1. ARP Request (broadcast)
2. ARP Reply (unicast)
IP | MAC | Age
172.16.10.200 | 00-00-5E-00-53-0B | 0 s
ARP cache of A after the exchange (arp -a / ip neigh)
Notes: Whether the destination is direct or the gateway, transmission on the link is always MAC to MAC. The source must resolve the MAC corresponding to the chosen IP before transmitting. IP uses ARP (Address Resolution Protocol, RFC 826, 1982) to obtain the IP → MAC mapping: it sends a question in broadcast ('who has IP X?') and the owner answers in unicast with its MAC. Every host keeps an ARP cache with the learned mappings, so it does not have to ask for every packet. ARP is encapsulated directly in Ethernet (EtherType 0x0806), not in IP, and only works within the link: routers do not forward ARP. In IPv6 the role belongs to Neighbor Discovery (ND, RFC 4861), using ICMPv6 and multicast.

## Slide 77: ARP, local host example (1 of 6): the scenario
A
172.16.10.1 /24
00-00-5E-00-53-0A
B
172.16.10.200 /24
00-00-5E-00-53-0B
Ethernet link: subnet 172.16.10.0/24
C
another station
Host A has yet to communicate with host B
A wants to open an SSH session (TCP 22) to B
A's TCP/IP stack applies the route determination logic: is B local or remote?
Notes: Host A (172.16.10.1/24) has never communicated with host B (172.16.10.200/24) and wants to open an SSH session to it. (The original used Telnet; SSH is the modern equivalent.) A's TCP/IP stack runs the route determination logic to find out whether B is local or remote. Point out that, from ARP's point of view, the application hardly matters: the process is the same for any IP packet.

## Slide 78: ARP, local host example (2 of 6): B is local; empty cache
A
172.16.10.1 /24
00-00-5E-00-53-0A
B
172.16.10.200 /24
00-00-5E-00-53-0B
Ethernet link: subnet 172.16.10.0/24
C
another station
Route determination
172.16.10.200 AND /24 = 172.16.10.0
172.16.10.1 AND /24 = 172.16.10.0
Equal → B is local
ARP cache of A
Looks up 172.16.10.200 → not found
A must send an ARP Request
The SSH packet waits in the queue until the reply
Notes: The AND of the destination IP and of the source IP with A's mask gives the same result, 172.16.10.0: B is local. A looks in its ARP cache for the mapping of 172.16.10.200, but the cache is empty (or the entry expired). A needs to ask the network.

## Slide 79: ARP, local host (3 of 6): ARP Request in broadcast
A
172.16.10.1 /24
00-00-5E-00-53-0A
B
172.16.10.200 /24
00-00-5E-00-53-0B
Ethernet link: subnet 172.16.10.0/24
C
another station
ARP Request: broadcast FF-FF-FF-FF-FF-FF (everyone receives it)
A sends an ARP Request in a broadcast Ethernet frame (FF-FF-FF-FF-FF-FF, EtherType 0x0806)
Every station on the link receives the frame and examines the request (including C)
Question: 'who has 172.16.10.200? reply to 172.16.10.1 (00-00-5E-00-53-0A)'
Notes: A transmits an ARP Request encapsulated in an Ethernet frame with a broadcast destination (FF-FF-FF-FF-FF-FF) and EtherType 0x0806. Every station on the link (on the VLAN) receives the frame and hands its contents to the ARP software, which compares the 'target IP' with its own. On a VLAN with hundreds of hosts, every ARP Request interrupts all of them: that is why large broadcast domains cost CPU on every station.

## Slide 80: The ARP Request packet
ARP packet (RFC 826), operation = 1 (Request)
Hardware type = 1 (Ethernet)
Protocol type = 0x0800 (IPv4)
HLEN = 6
PLEN = 4
Operation = 1 (Request)
Sender MAC (A): 00-00-5E-00-53-0A
Sender IP (A): 172.16.10.1
Target MAC: 00-00-00-00-00-00 (unknown)
Target IP (B): 172.16.10.200
Ethernet frame that carries it
Destination
FF-FF-FF-FF-FF-FF
Source
00-00-5E-00-53-0A
Type
0x0806
ARP (28 B) + padding (18 B)
FCS
Notes
The target MAC is zeroed: it is exactly what we want to discover
The hardware and protocol fields allow ARP for other pairs (e.g., Token Ring/IPX in 1999); today only Ethernet/Wi-Fi + IPv4
Whoever receives the request also learns the sender's IP/MAC pair (many stacks cache it)
Wireshark capture: filter 'arp'
Notes: ARP format (28 bytes for Ethernet/IPv4): hardware type (1 = Ethernet), protocol type (0x0800 = IPv4), hardware address length (6) and protocol address length (4), operation (1 = request, 2 = reply), sender MAC and IP, target MAC and IP. In the request, the target MAC is unknown (filled with zeros). The Ethernet frame carrying it has a broadcast destination, source = A's MAC and EtherType 0x0806; the data field is padded up to 46 bytes.

## Slide 81: ARP, local host example (4 of 6): B processes the request
A
172.16.10.1 /24
00-00-5E-00-53-0A
B
172.16.10.200 /24
00-00-5E-00-53-0B
Ethernet link: subnet 172.16.10.0/24
C
another station
1
Delivery to ARP
B's MAC layer forwards the ARP Request to the ARP software in B's IP stack (EtherType 0x0806).
2
Recognition
B's ARP recognizes the target IP, 172.16.10.200, as its own; the other stations (C) discard the request.
3
Reply
B's ARP process formulates an ARP Reply and hands it to the MAC layer for unicast transmission to A.
Notes: B's MAC layer hands the ARP Request to the ARP software in B's IP stack. ARP recognizes the target IP (172.16.10.200) as its own. The other stations (C) silently discard the request, because the target IP is not theirs. B then builds an ARP Reply and hands it to the MAC layer for transmission. Many implementations take the opportunity to record A's IP/MAC pair in B's cache, since they will probably answer A right away.

## Slide 82: ARP, local host example (5 of 6): ARP Reply in unicast
A
172.16.10.1 /24
00-00-5E-00-53-0A
B
172.16.10.200 /24
00-00-5E-00-53-0B
Ethernet link: subnet 172.16.10.0/24
C
another station
ARP Reply: unicast to 00-00-5E-00-53-0A
B's ARP sends the ARP Reply to A, providing B's MAC (00-00-5E-00-53-0B)
The reply is unicast: a frame from MAC B to MAC A; the other stations do not see it
B normally stores A's IP/MAC pair in its own cache (learned from the request)
Notes: B's ARP software sends the reply to A, providing B's MAC. The reply is unicast: an Ethernet frame from MAC B to MAC A (B learned A's MAC from the request itself). Depending on the stack, B also stores A's mapping in its ARP cache, avoiding an ARP Request in the reverse direction when answering the SSH session.

## Slide 83: The ARP Reply packet
ARP packet (RFC 826), operation = 2 (Reply)
Hardware type = 1 (Ethernet)
Protocol type = 0x0800 (IPv4)
HLEN = 6
PLEN = 4
Operation = 2 (Reply)
Sender MAC (B): 00-00-5E-00-53-0B
Sender IP (B): 172.16.10.200
Target MAC (A): 00-00-5E-00-53-0A
Target IP (A): 172.16.10.1
Ethernet frame that carries it
Destination
00-00-5E-00-53-0A
Source
00-00-5E-00-53-0B
Type
0x0806
ARP (28 B) + padding
FCS
IP | MAC | Type
172.16.10.200 | 00-00-5E-00-53-0B | dynamic
ARP cache of A after receiving the reply
Security
ARP authenticates nothing: any station can answer for any IP (ARP spoofing / poisoning)
Defenses: Dynamic ARP Inspection + DHCP snooping on the switches, static entries on critical hosts
Notes: In the reply, the operation is 2 and the sender and target fields are filled with B's data (sender) and A's data (target). The Ethernet frame is unicast: destination = A's MAC, source = B's MAC, EtherType 0x0806. On receiving it, A installs the entry 172.16.10.200 → 00-00-5E-00-53-0B in its cache.

## Slide 84: ARP, local host example (6 of 6): communication proceeds
A
172.16.10.1 /24
00-00-5E-00-53-0A
B
172.16.10.200 /24
00-00-5E-00-53-0B
Ethernet link: subnet 172.16.10.0/24
C
another station
SSH: frame to 00-00-5E-00-53-0B
A installs the entry 172.16.10.200 → 00-00-5E-00-53-0B in its ARP cache
A's stack now has destination IP and MAC: the queued SSH segment is transmitted
Subsequent packets use the cache (no new ARP) until the entry expires or is invalidated
Notes: On receiving the ARP Reply, A's ARP process installs B's entry in the cache. A's stack now has everything it needs: the destination IP (network layer) and the destination MAC (data link layer). The SSH segment that was queued is encapsulated and transmitted; the next packets use the cache, with no new ARP, until the entry expires.

## Slide 85: ARP, remote host example (1 of 4): the scenario
A
172.16.10.1 /24
gateway: 172.16.10.254
172.16.10.0/24
R1
.10.254 | .100.254
other subnets
172.16.100.0/24
B
172.16.100.1 /24
00-00-5E-00-53-0B
Host A has yet to communicate with B and wants to open an SSH session
A has a subnet mask (/24) and a default gateway: R1, 172.16.10.254
The default gateway gives A a next hop for every destination outside subnet 172.16.10.0/24
Notes: Same intent (A wants SSH to B), but now B is on another subnet: A is 172.16.10.1/24 and B is 172.16.100.1/24. A is configured with the subnet mask (/24) and with a default gateway, router R1 (172.16.10.254). The default gateway provides A with a next hop for every destination outside its local segment.

## Slide 86: ARP, remote host example (2 of 4): B is remote
A
172.16.10.1 /24
gateway: 172.16.10.254
172.16.10.0/24
R1
.10.254 | .100.254
other subnets
172.16.100.0/24
B
172.16.100.1 /24
00-00-5E-00-53-0B
Route determination
172.16.100.1 AND /24 = 172.16.100.0
172.16.10.1 AND /24 = 172.16.10.0
Different → B is remote
Next step
Next-hop lookup in A's route table
Goal: a router on A's link that reaches 172.16.100.0/24
Notes: By the route determination logic, A concludes that B is remote: 172.16.100.1 AND /24 = 172.16.100.0, different from 172.16.10.0. A must then perform the next-hop lookup to find a router able to reach the remote subnet.

## Slide 87: ARP, remote host (3 of 4): default route and ARP for the gateway
A
172.16.10.1 /24
gateway: 172.16.10.254
172.16.10.0/24
R1
.10.254 | .100.254
other subnets
172.16.100.0/24
B
172.16.100.1 /24
00-00-5E-00-53-0B
ARP Request: who has 172.16.10.254 (R1)?
Destination | Next hop | Source
172.16.10.0/24 | connected | interface
0.0.0.0/0 | 172.16.10.254 | default gateway
Route table of host A
Key point
A ARPs for R1 (172.16.10.254), NOT for B
The ARP broadcast does not cross the router: an ARP for B would go unanswered
Notes: The default gateway configuration created a default route entry in A's route table (0.0.0.0/0 via 172.16.10.254). A's stack believes R1 is the next hop for ALL remote destinations. Essential consequence: A ARPs for R1's local interface (172.16.10.254), not for B. An ARP for B would never be answered, since the broadcast does not cross R1.

## Slide 88: ARP, remote host example (4 of 4): communication via R1
A
172.16.10.1 /24
gateway: 172.16.10.254
172.16.10.0/24
R1
.10.254 | .100.254
other subnets
172.16.100.0/24
B
172.16.100.1 /24
00-00-5E-00-53-0B
frame to MAC R1; IP packet to B
Destination MAC: R1 (00-00-5E-00-53-01)
Source MAC: A
0x0800
Source IP 172.16.10.1 → destination IP 172.16.100.1 (B) | TCP 22
FCS
At the data link layer, A talks to R1's interface; at the network layer, to B
R1 receives the frame, discards the Ethernet header and routes by destination IP; on B's link, R1 does its own ARP for B
Resulting caches: A knows R1; R1 knows A and B; B knows R1 (and never A's MAC)
Notes: Once the MAC of R1's local interface is resolved, A's communication with B goes, at the data link layer, through the router's interface: frames from MAC A to MAC R1, carrying IP packets from 172.16.10.1 to 172.16.100.1. R1 receives the frames, discards the Ethernet header and routes by the destination network address. On B's link, R1 does its own ARP for B. A's cache will hold R1; R1's will hold A and B.

## Slide 89: Proxy ARP
LEGACY
An extension of ARP that routers can run: answer on behalf of hosts on other subnets (RFC 1027)
Original goal: minimize the routing knowledge required of hosts in a subnetted network
With Proxy ARP on the interface, the hosts on that subnet communicate with the whole network without a static route or a configured gateway
The hosts use the natural mask (e.g., /16) even though the network is divided into /24 subnets
In 2026: unnecessary with DHCP/RA; kept for special cases (VPN, migrations, legacy hosts); turn it off if you do not need it
Where it still shows up
VPN concentrators answering for remote clients with LAN IPs
Migration from a flat (bridged) network to a routed one without reconfiguring every host
'Local proxy ARP' to force traffic between hosts on the same VLAN through the router (private VLANs)
Risk: ARP caches full of entries pointing at the router; traffic 'mysteriously' routed
Notes: Proxy ARP (RFC 1027) is an extension of ARP that routers can run: answering ARP requests on behalf of hosts on other subnets. It was created to minimize the routing knowledge hosts needed in a subnetted network: hosts configured with the 'natural' mask (no subnets, no gateway) think everyone is on the same link and ARP for any destination; the router answers with its own MAC and forwards the traffic. Today it is rarely necessary (DHCP delivers mask and gateway), but it still exists in a few scenarios and is a classic source of strange behavior when left enabled without need.

## Slide 90: Proxy ARP, example (1 of 3): host with a 'flat' mask
A
172.16.10.1 /16 (natural mask)
no gateway configured
172.16.10.0/24
R1
Proxy ARP enabled
172.16.100.0/24
B
172.16.100.1 /24
ARP Request: who has 172.16.100.1 (B)?
Route determination on A (mask /16)
172.16.100.1 AND /16 = 172.16.0.0
172.16.10.1 AND /16 = 172.16.0.0
Equal → A believes B is local and ARPs for B
Without Proxy ARP
The ARP broadcast dies on A's link; B never receives it
A has no gateway: communication fails ('host unreachable')
Notes: Host A has address 172.16.10.1 with the natural mask 255.255.0.0 (/16) and no gateway. It wants to open SSH to B (172.16.100.1), which is actually on another /24 subnet behind R1. By the route determination logic, with the /16 mask, A is 'fooled': 172.16.100.1 AND /16 = 172.16.0.0 = 172.16.10.1 AND /16; A concludes B is local and ARPs for B, as it would for any host on network 172.16.0.0.

## Slide 91: Proxy ARP, example (2 of 3): R1 steps in
A
172.16.10.1 /16 (natural mask)
no gateway configured
172.16.10.0/24
R1
Proxy ARP enabled
172.16.100.0/24
B
172.16.100.1 /24
ARP Request: who has 172.16.100.1 (B)?
Destination | Next hop / interface
172.16.10.0/24 | connected, E0 (A's side)
172.16.100.0/24 | connected, E1 (B's side)
172.16.11.0/24 | via 172.16.10.230
Route table of R1
The proxy's decision
Is there a route to the target IP? Yes
Does the route leave through another interface? Yes → R1 answers on behalf of B
Notes: R1's interface on A's link receives the ARP Request broadcast. Normally the router would discard it, since the target IP is not its own. With Proxy ARP enabled on the interface, the proxy process consults R1's route table: there is a route to 172.16.100.1 (subnet 172.16.100.0/24 is connected to the other interface) and it does not leave through the same interface the request arrived on. Therefore R1 can serve as the next hop for A.

## Slide 92: Proxy ARP, example (3 of 3): R1 answers with its own MAC
A
172.16.10.1 /16 (natural mask)
no gateway configured
172.16.10.0/24
R1
Proxy ARP enabled
172.16.100.0/24
B
172.16.100.1 /24
ARP Reply: 172.16.100.1 is at MAC R1
IP | MAC
172.16.100.1 (B) | 00-00-5E-00-53-01 (R1!)
172.16.100.9 | 00-00-5E-00-53-01
172.16.200.3 | 00-00-5E-00-53-01
ARP cache of A: several remote IPs → the same MAC (R1)
R1 answers with the MAC of its interface instead of B's
A records the entry and starts sending frames to R1, which routes them
Troubleshooting: many IPs with the same MAC in the cache = Proxy ARP
Notes: R1 sends an ARP Reply to A placing the MAC of its own interface in place of B's MAC. A, believing the network is flat, receives the reply as if it came from B and records '172.16.100.1 → MAC R1' in its cache. From then on, A's frames to B go to R1, which routes them normally. Over time, A's cache accumulates several remote IPs mapped to R1's same MAC: the classic signature of Proxy ARP in action, useful in troubleshooting.

## Slide 93: ARP in 2026: gratuitous ARP, cache, security and IPv6
UPDATED
Gratuitous ARP
A host announces its own IP/MAC pair (sender = target)
Uses: detect a duplicate IP; update caches after a MAC change; VRRP/HSRP failover; VM migration
Cache and timers
Linux: entry 'reachable' for ≈ 30 s (15 to 45 s), then revalidated (ip neigh)
Cisco IOS: 4 h by default (arp timeout); Windows: ≈ 15 to 45 s
Large tables in data centers: thousands of VMs per VLAN
Security
ARP does not authenticate: cache poisoning allows interception (man in the middle)
Defenses: Dynamic ARP Inspection + DHCP snooping; static entries; segmentation
IPv6: Neighbor Discovery instead of ARP
ICMPv6 Neighbor Solicitation / Advertisement (RFC 4861)
Sent to a 'solicited-node' multicast (ff02::1:ffxx:xxxx), not to broadcast: only hosts with that suffix process it
Per-neighbor states: reachable, stale, delay, probe; also Router Discovery and redirects
Notes: Four topics that did not exist or did not matter in 1999. (1) Gratuitous ARP: a host announces its own IP/MAC pair (request or reply with sender = target); used to detect duplicate IPs, to update caches after a NIC swap and, crucially, by VRRP/HSRP and by VM migrations, to redirect traffic to the new owner of the IP. (2) Timers: Linux considers an entry 'reachable' for about 30 s (base_reachable_time, randomized between 15 and 45 s) and then revalidates it; Cisco IOS keeps entries for 4 h; VMs and containers create many entries. (3) Security: ARP does not authenticate; cache poisoning allows traffic interception; the standard defense is Dynamic ARP Inspection with DHCP snooping on the switches. (4) IPv6 does not use ARP: Neighbor Discovery (ND, RFC 4861) uses ICMPv6 Neighbor Solicitation/Advertisement sent to a 'solicited-node' multicast, so only the stations with that suffix process the request; neighbor state is tracked (reachable, stale, probe).

## Slide 94: IP in a routed internetwork: a complete example
MODULE 2 | PART 3
Four links, four routers (W, X, Y, Z) and two users (A and B): what happens to the frames and the packets at every hop
Notes: Synthesis example from the original (slides 108 to 117). Follow the headers at every hop with the students: the IP packet (source and destination) does not change; the Ethernet frame (MACs) is rebuilt at every router; the TTL drops by 1 at every hop.

## Slide 95: IP in a routed internetwork: the topology
172.16.25.0/24
A
172.16.25.22
00-00-5E-00-53-0A
X
.25.1 53-11
.26.1 53-12
172.16.26.0/24
W
.26.2 53-21
.27.1 53-22
172.16.27.0/24
B
172.16.27.23
00-53-0B
Y
Z
172.16.28.0/24
Element | Addresses
A | 172.16.25.22; gw .25.1
X | .25.1 (53-11), .26.1 (53-12)
W | .26.2 (53-21), .27.1 (53-22)
B | 172.16.27.23; gw .27.1
MACs: prefix 00-00-5E-00-53 (RFC 7042)
A starts the communication by applying route determination: is B local or remote?
B is remote: A looks up the next hop and finds the default route (X); resolves X's MAC with ARP
Two routing hops (X and W) to B's LAN
Notes: Four LANs interconnected by routers W, X, Y and Z. User A (172.16.25.22) wants to communicate with user B (172.16.27.23) through some application (SSH, HTTPS). The hosts received, via DHCP, their address, the /24 mask and the default gateway: X for A (172.16.25.1), W for B (172.16.27.1). The MACs follow the RFC 7042 documentation range; in the original they were real Cabletron (OUI 00-00-1D) and Cisco (00-00-0C) addresses. Overview of what will happen: A determines that B is remote, looks up the default route and resolves X's MAC; X routes to W over LAN 26; W delivers to B on LAN 27. Six steps on the next slides.

## Slide 96: The data transfer process: the six steps
172.16.25.0/24
A
172.16.25.22
00-00-5E-00-53-0A
X
.25.1 53-11
.26.1 53-12
172.16.26.0/24
W
.26.2 53-21
.27.1 53-22
172.16.27.0/24
B
172.16.27.23
00-53-0B
1
A sends the initial packet
Frame to X's MAC; IP packet to B.
2
X receives and processes
Strips the Ethernet header; consults the route table.
3
X forwards to the next hop
New frame to W's MAC; IP packet intact (TTL-1).
4
W receives the packet
Strips the Ethernet header; destination connected.
5
W delivers to B
ARP for B if needed; new frame to B's MAC.
6
B receives the packet
Own MAC and IP: delivery to transport (port).
Invariants: source IP (172.16.25.22) and destination IP (172.16.27.23) never change (no NAT). Variables: source and destination MACs on each link; TTL decremented at X and at W.
Notes: Map of the six steps to be detailed: (1) A sends the initial packet to X; (2) X receives and processes the packet; (3) X forwards the packet to W (next hop); (4) W receives the packet; (5) W delivers the packet to B; (6) B receives the packet. At each step, note what changes (Ethernet header, TTL) and what does not (IP addresses, payload).

## Slide 97: Step 1: A sends the initial packet
172.16.25.0/24
A
172.16.25.22
00-00-5E-00-53-0A
X
.25.1 53-11
.26.1 53-12
172.16.26.0/24
W
.26.2 53-21
.27.1 53-22
172.16.27.0/24
B
172.16.27.23
00-53-0B
Ethernet frame
Preamble
Destination MAC: X 53-11
Source MAC: A 53-0A
0x0800
IP packet
FCS
IP packet
TTL = 64
Proto 6
Source IP: 172.16.25.22 (A)
Destination IP: 172.16.27.23 (B)
TCP: port 22 + data
A formats an IP packet for B
To reach B, A sends to X: default route + ARP for X
Frame: A → X; packet: A → B; TTL = 64
Notes: A builds an IP packet destined for B (172.16.27.23). To reach B, A has to go through X: route determination says 'remote', the route table gives the default route via 172.16.25.1, and ARP (already resolved) gives X's MAC. The Ethernet frame leaves A with destination MAC = X, source MAC = A; the IP packet, with the initial TTL (64 on Linux and macOS, 128 on Windows), goes inside the frame's data field. The Layer 2 link is between A and X; the Layer 3 packet is from A to B.

## Slide 98: Step 2: X receives and processes the packet
172.16.25.0/24
A
172.16.25.22
00-00-5E-00-53-0A
X
.25.1 53-11
.26.1 53-12
172.16.26.0/24
W
.26.2 53-21
.27.1 53-22
172.16.27.0/24
B
172.16.27.23
00-53-0B
processes
Destination | Next hop
172.16.25.0/24 | connected
172.16.26.0/24 | connected
172.16.27.0/24 | 172.16.26.2 (W)
172.16.28.0/24 | 172.16.26.3 (Y)
Route table of X (OSPF or static)
1
Accepts the frame
Destination MAC = its own; discards the Ethernet header.
2
Validates the packet
Checksum ok, TTL > 1, destination is not X → routing.
3
Looks up the route
172.16.27.0/24 via 172.16.26.2 (W): binary AND with the mask.
Notes: X recognizes its own MAC in the frame and accepts it (frames for other MACs would be ignored by the interface). The Ethernet header is discarded; the IP packet is validated (checksum, TTL > 1) and, since the destination IP is not X's, it goes to the routing software. X consults its route table for the longest prefix matching 172.16.27.23: 172.16.27.0/24, learned by a dynamic protocol (or a static route), with next hop 172.16.26.2 (W) out the LAN 26 interface. Route determination here is based on the destination network, not the host.

## Slide 99: Step 3: X forwards the packet to the next hop (W)
172.16.25.0/24
A
172.16.25.22
00-00-5E-00-53-0A
X
.25.1 53-11
.26.1 53-12
172.16.26.0/24
W
.26.2 53-21
.27.1 53-22
172.16.27.0/24
B
172.16.27.23
00-53-0B
Ethernet frame
Preamble
Destination MAC: W 53-21
Source MAC: X 53-12
0x0800
IP packet
FCS
IP packet
TTL = 63
Proto 6
Source IP: 172.16.25.22 (A)
Destination IP: 172.16.27.23 (B)
TCP: port 22 + data
X knows the next hop for 172.16.27.0 is W (routing protocol or static)
X ARPs for 172.16.26.2 on LAN 26 (if needed)
New frame X → W; same packet A → B; TTL 63
Notes: X knows the next hop for 172.16.27.0/24 is W (172.16.26.2), learned from periodic routing-protocol updates or a static route. X builds a new Ethernet frame on LAN 26: destination MAC = W (resolved by ARP on LAN 26, if not already cached), source MAC = X's interface on LAN 26. The original IP packet is encapsulated with no change to the addresses; only the TTL drops to 63 and the header checksum is recomputed.

## Slide 100: Step 4: W receives the packet
172.16.25.0/24
A
172.16.25.22
00-00-5E-00-53-0A
X
.25.1 53-11
.26.1 53-12
172.16.26.0/24
W
.26.2 53-21
.27.1 53-22
172.16.27.0/24
B
172.16.27.23
00-53-0B
Destination | Next hop
172.16.26.0/24 | connected
172.16.27.0/24 | connected (E1)
172.16.25.0/24 | 172.16.26.1 (X)
172.16.28.0/24 | 172.16.27.9 (Z)
Route table of W
1
Accepts the frame
Destination MAC = W's interface on LAN 26; discards the Ethernet header.
2
Routes
Destination 172.16.27.23 matches 172.16.27.0/24, directly connected: the next hop is B itself.
Notes: W recognizes its MAC in the frame coming from X and discards all the Ethernet information. The network-layer information goes up to the routing software, which checks that the packet can be routed and looks up the route by destination prefix: 172.16.27.0/24 is directly connected to W's interface on LAN 27. Therefore, the 'next hop' is the final destination itself.

## Slide 101: Step 5: W delivers the packet to B
172.16.25.0/24
A
172.16.25.22
00-00-5E-00-53-0A
X
.25.1 53-11
.26.1 53-12
172.16.26.0/24
W
.26.2 53-21
.27.1 53-22
172.16.27.0/24
B
172.16.27.23
00-53-0B
Ethernet frame
Preamble
Destination MAC: B 53-0B
Source MAC: W 53-22
0x0800
IP packet
FCS
IP packet
TTL = 62
Proto 6
Source IP: 172.16.25.22 (A)
Destination IP: 172.16.27.23 (B)
TCP: port 22 + data
Destination on a connected network: W needs B's MAC
ARP Request from W on LAN 27 for 172.16.27.23 (or cache)
Frame W → B; packet A → B; TTL 62
Notes: W recognizes that the packet is destined for a directly connected network. To build the frame it needs B's MAC: it consults its ARP cache and, if there is no entry, sends an ARP Request on LAN 27 for 172.16.27.23. With B's MAC, W builds the frame: destination = B, source = W's interface on LAN 27, and encapsulates the original IP packet with TTL 62.

## Slide 102: Step 6: B receives the packet
172.16.25.0/24
A
172.16.25.22
00-00-5E-00-53-0A
X
.25.1 53-11
.26.1 53-12
172.16.26.0/24
W
.26.2 53-21
.27.1 53-22
172.16.27.0/24
B
172.16.27.23
00-53-0B
1
Accepts the frame
Destination MAC = B; copies the packet to the buffer.
2
Network layer
Destination IP = its own; Protocol 6 → delivers to TCP.
3
Transport and application
Port 22 → SSH server. The reply retraces the path in reverse (B → W → X → A).
Tally
3 links, 2 routers, 3 different frames
1 IP packet (addresses intact), TTL 64 → 62
Up to 6 ARP resolutions, all cached
Notes: B recognizes its MAC in the frame and copies the packet into its buffers. B's network layer verifies that the destination IP is its own and, by the Protocol field (6), hands the segment to TCP, which by the port number (22) hands it to the SSH server. B's reply to A takes the reverse path, with B doing its own route determination (A is remote → gateway W) and its own ARP for W. Close by asking: how many ARPs happened in total? (A for X, X for W, W for B, and on the return B for W, W for X, X for A: up to six, all cached afterwards.)

## Slide 103: Host names: from the hosts file to DNS
UPDATED
1999: local tables
Router: ip host name address
Hosts: hosts file
Local scope; no scale
2026: DNS (RFC 1034/1035 and successors)
Hierarchical namespace: root → TLD (.com, .br) → domain → host
Host resolver (DHCP/RA) → recursive server → authoritative servers
Records: A (IPv4), AAAA (IPv6), PTR (reverse), CNAME, MX, SRV, TXT
UDP/TCP 53; DNS over TLS (853) and HTTPS; DNSSEC
Host
resolver: 172.16.10.53
Recursive server
(172.16.10.53)
Root (.)
TLD (.com)
Authoritative
(example.com)
www.example.com? (AAAA)
2001:db8::80 (cached)
Typical precedence on the host: local cache → hosts file → DNS. The hosts file is still handy for testing (and causes trouble when forgotten).
Notes: The original slide showed the Cisco command 'ip host name address', which maps names to IPs locally on the router (useful only to the router itself). In 2026 the topic is DNS: a hierarchical namespace (root, TLDs, domains), resolved by recursive query from the resolver configured on the host (via DHCP or RA); records A (IPv4), AAAA (IPv6), PTR (reverse), CNAME, MX, SRV, TXT; transport UDP/TCP 53, with DNS over TLS (853) and over HTTPS (443) for privacy and DNSSEC for authenticity. The hosts file (/etc/hosts, C:\Windows\System32\drivers\etc\hosts) still exists and takes precedence over DNS on most systems, which makes it useful for testing and dangerous when forgotten.

## Slide 104: Proxy ARP configuration: vendor defaults
Platform | Default | How to enable / disable | Note
Cisco IOS / IOS-XE | Enabled | interface X / [no] ip proxy-arp | Also 'ip local-proxy-arp' for hosts on the same VLAN
Linux | Disabled | sysctl -w net.ipv4.conf.eth0.proxy_arp=1 | Used on VPN concentrators and virtualization
Juniper Junos | Disabled | set interfaces ge-0/0/0 unit 0 proxy-arp restricted ¦ unrestricted | 'restricted' answers only for hosts on other subnets
Cabletron (1999) | Disabled | IP General Config → Port Level Setup | Legacy
! Cisco IOS: disable Proxy ARP on the interface
configure terminal
interface GigabitEthernet0/0
no ip proxy-arp
! verify:
show ip interface GigabitEthernet0/0 | include Proxy
# Linux: enable Proxy ARP on eth0 (temporary)
sysctl -w net.ipv4.conf.eth0.proxy_arp=1
# persistent: /etc/sysctl.d/99-proxyarp.conf
net.ipv4.conf.eth0.proxy_arp = 1
# check neighbors:
ip neigh show dev eth0
Recommendation: Proxy ARP off by default; enable it only with a documented need (VPN, migration) and per interface.
Notes: In 1999 the slide compared Cabletron (disabled by default, configured in the 'Port Level Setup' of the IP General Config screen) and Cisco (enabled by default on every interface configured for IP; 'no ip proxy-arp' to turn it off). Today: Cisco IOS/IOS-XE still enables Proxy ARP by default on interfaces (check with 'show ip interface'); Linux disables it by default (sysctl net.ipv4.conf.<if>.proxy_arp); Junos disables it by default (proxy-arp restricted or unrestricted per interface). 2026 recommendation: leave it off unless there is a documented need; DHCP delivers the correct mask and gateway to the hosts.

## Slide 105: IP routing protocols
MODULE 2 | PART 4
RIP, administrative distance, EIGRP, multipath routing and redistribution; OSPF in detail; OSPFv3 and IS-IS; EGP and BGP-4
Notes: The original covered RIP, IGRP and OSPF, with EGP and BGP on two slides. The 2026 version replaces IGRP with EIGRP, adds administrative distance, OSPFv3/IS-IS and expands BGP-4.

## Slide 106: RIP: Routing Information Protocol
One of the historically most used interior protocols; a direct implementation of distance vector
Advertises the whole table every 30 s: v1 in broadcast, v2 in multicast 224.0.0.9 (UDP 520)
Metric: hop count; 16 = infinity → maximum diameter of 15 hops
Timers (Cisco): update 30 s, invalid 180 s, hold-down 180 s, flush 240 s
Loops mitigated by split horizon, poison reverse, hold-down and triggered updates
2026: suitable only for small networks; great for teaching
Version | RFC | Characteristics
RIPv1 (1988) | 1058 | Classful: no mask; broadcast; no authentication
RIPv2 (1998) | 2453 | Classless (VLSM/CIDR); multicast 224.0.0.9; authentication; next hop; tag
RIPng (1997) | 2080 | IPv6; UDP 521; ff02::9; authentication via IPsec
Table update criteria
Unknown destination → install
Metric lower than the current one → replace
Same outgoing neighbor with a different metric → accept (even if worse)
Route not advertised for 180 s → invalid; removed at 240 s
Notes: RIP is the most direct implementation of distance vector: every router sends its whole table to its neighbors every 30 s (v1 in broadcast, v2 in multicast 224.0.0.9), uses hop count as the metric and treats 16 hops as infinity, which limits the network diameter to 15. Timers (Cisco): update 30 s, invalid 180 s, hold-down 180 s, flush 240 s. Versions: RIPv1 (RFC 1058, 1988), classful, no mask; RIPv2 (RFC 2453, 1998), classless, with mask, next hop, authentication and multicast; RIPng (RFC 2080, 1997) for IPv6, UDP 521 and ff02::9. Status in 2026: RIP survives in very small networks, labs and simple devices; for everything else, OSPF or EIGRP. It is still the best protocol for teaching distance vector.

## Slide 107: RIP: origin and variants
LEGACY
Protocol | Family | Relation to RIP | Status
XNS RIP | Xerox Network Systems (1970s) | Origin of the algorithm and the format | Extinct
routed (BSD UNIX 4.2, 1983) | TCP/IP | The implementation that popularized RIP on IP before RFC 1058 | Evolved into RIPv2 / RIPng
IPX RIP | Novell NetWare | Very similar to Xerox RIP; metric in ticks and hops | Extinct with IPX
RTMP | AppleTalk | Modified version of RIP | Extinct (Apple moved to IP in 2009)
RTP | Banyan VINES | Slight variation of Xerox RIP | Extinct
Lesson: a routing algorithm (Bellman-Ford) is independent of the network protocol. The same holds today: OSPF and IS-IS implement Dijkstra for IPv4 and IPv6; BGP carries IPv4, IPv6, VPNs and EVPN with the same path-vector mechanism.
Notes: RIP was not born with TCP/IP: it was developed at Xerox PARC as the routing protocol of XNS (Xerox Network Systems) in the late 1970s. The 'routed' implementation in BSD UNIX 4.2 (1983) spread it across TCP/IP years before it was formalized in RFC 1058. Novell adapted the XNS RIP for IPX; AppleTalk's RTMP and Banyan VINES' RTP were variations. All those derivatives died with their protocols; the only RIP still alive is the IP one (v2 and RIPng). The value of the slide is historical: it shows how the same Bellman-Ford idea was reused in every protocol family.

## Slide 108: RIPv2: message format and what is new
bit 0
bit 31
Command (1)
Version = 2
unused (0)
Address family identifier (2 = IP)
Route tag
Network IP address
Subnet mask (new in v2)
Next hop (new in v2)
Metric (1 to 16)
4-byte header + up to 25 entries of 20 bytes (504 bytes per message)
What version 2 added (RFC 2453)
Subnet mask per route: VLSM and CIDR
Next hop: avoids an extra hop when several routers share the link
Route tag: marks external/redistributed routes
Authentication: simple password; MD5 (RFC 2082); SHA (RFC 4822)
Multicast 224.0.0.9 instead of broadcast: hosts without RIP are not interrupted
Keeps: UDP 520, 30 s, 15 hops, Bellman-Ford
RIPng (RFC 2080) is RIPv2 for IPv6: 128-bit prefixes with length, UDP 521, group ff02::9, no authentication of its own (uses IPsec). Same limitations of 15 hops and 30 s.
Notes: The RIPv2 message (UDP 520) has a 4-byte header (command 1 = request, 2 = response; version 2) and up to 25 entries of 20 bytes. Each entry carries: address family identifier (2 = IP), route tag (to mark redistributed routes), IP address, subnet mask (the big novelty, which enables VLSM and CIDR), next hop (lets a router point to a better router on the same link) and metric (1 to 16). Authentication occupies the first entry (AFI 0xFFFF): simple password in RFC 2453, MD5 in RFC 2082 and modern cryptographic algorithms in RFC 4822. Using multicast 224.0.0.9 instead of broadcast spares the hosts that do not run RIP.

## Slide 109: Administrative distance: choosing among route sources
Route source | AD (Cisco)
Connected interface | 0
Static route | 1
EIGRP summary | 5
External BGP (eBGP) | 20
Internal EIGRP | 90
IGRP | 100 (legacy)
OSPF | 110
IS-IS | 115
RIP | 120
EGP | 140 (legacy)
External EIGRP | 170
Internal BGP (iBGP) | 200
Unknown / unusable | 255
Selection rule
1st: longest prefix (always wins, regardless of source)
2nd: among equal routes, the lowest AD enters the table
3rd: among routes from the same source, the lowest metric; tie → ECMP
Practical use: floating static
ip route 0.0.0.0 0.0.0.0 203.0.113.1 250
Only installed if the BGP-learned default route (AD 20) disappears: automatic backup
Junos uses 'preference' with its own scale; the concept is the same
Notes: New slide. When the same prefix is learned from different sources (static, OSPF, EIGRP, BGP...), the metrics are not comparable (hops versus cost versus bandwidth). The router uses administrative distance (AD): a trustworthiness value per source; the lowest wins and only that route goes into the routing table. The metric only breaks ties among routes from the same source. The values in the table are Cisco's defaults and widely copied; Junos uses 'route preference' with a different scale (direct 0, static 5, OSPF 10, IS-IS 15/18, RIP 100, OSPF external 150, BGP 170). AD is also the tool for floating static routes (backup): a static route with AD 250 only enters the table if the dynamic route disappears.

## Slide 110: From IGRP to EIGRP
UPDATED
IGRP (Cisco, 1980s): legacy
Created to overcome RIP's 15-hop limit (IGRP: up to 255)
Distance vector with a composite metric: delay, bandwidth, reliability and load, combined with adjustable weights
Multipath (up to 4 paths)
Classful (no mask in updates); advertisements every 90 s
Proprietary; removed from IOS in 2005
EIGRP (Cisco, 1992; RFC 7868, 2016)
Advanced distance vector: the DUAL algorithm guarantees loop-free routes and subsecond convergence, with no hold-down
IGRP's composite metric × 256; K1 and K3 (bandwidth and delay) by default
Only triggered, reliable updates (RTP); adjacencies by Hello (IP protocol 88, multicast 224.0.0.10)
Classless (VLSM/CIDR), summarization on any interface, IPv6 (ff02::a), unequal-cost multipath (variance)
AD 90 (internal) and 170 (external); 'open' through RFC 7868, but still essentially Cisco
Notes: IGRP (Interior Gateway Routing Protocol) was created by Cisco in the mid-1980s to overcome RIP's limitations, mainly the 15-hop maximum, using distance vector with a composite metric (delay, bandwidth, reliability and load) and multipath. It was classful and proprietary; Cisco removed it from IOS in 2005. Its successor, EIGRP (1992), kept the composite metric (multiplied by 256) and added the DUAL algorithm, which guarantees loop freedom and fast convergence without hold-down, triggered-only reliable updates (RTP), support for VLSM/CIDR, IPv6 and unequal-cost multipath. In 2016 Cisco published the specification as RFC 7868 (informational), allowing third-party implementations, but in practice EIGRP remains a Cisco-network protocol; OSPF is the multivendor choice. The original mentioned using IGRP to route ISO CLNP; that was Cisco specific and fell out of use.

## Slide 111: The EIGRP composite metric
Full formula (K1 to K5 configurable)
metric = 256 × [ K1 × B + (K2 × B) / (256 − L) + K3 × D ] × [ K5 / (R + K4) ] (the last factor only applies if K5 ≠ 0)
With the default weights (K1 = K3 = 1, K2 = K4 = K5 = 0):
metric = 256 × ( 10,000,000 / minimum_bandwidth[kbps] + Σ delay[µs] / 10 )
Example: three 1 Gbps links
Minimum bandwidth 1,000,000 kbps → 10^7 / 10^6 = 10
Delay: 3 × 10 µs = 30 µs → 30 / 10 = 3
metric = 256 × (10 + 3) = 3,328
Example: one 2 Mbps serial link
Bandwidth 2,000 kbps → 10^7 / 2,000 = 5,000
Default serial delay: 20,000 µs → 2,000
metric = 256 × (5,000 + 2,000) = 1,792,000
Notes: To compare two routes to the same destination, EIGRP computes a composite metric that can be understood as an expression of the total transmission delay. The full formula combines bandwidth (B), delay (D), reliability (R) and load (L) with weights K1 to K5 the administrator may adjust; by default K1 = K3 = 1 and K2 = K4 = K5 = 0, so only bandwidth and delay count, and reliability is not considered (as was already the case in IGRP). Bandwidth = 10^7 divided by the lowest bandwidth on the path in kbps; delay = the sum of the interface delays in tens of microseconds. The result is multiplied by 256 relative to IGRP (32-bit scale). Important: the bandwidth and delay values are the ones configured on the interfaces (bandwidth, delay), not measured; adjusting 'delay' is the recommended way to influence route selection.

## Slide 112: Example: the same topology with RIP and with EIGRP
Network A
R1
R2
Network B
serial 2 Mbps
R3
R4
1 Gbps
1 Gbps
1 Gbps
Protocol | Path chosen from A to B | Metric | Alternative
RIP | R1 → R2 (direct, 2 Mbps) | 1 hop | R1 → R3 → R4 → R2 = 3 hops (worse for RIP)
EIGRP | R1 → R3 → R4 → R2 (1 Gbps) | 3,328 | R1 → R2 = 1,792,000 (much worse)
OSPF?
Cost = reference bandwidth / bandwidth; also picks the 1 Gbps path
Notes: Consider the route R1 would use to send packets from network A to network B. With RIP, the metric is hops: the direct R1-R2 link (1 hop) wins, even though it is a 2 Mbps serial. With EIGRP, the composite metric prefers the path R1-R3-R4-R2, three hops at 1 Gbps (metric 3,328 versus 1,792,000). The original used 19.2 kbps versus T1 (1.544 Mbps); the speeds changed, the lesson did not: hops are a poor metric when links are heterogeneous.

## Slide 113: Loop detection: from IGRP's hold-down to EIGRP's DUAL
IGRP (legacy)
Split horizon and triggered updates, without poison reverse
Early versions: hold-down
Later versions: 'route poisoning': a path with an increasing metric is treated as unusable until confirmed by the following update
EIGRP: the DUAL algorithm
FD (feasible distance): the lowest known metric to the destination
RD (reported distance): the metric advertised by each neighbor
Feasibility condition: RD < FD ⇒ the neighbor is a feasible successor (a guaranteed loop-free path)
Successor fails and a feasible successor exists → local switch, no recomputation and no hold-down
When there is no feasible successor
The route goes active: queries to the neighbors, which reply with their best metric
Converges when every reply arrives; 'stuck in active' (SIA) if a neighbor is slow: 3-minute limit, mitigated by summarization and stub
Notes: IGRP used split horizon and triggered updates, without poison reverse; the early versions also used hold-down and the later ones 'route poisoning' (any path whose metric increased was treated as unusable until confirmed). EIGRP solved the problem definitively with DUAL (Diffusing Update Algorithm, by J.J. Garcia-Luna-Aceves): for each destination, the router keeps the feasible distance (FD, the best known metric) and, for each neighbor, the reported distance (RD, the metric the neighbor advertises). A neighbor is a feasible successor if its RD is lower than the FD: the feasibility condition mathematically guarantees that the path through it does not pass through me and therefore cannot loop. If the successor fails and a feasible successor exists, the switch is local and instantaneous; if none exists, the router goes 'active' and sends queries to its neighbors, which reply; the route converges when all replies arrive.

## Slide 114: Multipath routing (ECMP and unequal cost)
Routers keep several paths per destination, not only the best one
Two advantages: immediate switchover to the alternate path on failure and load sharing across equal-cost paths
ECMP in every modern IGP and in BGP: 4 to 64 paths; distribution by hash of the 5-tuple (a flow is never reordered), RFC 2991/2992
EIGRP variance N: also uses paths up to N times worse, if they are feasible successors (unequal cost)
Data center leaf-spine fabrics: dozens of ECMP paths over BGP
R1
R2
Ra
Rb
Rc
Three equal-cost paths: ECMP distributes the flows by hash
Flow (5-tuple) | Hash | Path
10.1.1.5:40001 → 10.2.2.9:443 | ... 0 | via Ra
10.1.1.5:40002 → 10.2.2.9:443 | ... 1 | via Rb
10.1.1.7:51000 → 10.2.2.9:22 | ... 2 | via Rc
Each flow always follows the same path: no TCP segment reordering.
Notes: IGRP kept a list of possible paths in memory, not just one per destination, which allowed switching to the backup path on failure and splitting load across equal-cost paths. Today every IGP does ECMP (Equal-Cost Multi-Path): routes with identical metrics are installed together (4 to 64, depending on the platform) and packets are distributed by hashing the 5-tuple, so a TCP flow is never reordered (RFC 2991/2992). EIGRP goes further with 'variance': it also accepts paths up to N times worse than the best, as long as they are feasible successors, and splits load proportionally. Modern data centers depend on ECMP over BGP in leaf-spine fabrics.

## Slide 115: Route redistribution (1 of 3): two routing domains
RIP domain
EIGRP domain
R1
R2
R3
R4
R5
R3
B
C
D
E
A
F
R3: boundary (both)
Table of R1 (RIP)
Net | Source | Metric
A | C | 0
B | C | 0
C | R | 1
D, E, F | unknown | -
Table of R3 (RIP + EIGRP)
Net | Source | Metric
C | C | 0
D | C | 0
B | R | 1
A | R | 2
E | D | 3,072
F | D | 3,328
Table of R5 (EIGRP)
Net | Source | Metric
E | C | 0
F | C | 0
D | D | 3,072
A, B, C | unknown | -
Without redistribution, only R3 (which runs both protocols) knows every network. The others reach only their own domain.
Notes: Scenario: the company runs RIP in the old part of the network (R1, R2) and EIGRP in the new part (R4, R5); R3 takes part in both processes. Without redistribution, each router knows only the networks of its own domain, plus the connected ones: R1 cannot reach D, E and F; R5 cannot reach A, B and C. Only R3 knows everything, having routes from both sources. Redistribution is the mechanism that injects routes learned by one process into the advertisements of the other. Sources in the tables: C = connected, R = RIP, D = EIGRP (the notation of Cisco's 'show ip route'). EIGRP metrics are illustrative values.

## Slide 116: Route redistribution (2 of 3): EIGRP → RIP
RIP domain
EIGRP domain
R1
R2
R3
R4
R5
R3
B
C
D
E
A
F
R3: boundary (both)
redistribute eigrp → rip (seed 1)
Table of R1 (RIP)
Net | Source | Metric
A | C | 0
B | C | 0
C | R | 1
D | R (redistr.) | 3
E | R (redistr.) | 3
F | R (redistr.) | 3
Table of R3
Net | Source | Metric
C | C | 0
D | C | 0
B | R | 1
A | R | 2
E | D | 3,072
F | D | 3,328
Table of R5 (EIGRP)
Net | Source | Metric
E | C | 0
F | C | 0
D | D | 3,072
A, B, C | still unknown | -
router rip
redistribute eigrp 100 metric 1
Seed metric is mandatory: the EIGRP routes enter RIP with 1 hop (R2 sees 2, R1 sees 3). Traffic from A to F leaves R1 toward R3.
Notes: R3 is configured to redistribute the routes learned by EIGRP into the RIP process. Since the metrics are incompatible (3,072 does not fit in 'hops'), a seed metric must be set for the redistributed routes, for example 1 hop; R2 will see them with 2 and R1 with 3. Without the seed metric, many implementations drop the routes (RIP) or mark them unreachable. Now R1 and R2 reach D, E and F through the route via R3.

## Slide 117: Route redistribution (3 of 3): both directions and the risks
RIP domain
EIGRP domain
R1
R2
R3
R4
R5
R3
B
C
D
E
A
F
R3: boundary (both)
eigrp → rip
rip → eigrp
Table of R1 (RIP)
Net | Source | Metric
A | C | 0
B | C | 0
C | R | 1
D | R | 3
E | R | 3
F | R | 3
Table of R5 (EIGRP)
Net | Source | Metric
E | C | 0
F | C | 0
D | D | 3,072
C | D EX (AD 170) | 2,816,000
B | D EX | 2,816,000
A | D EX | 2,816,000
Risks and defenses
Feedback: a route returns to its domain of origin with a better metric → loop or suboptimal path
Defenses: route tags + route-maps; prefix filters; AD (external 170 > RIP 120); one-way redistribution + default route
router eigrp 100
redistribute rip metric 10000 100 255 1 1500 route-map RIP-to-EIGRP
Notes: Mutual redistribution is completed: R3 also injects the RIP routes into EIGRP, with a seed metric expressed in EIGRP's five components (bandwidth, delay, reliability, load, MTU), and R4/R5 start reaching A, B and C. Mutual redistribution is powerful and dangerous: a route can return to its domain of origin with a better metric (route feedback) and create loops or suboptimal paths. Standard defenses: use route tags to avoid redistributing back what came from the other side, filter with prefix lists, and adjust administrative distance (external EIGRP has AD 170 precisely to lose against RIP, 120, in case of feedback). Whenever possible, prefer a single IGP or one-way redistribution with a default route in the other direction.

## Slide 118: OSPF: Open Shortest Path First
Open: public IETF specification (OSPF working group, late 1980s)
Shortest Path First: Dijkstra's algorithm over a link-state database
Created because RIP could not serve large, heterogeneous internetworks: 15 hops, slow convergence, no VLSM
Versions: OSPFv1 (RFC 1131, 1989); OSPFv2 (RFC 1247, 1991 → RFC 2328, 1998) for IPv4; OSPFv3 (RFC 5340, 2008) for IPv6 and, with address families (RFC 5838), also IPv4
Runs directly over IP (protocol 89); multicast 224.0.0.5 (all OSPF routers) and 224.0.0.6 (DR/BDR); ff02::5 and ff02::6 in v3
Interface cost
cost = reference bandwidth / interface bandwidth
Default: 10^8 (100 Mbps) → 1 Gbps and 100 Gbps would both cost 1!
Set 'auto-cost reference-bandwidth' (e.g., 100,000 Mbps) on every router
Why OSPF in 2026
Multivendor, mature, scalable with areas
Subsecond convergence with BFD and tuned timers
Alternative in providers and data centers: IS-IS
Notes: As the acronym says, OSPF has two primary characteristics: it is 'open' (a public specification, from the IETF) and based on the Shortest Path First algorithm (Dijkstra). It was developed by the IETF OSPF working group in the late 1980s (OSPFv1, RFC 1131, 1989; OSPFv2, RFC 1247, 1991; current version RFC 2328, 1998) because RIP was increasingly unable to serve large, heterogeneous internetworks: 15-hop limit, slow convergence, hop metric, no VLSM (v1). In 2026 OSPFv2 is still the most used IGP in enterprise networks; OSPFv3 (RFC 5340) routes IPv6 (and also IPv4, through address families, RFC 5838).

## Slide 119: OSPF: protocol overview (1 of 2)
1
Topology database (LSDB)
Every router maintains a database describing the topology of the area: every router, link and cost, in the form of LSAs.
2
The same algorithm everywhere
Every router runs exactly the same SPF (Dijkstra), in parallel, over the same LSDB; each computes the shortest-path tree with itself as the root.
3
Routes per type of service (legacy)
RFC 1247 allowed separate routes per ToS; RFC 2328 removed the feature. Today differentiation is done by QoS and traffic engineering, not by the IGP.
OSPF packet types (IP protocol 89)
1 Hello: neighbor discovery and maintenance
2 Database Description: LSDB summary
3 Link State Request: asks for missing LSAs
4 Link State Update: carries LSAs (flooding)
5 Link State Ack: acknowledges receipt
Reliable exchange: every LSA is acknowledged
Notes: Three principles: (1) every router maintains a database (LSDB) describing the topology of the autonomous system, or rather of the area; (2) every router runs exactly the same algorithm (SPF) in parallel over that database, each with itself as the root; (3) in the original specification, OSPF computed separate routes for each type of service (ToS); that was removed in RFC 2328 because it was never usefully implemented. Today service differentiation is done by QoS and traffic engineering (MPLS-TE, Segment Routing), not by the IGP. Synchronization of the LSDB between adjacent neighbors uses Database Description, Link State Request, Update and Acknowledgment packets; the exchange is reliable (every LSA is acknowledged).

## Slide 120: OSPF: protocol overview (2 of 2)
Areas
Sets of networks grouped together; an area's topology is hidden from the others
Less routing traffic, smaller LSDB, faster SPF
Area 0 (backbone) interconnects all the others
Flexible subnets (VLSM / CIDR)
Every advertised route carries its mask
Summarization configurable at area (ABR) and AS (ASBR) boundaries
Authentication
OSPFv2: null, simple password or cryptographic (MD5, RFC 2328; HMAC-SHA, RFC 5709)
OSPFv3: IPsec (RFC 4552) or Authentication Trailer (RFC 7166)
External routes
Routes from another AS or another protocol (redistribution) cross the AS transparently
Marked as external (E1/E2), with a route tag
Notes: Four more characteristics: (1) OSPF allows sets of networks to be grouped into areas, whose topology is hidden from the rest of the AS, reducing routing traffic and LSDB size; (2) it supports flexible configuration of IP subnets (VLSM and CIDR) from the start, since every route carries a mask; (3) all protocol exchanges can be authenticated: null, simple password or cryptographic (MD5 in RFC 2328; HMAC-SHA in RFC 5709); in OSPFv3 authentication uses IPsec (RFC 4552) or the Authentication Trailer (RFC 7166); (4) externally derived routes (from another AS or another protocol, via redistribution) are carried transparently throughout the AS, marked as external, with tags.

## Slide 121: OSPF topology: backbone and areas
Area 0 (backbone)
Area 1
Area 2
Area n (stub)
ABR
ABR
ABR
Every area connects to area 0 through area border routers (ABRs); inter-area traffic always crosses the backbone
Types: normal, stub (no externals), totally stubby, NSSA (a stub that injects externals, type 7 LSA)
An area that cannot reach the backbone: virtual link (temporary fix)
Notes: Area 0 (the backbone) is the center: every other area must connect directly to it through area border routers (ABRs), and traffic between two non-backbone areas always passes through area 0. When an area cannot physically connect to the backbone, a virtual link crosses a transit area; it is a temporary fix, not a design. Area types: normal, stub (no type 5 external routes; receives a default route), totally stubby (also no inter-area routes), NSSA (a stub that can still inject externals via type 7 LSAs). In 2026, with routers able to hold huge LSDBs, many enterprise networks use a single area 0; areas remain valuable in very large networks or with unstable links.

## Slide 122: OSPF router classification
Area 0 (backbone)
BB
backbone
ASBR
AS boundary
Other AS
(BGP)
Area 1
Area 2
ABR
ABR
Int
internal
Int
internal
Int
internal
Int
internal
Internal | Backbone | ABR (Area Border Router) | ASBR (AS Boundary Router)
All interfaces in a single area | At least one interface in area 0 | Interfaces in more than one area; one LSDB per area; summarizes | Injects external routes (redistribution, BGP)
Notes: Four roles, not mutually exclusive: internal router (all interfaces in the same area); backbone router (at least one interface in area 0); area border router, ABR (interfaces in more than one area, one of them the backbone; keeps one LSDB per area and summarizes between them); AS boundary router, ASBR (injects external routes, by redistribution or BGP). An ABR is always also a backbone router; an ASBR can be in any area (except stub).

## Slide 123: Network types supported by OSPF
Point-to-point
Two routers; direct adjacency, no DR/BDR
Hello 10 s, dead 40 s; multicast 224.0.0.5
Also recommended on router-to-router Ethernet links (ip ospf network point-to-point)
Broadcast multi-access (Ethernet)
Automatic neighbor discovery by multicast
Elects DR and BDR; Hello 10 s, dead 40 s
LANs, VLANs, switches between routers
Non-broadcast multi-access (NBMA)
Frame Relay, ATM, X.25 in 1999 (legacy)
Neighbors configured manually; DR elected; Hello 30 s, dead 120 s
Today: very rare (some satellite networks and multipoint tunnels)
Point-to-multipoint
Treats a cloud as a collection of point-to-point links; no DR
Hello 30 s by default; useful on hub-and-spoke tunnels (DMVPN)
'non-broadcast' variant with manual neighbors
Notes: OSPF adapts its behavior to the link type: point-to-point (two routers; direct adjacency, no DR; Hello 10 s); broadcast multi-access (Ethernet; discovers neighbors by multicast and elects DR/BDR; Hello 10 s); non-broadcast multi-access, NBMA (Frame Relay, ATM, X.25 in 1999; neighbors configured manually, DR elected, Hello 30 s); point-to-multipoint (treats the cloud as a set of p2p links). In 2026 WAN links are Ethernet or tunnels, and the recommended practice on router-to-router links over Ethernet is to configure 'ip ospf network point-to-point', eliminating the DR election and speeding up the adjacency.

## Slide 124: The Hello protocol
R1
R2
R3
Multi-access network 172.16.50.0/24
HELLO → 224.0.0.5
HELLO → 224.0.0.5
HELLO → 224.0.0.5
Hello field | Must match?
Area ID | Yes
Hello / dead intervals | Yes
Authentication (type and key) | Yes
Network mask (broadcast) | Yes
Stub / NSSA flags | Yes
Priority, router ID, DR/BDR | No (used in the election)
Timers
Broadcast and p2p: Hello 10 s, dead 40 s
NBMA and point-to-multipoint: Hello 30 s, dead 120 s
Fast detection: BFD (RFC 5880) in tens of ms, without touching the timers
On multi-access, the Hello also elects DR and BDR
Notes: OSPF routers use Hello packets to discover other routers with interfaces on the same network (neighbors) and to maintain the relationship. Hellos are sent periodically (10 s on broadcast and p2p; 30 s on NBMA) to multicast 224.0.0.5; if no Hello arrives during the dead interval (4× Hello), the neighbor is declared down. To form a neighborship, some Hello parameters must match: area ID, Hello and dead intervals, authentication type and key, network mask (on broadcast links), stub-area flags. The MTU is compared later, during the Database Description exchange. On multi-access networks the Hello also elects the designated router (DR) and the backup (BDR). With BFD (RFC 5880) failure detection drops to tens of milliseconds without lowering the OSPF timers.

## Slide 125: Neighbors and adjacencies
1
Down → Init
I received a Hello from the neighbor, but it has not listed my router ID yet.
2
2-Way
Bidirectional communication confirmed. On multi-access, DROthers stop here with each other; the DR/BDR election happens at this point.
3
ExStart → Exchange
Master/slave negotiation and exchange of Database Description (LSDB summary); MTU check.
4
Loading → Full
Link State Requests for the missing LSAs; when done, the LSDBs are synchronized: full adjacency.
Who becomes adjacent to whom
Point-to-point and virtual links: both routers, always
Multi-access: everyone with the DR and with the BDR; DROthers stay in 2-Way with each other
Adjacencies control flooding: LSAs flow only over them
'show ip ospf neighbor': FULL is the goal; 2-WAY/DROTHER is normal
Notes: Neighbors are routers that discovered each other through Hello; adjacent routers are neighbors that synchronized their LSDBs and exchange LSAs with each other. Not every pair of neighbors becomes adjacent: on point-to-point links and virtual links, the two always become adjacent; on multi-access networks, each router forms an adjacency only with the DR and the BDR, and the others (DROthers) stay in the 2-Way state with each other. Adjacencies control the distribution of protocol packets: an LSA is flooded only over adjacencies. States of the neighbor state machine: Down, Attempt (NBMA), Init, 2-Way, ExStart, Exchange, Loading, Full.

## Slide 126: Designated router (DR) and backup (BDR)
Multi-access network (Ethernet)
DR
BDR
R3
R4
R5
LSAs → 224.0.0.6
DR refloods → 224.0.0.5
Routers (n) | Without DR: n(n-1)/2 | With DR and BDR: 2(n-2)+1
5 | 10 | 7
10 | 45 | 17
20 | 190 | 37
Rules
Election: highest interface priority (0 = never a DR); tie → highest router ID
Not preemptive: a new router does not displace the current DR
The DR generates the network LSA (type 2) of the multi-access network
The BDR takes over if the DR fails; a new election only for the BDR
Tip: pin the DR with a high priority on the most capable router; avoid DRs on access routers
Notes: Every multi-access network has a designated router, elected by Hello: highest interface priority (0 = never), tie broken by the highest router ID; the election is not preemptive (a new router with a higher priority does not displace the current DR). The DR generates the network LSA (type 2) that represents the multi-access network in the LSDB and is the hub of synchronization: every router sends its LSAs to the DR/BDR (224.0.0.6) and the DR refloods them to everyone (224.0.0.5). Without a DR, n routers would need n(n-1)/2 adjacencies; with DR and BDR, 2(n-2)+1. Fewer adjacencies mean less routing traffic and a smaller LSDB (the network LSA replaces n² link descriptions).

## Slide 127: Link-state advertisements (LSAs) and the LSDB
Type | Name | Generated by | Scope | Contents
1 | Router | Every router | Area | The router's links and costs
2 | Network | DR | Area | Routers on the multi-access network
3 | Summary (network) | ABR | Area | Prefixes of other areas
4 | Summary (ASBR) | ABR | Area | How to reach the ASBR
5 | AS External | ASBR | AS (except stub) | External prefixes (E1/E2)
7 | NSSA External | ASBR in NSSA | NSSA area | Externals; the ABR converts them to type 5
8 / 9 | Link / Intra-Area-Prefix | OSPFv3 | Link / area | Link-local addresses and prefixes (v3)
Life cycle of an LSA
Flooding throughout the area over adjacencies; every LSA acknowledged (Ack)
Sequence number: the highest is the most recent
LS Age: re-sent every 30 min (LSRefreshTime); discarded at 60 min (MaxAge)
Identical LSDB on every router in the area → each runs SPF with itself as the root → intra-area routing table
'show ip ospf database' lists the LSAs by type
Notes: LSAs are flooded throughout the area, ensuring every router in the area has exactly the same topological database (LSDB), made of the LSAs from each router in the area. From the LSDB, each router computes the shortest-path tree with itself as the root; from that tree comes the intra-area routing table. Every LSA has a sequence number (to detect the most recent), an age (LS Age; re-sent every 30 min, LSRefreshTime; discarded at 60 min, MaxAge) and a checksum. Main types: 1 (router: the router's links, area scope), 2 (network: generated by the DR), 3 (network summary: generated by the ABR for routes from other areas), 4 (ASBR summary: where the ASBR is), 5 (AS external: generated by the ASBR, scope of the whole AS except stubs), 7 (NSSA external, converted to 5 by the ABR). OSPFv3 renumbers and adds types 8 (link) and 9 (intra-area prefix).

## Slide 128: Inter-area routing
Area 1
172.16.0.0/22
(4 /24 subnets)
Area 0 (backbone)
Area 2
172.16.8.0/22
ABR1
ABR2
type 3 LSA: 172.16.0.0/22, cost 20
type 3 LSA: 172.16.8.0/22, cost 15
type 3 → inside area 2
Each ABR summarizes its areas in type 3 LSAs (prefixes and costs only) and sends them over the backbone to the other ABRs
With that, every ABR computes paths to destinations outside its areas and advertises them inside its areas
Inter-area computation = distance vector over the backbone → every area must touch area 0
area range (manual summarization) reduces type 3 LSAs; stub / totally stubby areas receive only a default route from the ABR
Notes: Each ABR summarizes the topology of its attached areas in type 3 LSAs (prefixes and costs only, not the topology) and transmits them over the backbone to all other ABRs; thus every ABR computes paths to destinations outside its areas. The ABRs then advertise those paths (again as type 3) inside their areas, enabling routing to other areas. Inter-area computation is a distance vector over the backbone (hence the requirement that every area touch area 0). Manual summarization at the boundary (area range) reduces the number of type 3 LSAs; stub and totally stubby areas receive only a default route from the ABR instead of the external and inter-area routes.

## Slide 129: AS external routes
Other AS /
static routes
ASBR
ABR
R
type 5 LSA: 203.0.113.0/24 (E2, cost 20)
type 5 (flooded)
type 4 LSA: ASBR is at cost 10
Type | Metric | Use
E2 (default) | External cost only (the same across the AS); internal cost only breaks ties | 'Far away' routes, when the internal cost is irrelevant
E1 | External cost + internal cost to the ASBR | Several ASBRs advertising the same prefix: optimal choice
Rules
The ASBR generates type 5; flooded throughout the AS, except stub areas
The ABR generates type 4 to say where the ASBR is
In an NSSA: type 7, translated to 5 by the ABR
Redistribution into OSPF: 'redistribute bgp 65000 subnets metric-type 1'
Notes: Routers that have information about other ASs (or about static routes and other protocols, redistributed) are ASBRs and flood that information throughout the AS in type 5 LSAs. To use an external route, every router needs to know how to reach the ASBR that advertised it; that is why the ABRs generate type 4 LSAs describing the location of the ASBRs. Two kinds of external metric: E1 (external cost + internal cost to the ASBR; compares paths fully) and E2 (default; external cost only, the same across the AS; tie broken by the internal cost). Stub areas do not receive type 5 and use the ABR's default route; NSSAs use type 7, converted to 5 by the ABR.

## Slide 130: OSPFv3 and IS-IS: the link-state IGPs in 2026
UPDATED
OSPFv3 (RFC 5340, 2008)
Runs per link, with a link-local next hop (fe80::/10); transport ff02::5 and ff02::6
Type 1 and 2 LSAs carry topology only; prefixes go in type 8 (link) and type 9 (intra-area prefix) LSAs
Several instances per link (Instance ID)
Authentication through IPsec (RFC 4552) or the Authentication Trailer (RFC 7166)
Address families (RFC 5838): IPv4 and IPv6 in a single protocol, separate instances per AF
IS-IS (ISO 10589; RFC 1195; RFC 5308)
Same algorithm (Dijkstra), encapsulated directly at Layer 2: it does not need IP to form adjacencies
Two levels: L1 (intra-area) and L2 (backbone); L1/L2 routers form the boundary
Identification by NSAP/NET; extensible through TLVs: IPv4, IPv6, multi-topology, TE, Segment Routing
Preferred by large providers and in fabrics; base of SR-MPLS and SRv6
Same concepts of LSP (the LSA equivalent), flooding, DIS (the DR equivalent, preemptive)
Notes: New slide. OSPFv3 (RFC 5340) adapts OSPF to IPv6: it runs per link (not per subnet) using link-local addresses as next hop, removes addressing from the router and network LSAs (which now describe topology only) and creates type 8 (link) and type 9 (intra-area prefix) LSAs for prefixes; with address families (RFC 5838) it can also route IPv4, allowing a single protocol in dual stack. IS-IS (ISO 10589; RFC 1195 for IP; RFC 5308 for IPv6) offers the same algorithm with direct Layer 2 encapsulation (no IP), two hierarchical levels (L1 intra-area, L2 backbone), NSAP identifiers and TLV extensibility, which made it the preferred IGP of large providers and the base of Segment Routing (SR-MPLS and SRv6).

## Slide 131: Interior and exterior routing protocols
AS 100
R1
R2
R3
R4
RB
border (BGP)
Interior (IGP): OSPF, IS-IS, EIGRP, RIP (IGRP: legacy)
Internet
(other ASs)
P1
P2
eBGP
Exterior (EGP): BGP-4 (original EGP: legacy)
 | Interior (IGP) | Exterior (BGP)
Goal | Best path by metric inside the AS | Reachability between ASs according to business policies
Scale | Hundreds to thousands of routers | The whole Internet: ≈ 1 million IPv4 prefixes, > 200,000 IPv6
Notes: Inside an autonomous system (AS 100 in the diagram) run the interior protocols (IGPs): RIP, EIGRP, OSPF, IS-IS, which optimize paths by metric. Between autonomous systems, on the Internet, runs the exterior protocol (EGP, in the generic sense): today exclusively BGP-4, which decides by policy (who is a customer, who is a provider, who is a peer) and not just by metric. The original listed IGRP among the interior ones and EGP among the exterior ones; both are legacy.

## Slide 132: Exterior Gateway Protocol (EGP): the predecessor
LEGACY
Core (ARPANET)
C1
C2
C3
AS 1
AS 2
AS 3
AS n
G
G
G
G
Designed for a very specific topology: a core system (ARPANET) with the ASs hanging off it, each AS through a single router
No multiple paths from an AS to the core; no loop detection (the topology had to be a tree); reachability only, no metric
Unworkable once the Internet lost its single core (NSFNET and commercial providers); replaced by BGP by the mid-1990s
Notes: EGP (RFC 904, 1984) was designed for a very specific topology: it assumed a 'core' system of the Internet (the ARPANET) to which the various ASs attached, each through a single router, forming a tree. It did not allow multiple paths from an AS to the core, did not detect loops (which is why the topology had to be a tree) and only reported reachability, with no comparable metric. When the Internet stopped having a single core (NSFNET, commercial providers, early 1990s), EGP became unworkable and was replaced by BGP; in 1999 the slide said 'BGP is slowly replacing EGP'; the replacement was complete by the mid-1990s. The acronym EGP survives only as a generic term for 'exterior protocol'.

## Slide 133: BGP-4: the routing protocol of the Internet
UPDATED
Created to overcome EGP's limitations as the Internet grew; BGP-4 since 1994 (RFC 1654 → RFC 1771 → RFC 4271, 2006)
Detects loops: the AS_PATH lists the ASs traversed; a route that already contains my AS is rejected
Policy-oriented path vector; explicitly configured TCP 179 sessions (no automatic discovery)
eBGP between different ASs (AD 20); iBGP inside the AS (AD 200), in full mesh or with route reflectors (RFC 4456)
MP-BGP (RFC 4760): IPv6, VPNv4/VPNv6 (MPLS L3VPN), EVPN; 32-bit ASNs (RFC 6793)
Also inside data centers: BGP as the IGP of leaf-spine fabrics (RFC 7938)
AS 64500
AS 64501
AS 64502
A
B
C
eBGP
A advertises 203.0.113.0/24 with AS_PATH 64500; B re-advertises it to C with AS_PATH 64501 64500; C would never accept back a route with 64502 in the path.
Global table 2026: ≈ 1 million IPv4 prefixes; > 200,000 IPv6 (bgp.potaroo.net).
Notes: BGP was developed to overcome EGP's limitations as the Internet grew (BGP-1 in 1989, RFC 1105; BGP-4 in 1994, RFC 1654; current version RFC 4271, 2006). Unlike EGP, it detects loops: every advertisement carries the list of ASs traversed (AS_PATH) and a router rejects any route whose path already contains its own AS. It is a path-vector, policy-oriented protocol that runs over TCP (port 179) with explicitly configured sessions between peers: eBGP between different ASs (normally direct neighbors) and iBGP inside the same AS (full mesh or route reflectors, RFC 4456). With multiprotocol extensions (MP-BGP, RFC 4760) it carries IPv6, MPLS VPNs, EVPN and much more; with 32-bit ASNs (RFC 6793) it solved the exhaustion of AS numbers. In 2026 the global table has about 1 million IPv4 prefixes and more than 200,000 IPv6 prefixes.

## Slide 134: BGP-4: attributes and best-path selection
Attribute | Category | Purpose
ORIGIN | Mandatory | How the route entered BGP (IGP, EGP, incomplete)
AS_PATH | Mandatory | List of ASs; loop detection; policy by prepending
NEXT_HOP | Mandatory | Next-hop IP (eBGP: the peer; iBGP: unchanged)
LOCAL_PREF | Discretionary | Exit preference inside the AS (highest wins)
MED | Optional non-trans. | Suggests an entry point to the neighbor (lowest wins)
COMMUNITY | Optional transitive | Tags for policy (RFC 1997, 8092)
AGGREGATOR / ATOMIC_AGG. | Optional / discr. | Route aggregation information
Selection order (Cisco)
1. Highest weight (local, Cisco) 2. Highest LOCAL_PREF
3. Locally originated route 4. Shortest AS_PATH
5. Lowest ORIGIN (IGP < EGP < incomplete) 6. Lowest MED
7. eBGP over iBGP 8. Lowest IGP metric to the NEXT_HOP
9. Oldest route 10. Lowest router ID / peer address
Routing security
Prefix and AS_PATH filters, per-peer prefix limits, RPKI/ROV (RFC 6811), MANRS.
Notes: Every BGP route carries attributes: well-known mandatory (ORIGIN, AS_PATH, NEXT_HOP), well-known discretionary (LOCAL_PREF, ATOMIC_AGGREGATE), optional transitive (AGGREGATOR, COMMUNITY) and optional non-transitive (MED, ORIGINATOR_ID, CLUSTER_LIST). Policy is implemented by manipulating attributes: LOCAL_PREF to prefer an exit inside the AS, AS_PATH prepending to discourage an entry, MED to suggest an entry point to the neighbor, communities to tag routes (RFC 1997, large communities RFC 8092). The selection order shown is Cisco's (RFC 4271 defines it from LOCAL_PREF on); other vendors differ in details (Junos has no 'weight'). Security: prefix and AS_PATH filters, prefix limits, RPKI/ROV (RFC 6811) to validate the origin; BGPsec exists but is little deployed.

## Slide 135: Controlling IP access
MODULE 2 | PART 5
Access control lists (ACLs): how routers filter traffic, classic standard-ACL examples and the evolution toward stateful firewalls
Notes: The ACL examples use the classic Cisco IOS syntax, being the most widespread and the same as the original; the concepts (wildcard mask, implicit deny, direction, placement) apply to any vendor.

## Slide 136: ACLs in the router's processing flow
Control plane
Routing table / FIB
ARP cache / adjacencies
ACLs (ordered rules)
Queues / QoS
Data plane
Ingress
interface
Inbound
ACL (in)
Routing
(FIB lookup)
Outbound
ACL (out)
Egress
interface
deny → drop
Rules evaluated in order; the first match decides; implicit deny at the end
Applied per interface and direction (in: before routing; out: after); a denied packet is dropped (optionally with ICMP)
Uses beyond filtering: selecting traffic for NAT, QoS, VPN, route-maps, management access
Notes: An access control list is an ordered sequence of 'permit' or 'deny' rules evaluated top to bottom; the first match decides, and at the end there is an implicit deny of everything. Applied to an interface in a direction (in or out), the ACL is consulted before routing (inbound) or after it (outbound), silently discarding (or with ICMP 'administratively prohibited') the denied packets. ACLs also serve purposes other than filtering: selecting traffic for NAT, QoS, VPN, route-maps and management access (vty).

## Slide 137: Standard ACL example (1 of 3): permit only the internal network
External network: not 172.16.0.0
R1
S0
E0
E1
172.16.20.0/24
172.16.10.0/24
H1
172.16.20.9
H2
172.16.10.9
H3
172.16.10.254
access-list 1 permit 172.16.0.0 0.0.255.255
! (implicit: access-list 1 deny 0.0.0.0 255.255.255.255)
interface Ethernet0
ip access-group 1 out
interface Ethernet1
ip access-group 1 out
Reading
Wildcard 0.0.255.255 = 'the first two octets must be 172.16'
Traffic from outside (via S0) to the LANs: denied outbound on E0/E1
Traffic between the LANs: permitted (source 172.16.x.x)
Notes: Standard ACLs (numbered 1 to 99, or named) filter by source IP address only. The wildcard mask is the inverse of the subnet mask: 0 = the bit must match, 1 = don't care; 0.0.255.255 matches any address starting with 172.16. List 1 permits traffic sourced in 172.16.0.0/16 and, through the implicit deny, drops everything else. Applied outbound on E0 and E1, it prevents traffic coming from the external network (through S0) from reaching the LANs, while traffic between the two internal LANs still passes. 2026 note: 'ip access-group ... out' still exists; to protect LANs from external traffic, the natural place is inbound on S0 (a single ACL) or a stateful firewall.

## Slide 138: Standard ACL example (2 of 3): deny a specific host
External network: not 172.16.0.0
R1
S0
E0
E1
172.16.20.0/24
172.16.10.0/24
H1
172.16.20.9
H2
172.16.10.9
H3
172.16.10.254
H3 → 172.16.20.0: blocked on E0 out
access-list 1 deny 172.16.10.254 0.0.0.0
access-list 1 permit 0.0.0.0 255.255.255.255
! modern equivalent:
! access-list 1 deny host 172.16.10.254
! access-list 1 permit any
interface Ethernet0
ip access-group 1 out
Reading
Wildcard 0.0.0.0 = match all 32 bits (a single host)
Order matters: a 'permit any' before the 'deny' would void the rule
H3 still reaches the Internet and its own LAN
Notes: Now ACL 1 denies host 172.16.10.254 (wildcard 0.0.0.0: every bit must match; 'host 172.16.10.254' is the shorthand) and permits everything else (0.0.0.0 255.255.255.255, or 'any'). Applied outbound on E0, it stops that host from reaching network 172.16.20.0/24, but not from talking to the external network or to its own LAN. Order matters: if the permit any came first, the deny would never be evaluated.

## Slide 139: Standard ACL example (3 of 3): deny a subnet
External network: not 172.16.0.0
R1
S0
E0
E1
172.16.20.0/24
172.16.10.0/24
H1
172.16.20.9
H2
172.16.10.9
H3
172.16.10.254
172.16.10.0/24 → LAN 20: blocked
access-list 1 deny 172.16.10.0 0.0.0.255
access-list 1 permit 0.0.0.0 255.255.255.255
interface Ethernet0
ip access-group 1 out
show access-lists 1 ! per-rule counters
Reading
Wildcard 0.0.0.255 = 'the first three octets must be 172.16.10'
One direction only: LAN 20 still reaches LAN 10 (the reply to traffic initiated by LAN 20 passes)
To filter by protocol and port: extended ACL
Notes: Variant: deny the whole subnet 172.16.10.0/24 (wildcard 0.0.0.255) and permit the rest, applied outbound on E0. No host on LAN 10 reaches LAN 20; LAN 20 and the external network still reach LAN 10 (the ACL looks only at the source and only outbound on E0). It is a classic example of the limitation of standard ACLs: to allow only HTTPS from LAN 10 to a server on LAN 20 you would need an extended ACL.

## Slide 140: ACLs in 2026: extended, named, IPv6 and stateful firewalls
UPDATED
Extended ACL
Protocol, source, destination, ports, flags (established)
Place close to the source; standard ACLs close to the destination
Named: editing by sequence number; remarks
ip access-list extended LAN10-to-WEB
remark permit HTTPS from LAN 10 to the server
permit tcp 172.16.10.0 0.0.0.255 host 172.16.20.80 eq 443
permit icmp 172.16.10.0 0.0.0.255 172.16.20.0 0.0.0.255 echo
deny ip any any log
interface GigabitEthernet0/1
ip access-group LAN10-to-WEB in
IPv6
ipv6 access-list NAME / permit tcp 2001:db8:10::/64 host 2001:db8:20::80 eq 443
Never block ICMPv6 indiscriminately: ND and PMTUD depend on it (RFC 4890)
Beyond ACLs
ACLs are stateless: they do not know whether a packet is a reply to a legitimate connection
Stateful firewall / NGFW: tracks the 5-tuple and TCP state; application inspection
Zero trust: microsegmentation by identity; the principle (ordered rules, implicit deny) continues
Notes: Extended ACLs (100 to 199 or named) filter by protocol, source, destination and ports, and should be placed close to the source (to drop early); standard ACLs, source only, go close to the destination (to avoid blocking too much). Named ACLs allow editing rules by sequence number. In IPv6, 'ipv6 access-list' has a similar syntax with prefixes; be careful not to block ICMPv6 (ND, PMTUD), without which IPv6 does not work (RFC 4890). The fundamental limitation of ACLs: they are stateless; to allow replies to connections initiated from inside without opening everything, stateful inspection is used (zone-based firewall, NGFW), which tracks the 5-tuple and the TCP state. In 'zero trust' architectures, filtering moves to microsegmentation by workload identity, but the principle of ordered rules with an implicit deny remains.

## Slide 141: Additional IP routing topics
MODULE 2 | PART 6
Broadcast handling and DHCP relay, directed broadcast, secondary addresses and unnumbered interfaces
Notes: Four operational topics from the original (slides 157 to 163), with updated Cisco commands and equivalents on other platforms.

## Slide 142: IP broadcast handling: the DHCP problem
Cli
no address
(0.0.0.0)
172.16.20.0/24
R1
E0: 172.16.20.1
R2
172.16.75.0/24
DHCP
server 172.16.75.20
DHCP Discover: 0.0.0.0 → 255.255.255.255 (UDP 68 → 67)
?
What does the router do with the DHCP client's broadcast (formerly BootP)? By default, it drops it: routers do not forward 255.255.255.255
Without a relay, the client never gets an address (unless there is a server per subnet)
Solution: DHCP relay (RFC 1542 / RFC 2131): the router forwards the request as unicast to the server, filling giaddr with its address on the client's subnet
Option 82 (RFC 3046): circuit/port identification for policies on the server
Notes: Question from the original: what does the router do with a BootP request (today, a DHCP Discover) sent in broadcast by a station with no address, if the server is on another subnet? By default, nothing: routers do not forward broadcasts (255.255.255.255), and that is one of the reasons they exist. Without intervention, the client would never get an address. Solutions: a DHCP server per subnet (impractical) or configuring the router to forward certain broadcasts as unicast to the server: the relay agent (RFC 1542 for BOOTP; RFC 2131 for DHCP), called 'ip helper-address' on Cisco. The relay rewrites the destination to the server's IP, puts its own address in the giaddr field (so the server knows which subnet to pick the address from) and may add option 82 (RFC 3046) with circuit information.

## Slide 143: DHCP relay and directed broadcast: configuration
Cli
R1
ip helper-address
R2
DHCP
172.16.75.20
broadcast
unicast 172.16.20.1 → 172.16.75.20 (giaddr = 172.16.20.1)
! Cisco IOS: relay on the clients' interface
interface GigabitEthernet0/0
ip address 172.16.20.1 255.255.255.0
ip helper-address 172.16.75.20
! list of forwarded UDP ports (default: 37 49 53 67 68 69 137 138)
ip forward-protocol udp 67
no ip forward-protocol udp 137
Platform | DHCP relay
Linux | isc-dhcp-relay / dhcrelay -i eth0 172.16.75.20
Juniper Junos | forwarding-options dhcp-relay server-group ...
L3 switch (several) | ip dhcp relay address 172.16.75.20 (per VLAN/SVI)
Directed broadcast: RFC 2644 (1999) requires routers NOT to forward it by default (smurf attack); 'no ip directed-broadcast' has been the IOS default since 12.0.
Notes: On Cisco, 'ip helper-address' on the interface facing the clients does the relay; by default it forwards UDP broadcasts on ports 37 (time), 49 (TACACS), 53 (DNS), 67/68 (DHCP/BOOTP), 69 (TFTP), 137 and 138 (NetBIOS); 'ip forward-protocol udp' adjusts the list. The global 'ip forward-protocol' command from the original still exists. Equivalents: Linux with isc-dhcp-relay or dhcrelay; Junos with forwarding-options dhcp-relay; L3 switches with 'ip dhcp relay'. As for directed broadcast (e.g., 172.16.20.255 coming from outside), RFC 2644 (BCP 34, 1999) ruled that routers must NOT forward it by default, in response to 'smurf' attacks; IOS has disabled 'ip directed-broadcast' since release 12.0 and practically no legitimate use (remote Wake-on-LAN) justifies turning it back on without an ACL.

## Slide 144: Secondary addresses
R1
E0
A single physical link (VLAN 25)
E0: 172.16.25.1/24 (primary)
172.16.27.1/24 (secondary)
H
172.16.25.10
H
172.16.25.11
H
172.16.27.10
H
172.16.27.11
Traffic 172.16.25.x ↔ 172.16.27.x goes through the router, even on the same wire
interface GigabitEthernet0/0
ip address 172.16.25.1 255.255.255.0
ip address 172.16.27.1 255.255.255.0 secondary
When to use it (and when not)
Hosts exhausted on the subnet with no immediate renumbering; bridged → routed migration
Caveats: IGP adjacencies only over the primary; DHCP relay uses the primary as giaddr
Better in 2026: a new VLAN + new subnet (or IPv6, where several addresses per interface are the rule)
Legacy: the original configured 'interface tokenring 0' with 134.141.25.1 and 134.141.27.1 secondary.
Notes: A secondary address assigns the same interface a second (or third...) IP address, on another subnet. Use cases from the original, still valid: (1) the subnet ran out of host numbers and immediate renumbering is not possible; (2) migration from a flat (bridged) network to a routed one, with several subnets coexisting on the same link during the transition. Limitations: hosts on the two subnets only talk through the router (even though they share the wire); routing protocols treat secondaries specially (OSPF advertises them but does not form adjacencies over them; EIGRP/RIP do not always send updates from secondaries); DHCP relay uses the primary as giaddr. In 2026 the right alternative is almost always a new VLAN with its own subnet; secondaries are left for short migrations. In IPv6 multiple addresses per interface are the norm, not the exception.

## Slide 145: Unnumbered interfaces (IP unnumbered)
R1
Loopback0: 172.16.255.1/32
R2
Loopback0: 172.16.255.2/32
point-to-point link with no subnet of its own
Serial0/0: ip unnumbered Loopback0
Serial0/0: ip unnumbered Loopback0
interface Loopback0
ip address 172.16.255.1 255.255.255.255
interface Serial0/0
ip unnumbered Loopback0
! BGP unnumbered (FRRouting / Cumulus): no IPv4 on the link
router bgp 65001
neighbor swp1 interface remote-as external
! session over IPv6 link-local; IPv4 via RFC 8950
Rules and limitations
The lending interface must have an IP (use a loopback); you cannot ping the unnumbered interface nor point a static route at its 'IP'; saves a /30 per link (today: /31 or unnumbered)
Notes: 'ip unnumbered' enables IP processing on a point-to-point interface without assigning it a subnet of its own: the interface 'borrows' the address of another interface on the same router (today almost always a /32 loopback), which must have an IP address. In 1999 the goal was saving subnets on serial links (every /30 spent 4 addresses). The concept came back strongly in 2026 in data center fabrics: 'BGP unnumbered' establishes eBGP sessions over the IPv6 link-local addresses of the links (RFC 5549, now RFC 8950), without configuring any IPv4 link address, with automatic neighbor discovery through RA; OSPF and IS-IS also operate on unnumbered links. Classic limitations: you cannot ping the interface directly nor use static routes with a next hop on it (the interface is used as the exit).

## Slide 146: IPv6: from 'IPng' to the dominant protocol
MODULE 2 | PART 7
Motivation, differences from IPv4, header and extension headers, addressing, neighbor discovery and autoconfiguration, routing, flows, security and transition
Notes: In 1999 this topic was called 'IPng or IPv6' and was based on drafts (RFC 1883, from 1995). The 2026 edition follows RFC 8200 (2017, Internet Standard) and reflects an Internet where more than half of the accesses to Google already use IPv6.

## Slide 147: Why IPv6: from 'IPng' (1995) to RFC 8200 (2017)
UPDATED
Year | Milestone
1992 to 1994 | IETF studies successors to IPv4 (IPng); CIDR and private addresses buy time
1995 | RFC 1752 selects the IPng; RFC 1883 publishes IPv6 (version 6; version 5 had been used by ST)
1998 | RFC 2460 (Draft Standard); 6bone test network
2008 to 2012 | Google, Facebook and others turn on IPv6; World IPv6 Launch (2012)
2011 | IANA hands out the last IPv4 /8 blocks (February 3)
2017 | RFC 8200: IPv6 becomes an Internet Standard (STD 86)
2020 | LACNIC exhausts its final IPv4 phase (August)
2026 | > 50% of accesses to Google over IPv6 (Mar 28); Brazil ≈ 59% IPv6-capable (APNIC, Oct 5)
The problem
32 bits = 4.29 billion addresses, many wasted by the classes
NAT and CGNAT break the end-to-end model and raise operating costs
The global routing table keeps growing
The answer
128 bits: 3.4 × 10^38 addresses (≈ 6.7 × 10^23 per m² of the Earth's surface)
Simpler header, autoconfiguration, native multicast, no broadcast
Transition still under way: dual stack, tunnels and translation (NAT64)
Notes: Why IPng? The notes of the 1999 original asked exactly that. The answer was already the exhaustion of the 32-bit IPv4 space (4.3 billion addresses, many of them wasted by the classes) and the growth of the routing table. In 1995 the IETF chose the SIPP proposal as 'IP next generation' (RFC 1752), published IPv6 in RFC 1883 (December 1995), revised it in RFC 2460 (1998) and elevated it to Internet Standard in RFC 8200 (July 2017, STD 86). The predicted exhaustion happened: IANA handed out its last /8 blocks on February 3, 2011; LACNIC exhausted its final phase in August 2020. Adoption, slow for 15 years, accelerated with mobile networks and the large platforms: on March 28, 2026 native IPv6 access to Google exceeded 50% for the first time (50.10%, Internet Society Pulse); in Brazil, APNIC Labs measured about 59% of users as IPv6-capable on October 5, 2026.

## Slide 148: Main differences between IPv6 and IPv4
Aspect | IPv4 (RFC 791) | IPv6 (RFC 8200)
Address | 32 bits; 4.3 × 10^9 | 128 bits; 3.4 × 10^38; allocation hierarchy; native anycast
Header | 20 to 60 bytes, 13 fields, options in the header, checksum | Fixed 40 bytes, 8 fields, no checksum; options in extension headers
Fragmentation | In routers and at the source | Only at the source (Path MTU Discovery); minimum MTU 1,280 bytes
Address resolution | ARP (broadcast) | Neighbor Discovery, ICMPv6 (solicited-node multicast)
Broadcast | Yes (limited and directed) | Does not exist: multicast ff02::1 (all nodes) plays the role
Configuration | Manual or DHCP | SLAAC (RA), DHCPv6 (stateful or stateless), manual; several addresses per interface
QoS / flows | ToS → DSCP/ECN | Traffic Class (DSCP/ECN) + 20-bit Flow Label
Security | IPsec optional (added later) | IPsec built in through extension headers (AH, ESP); support recommended (SHOULD), not mandatory (RFC 8504)
NAT | Ubiquitous (scarcity) | Unnecessary: end-to-end model; stateful firewall instead of NAT
Notes: The original listed six groups of changes, which remain the canonical summary (RFC 8200, section 1): (1) expanded addressing and routing capabilities: 128 bits, allocation hierarchy, scalable multicast with scopes; (2) a new address type, anycast, which delivers to the 'nearest' member of a group; (3) header format simplification: fields removed or made optional, fixed 40-byte header; (4) improved support for options, through chained extension headers; (5) flow labeling capability (flow label) for differentiated handling; (6) built-in authentication and privacy (IPsec). Add for 2026: no fragmentation in routers (the source uses PMTUD), no header checksum, ND instead of ARP and broadcast, autoconfiguration (SLAAC) and several addresses per interface as the rule.

## Slide 149: The IPv6 header
bit 0
bit 31
Version (4) = 6
Traffic class (8)
Flow label (20)
Payload length (16)
Next header (8)
Hop limit (8)
Source address (128 bits = 4 words)
Destination address (128 bits = 4 words)
Fixed 40 bytes; no IHL, no checksum, no fragmentation fields, no options in the header
Field | Function
Traffic class | DSCP + ECN (RFC 2474, 3168)
Flow label | Identifies flows; ECMP hash (RFC 6437/6438)
Payload length | Bytes after the 40-byte header
Next header | 6 TCP, 17 UDP, 58 ICMPv6, 0/43/44/50/51/60 extensions
Hop limit | Former TTL; 0 → discard + ICMPv6
History: RFC 1883 (1995) had a 4-bit 'Prio' and a 24-bit Flow Label, as in the 1999 slide; RFC 2460 (1998) settled on 8 + 20 bits.
Notes: Eight fields, fixed 40 bytes: Version (4 bits, = 6); Traffic Class (8 bits: DSCP + ECN, as in IPv4); Flow Label (20 bits); Payload Length (16 bits, bytes after the fixed header, including extensions; jumbograms through an option); Next Header (8 bits, same values as the IPv4 Protocol field, plus those of the extensions); Hop Limit (8 bits, the renamed TTL, without the 'time' meaning); 128-bit source and destination addresses. Note what disappeared compared with IPv4: IHL (the header is fixed), Identification/Flags/Offset (moved to the fragmentation extension), Checksum (the link and transport layers already verify) and Options (extensions). Update: the 1999 slide showed a 4-bit 'Prio' and a 24-bit 'Flow Label', the RFC 1883 format; RFC 2460 changed it to an 8-bit Traffic Class and a 20-bit Flow Label, kept in RFC 8200.

## Slide 150: Extension headers
IPv6 header
Next = 0
Hop-by-Hop (0)
Next = 60
Dest. Options (60)
Next = 43
Routing (43)
Next = 44
Fragment (44)
Next = 51
AH (51)
Next = 50
ESP (50)
Next = 60
Dest. Options (60)
Next = 6
TCP (6)
+ data
Extension | Value | Who processes it / use
Hop-by-Hop Options | 0 | Every router; jumbograms, Router Alert (MLD, RSVP)
Destination Options | 60 | Destination (and intermediate destinations if before Routing); Mobile IPv6
Routing | 43 | Type 0 deprecated (RFC 5095); type 2 MIPv6; type 4 SRv6 (RFC 8754)
Fragment | 44 | Only the source fragments; reassembly at the destination
AH / ESP | 51 / 50 | IPsec: authentication; confidentiality + integrity
No next header | 59 | Nothing follows
Rules (RFC 8200)
Recommended order: the chain above; each extension at most once (Dest. Options up to twice)
Routers do not insert or remove extension headers in transit
Only Hop-by-Hop is examined by every hop
In practice: many networks drop packets with extension headers (RFC 7872); use sparingly
Notes: The IPv4 options became extension headers chained through the Next Header field and processed only by whoever needs them: Hop-by-Hop (0; the only one examined by every router; jumbograms, Router Alert), Destination Options (60; examined by the destination, or by intermediate destinations if it comes before Routing), Routing (43; type 0 was deprecated for security reasons, RFC 5095; type 2 in Mobile IPv6; type 4 is the Segment Routing Header of SRv6, RFC 8754), Fragment (44; only the source fragments), AH (51) and ESP (50) from IPsec. The recommended order is the one shown. RFC 8200 also established that routers must not insert or remove extension headers in transit. In practice, packets with many extension headers are frequently dropped by firewalls and by forwarding hardware (RFC 7872), which limits the use of extension headers to the essential.

## Slide 151: IPv6 addressing: 128 bits, three types, no broadcast
Notation (RFC 4291, canonical form RFC 5952)
2001:0db8:0000:0000:0000:0000:0000:0001 → 2001:db8:0:0:0:0:0:1 → 2001:db8::1
Eight 16-bit groups in hexadecimal; leading zeros omitted; a single run of zeros becomes '::'; lowercase; CIDR prefix (/64)
Unicast
Identifies one interface
Global, unique local (ULA), link-local
Anycast
Same address on several interfaces; delivered to the 'nearest' one (IGP/BGP metric)
Syntactically identical to unicast; DNS root, CDNs
Multicast
ff00::/8; delivered to all members of the group
Replaces broadcast: ff02::1 = all nodes on the link
Typical structure of a global unicast address (GUA)
Global routing prefix (48 bits): 2001:db8:abcd
Subnet ID (16): 0010
Interface ID (64 bits): 0000:0000:0000:0001 (or EUI-64 / random)
Subnets are /64 by convention (SLAAC requires it); organizations receive a /48 (65,536 subnets) or a /56; ISPs, a /32 or larger. 2^128 ≈ 3.4 × 10^38 addresses.
Notes: 128-bit addresses written as eight groups of four hexadecimal digits separated by colons; leading zeros in each group may be omitted and a single run of all-zero groups may be replaced by '::' (RFC 4291; canonical form in lowercase with the longest run of zeros compressed, RFC 5952). The prefix uses CIDR notation (/64). Three types: unicast (one interface), anycast (the nearest member of a set; syntactically identical to unicast) and multicast (all members of the group); there is no broadcast. The total of 2^128 addresses is the number the original displayed in its title: 340,282,366,920,938,463,463,374,607,431,768,211,456.

## Slide 152: IPv6 address types and scopes
Type | Prefix | Scope and use | Reference
Global unicast (GUA) | 2000::/3 | Routable on the Internet; allocated by IANA → RIR → ISP → organization (/48, /56) | RFC 4291
Unique local (ULA) | fc00::/7 (fd00::/8) | Private, not routable on the Internet; 40 random bits avoid collisions in mergers; no NAT | RFC 4193
Link-local | fe80::/10 | Automatic on every interface; ND, next hop for OSPFv3/BGP; never routed | RFC 4291
Loopback / unspecified | ::1 / :: | Equivalent to IPv4's 127.0.0.1 and 0.0.0.0 | RFC 4291
IPv4-mapped | ::ffff:0:0/96 | Represents IPv4 in dual-stack sockets (::ffff:203.0.113.5) | RFC 4291
NAT64 well-known | 64:ff9b::/96 | IPv6 → IPv4 translation (DNS64 synthesizes AAAA) | RFC 6052
Documentation | 2001:db8::/32 | Examples and courses (used in this deck) | RFC 3849
Multicast | ff00::/8 | ff02:: link, ff05:: site, ff0e:: global; ff02::1 all nodes, ff02::2 routers, ff02::1:ffxx:xxxx solicited-node | RFC 4291
'Site-local' addresses (fec0::/10), planned in the drafts of the 1990s, were deprecated by RFC 3879 (2004) and replaced by ULAs.
Notes: Reference table. Global unicast (GUA, 2000::/3) is routable on the Internet; unique local (ULA, fc00::/7, in practice fd00::/8 with 40 random bits, RFC 4193) is the equivalent of private addresses, without NAT; link-local (fe80::/10) exists automatically on every interface and is used by ND and by the routing protocols as the next hop; ::1 is the loopback and :: the unspecified address. Special addresses: IPv4-mapped (::ffff:a.b.c.d) for dual-stack sockets; 64:ff9b::/96 for NAT64; 2001:db8::/32 for documentation. Multicast ff00::/8 carries the scope in the second nibble (1 interface, 2 link, 5 site, 8 organization, e global); well-known groups: ff02::1 all nodes, ff02::2 all routers, ff02::5/6 OSPF, ff02::9 RIPng, ff02::a EIGRP, ff02::d PIM, ff02::12 VRRP, ff02::1:2 DHCPv6 agents and ff02::1:ffxx:xxxx solicited-node.

## Slide 153: Neighbor Discovery (ND) and autoconfiguration (SLAAC)
ICMPv6 message | Type | Function
Router Solicitation | 133 | Host asks for an RA at startup (ff02::2)
Router Advertisement | 134 | Prefixes, default router, MTU, M/O/A flags, RDNSS; periodic and on request
Neighbor Solicitation | 135 | Resolves an address (= ARP Request); DAD; NUD
Neighbor Advertisement | 136 | Reply (= ARP Reply); unsolicited announcement
Redirect | 137 | Router points to a better next hop on the link
1
Link-local
fe80:: + interface ID; duplicate address detection (DAD) with an NS for its own address.
2
RS → RA
Host sends an RS to ff02::2; the router replies with an RA: prefix 2001:db8:10::/64 (A flag), default router, MTU, DNS.
3
Global address
Prefix + interface ID (stable random, RFC 7217; EUI-64 in legacy systems) + temporary addresses (RFC 8981); new DAD.
4
DHCPv6 if M/O
M = 1: addresses from DHCPv6 (stateful); O = 1: options only (DNS, NTP); ff02::1:2, UDP 546/547 (RFC 9915).
Equivalences: NS/NA = ARP (but over solicited-node multicast ff02::1:ffxx:xxxx, without interrupting every host); RA = default gateway + prefix + (optionally) DNS, without DHCP; DAD prevents duplicate addresses; NUD tracks the state of each neighbor (reachable, stale, probe).
Switch protections: RA Guard (RFC 6105), DHCPv6 Guard, ND inspection; SEND (RFC 3971) exists but is rarely used.
Notes: Neighbor Discovery (RFC 4861) gathers into five ICMPv6 messages what IPv4 did with ARP, ICMP Router Discovery and Redirect: Router Solicitation (133) and Router Advertisement (134) to discover routers, prefixes, MTU and parameters; Neighbor Solicitation (135) and Neighbor Advertisement (136) to resolve addresses and verify reachability (NUD) and duplication (DAD); Redirect (137). Stateless address autoconfiguration (SLAAC, RFC 4862) lets a host, without any server, generate its link-local address, check for duplicates, receive the /64 prefix in the RA and form a global address with an interface identifier derived from the MAC (EUI-64, now discouraged for privacy reasons) or a stable random one (RFC 7217), plus temporary addresses (RFC 8981). The RA flags define the role of DHCPv6 (RFC 9915): M (stateful: addresses from DHCPv6), O (stateless: only DNS and options) and A (autoconfigurable prefix). The RA can also carry DNS servers (RDNSS, RFC 8106).

## Slide 154: IPv6 routing
IGP / EGP | IPv6 | Notes
RIP | RIPng, RFC 2080 | UDP 521, ff02::9; same limitations
OSPF | OSPFv3, RFC 5340 | Per link, link-local; AF for IPv4 (RFC 5838)
IS-IS | RFC 5308 / MT RFC 5120 | One protocol for both families; multiple topologies
EIGRP | EIGRP for IPv6, RFC 7868 | ff02::a; same DUAL and metric
BGP | MP-BGP, RFC 4760 (AFI 2) | Global IPv6 table > 200,000 prefixes; sessions over IPv6 or IPv4
Static | ipv6 route 2001:db8::/32 ... | Next hop may be link-local + interface
The 'new features' of 1999, seen from 2026
Provider selection (policy, cost): exists through BGP multihoming with PI/PA prefixes and through traffic engineering; not through IPv6 fields
Host mobility (Mobile IPv6, RFC 6275): standardized, little used; mobility was solved above (QUIC, apps) and in the mobile networks
Automatic re-addressing: works; prefixes with preferred/valid lifetimes in the RA allow renumbering (RFC 4192)
Typical practice: dual stack with OSPFv3 or IS-IS + MP-BGP; IPv6-only with NAT64 in mobile carriers and data centers
Recommendations: /64 subnets on every link (even point-to-point, with /127 optional, RFC 6164); /128 loopbacks; filter ULA and link-local at the borders; handle ICMPv6 with care (RFC 4890).
Notes: As the original anticipated, every IPv4 routing algorithm was extended to IPv6 with small changes: RIPng (RFC 2080), OSPFv3 (RFC 5340), IS-IS with multitopology (RFC 5308/5120), EIGRP for IPv6 (RFC 7868) and MP-BGP (RFC 4760, AFI 2); identical static routes; longest prefix match on prefixes of up to 128 bits. Of the 'new features' listed in 1999: policy-based provider selection exists through multihoming with BGP and provider-independent (PI) or provider-aggregatable (PA) prefixes; host mobility (Mobile IPv6, RFC 6275) was standardized but is hardly used, because mobility ended up being solved in the upper layers (QUIC, applications) and in the mobile networks; automatic re-addressing (renumbering) does work: prefixes advertised in RAs with 'preferred' and 'valid' lifetimes allow switching providers without reconfiguring hosts (RFC 4192). In 2026 practice, dual stack with OSPFv3/IS-IS internally and MP-BGP externally is the typical setup; IPv6-only networks with NAT64 are growing in mobile carriers and data centers.

## Slide 155: IPv6 flows and traffic class
Several flows active between the same source and destination; traffic without a flow carries label 0
Flow = source address + flow label ≠ 0 (20 bits), assigned pseudorandomly by the source (RFC 6437); routers do not change it
Real use: input to the ECMP / LAG hash without reading the transport header (RFC 6438), useful with extension headers or ESP
Per-flow resource reservation (RSVP/IntServ) never took off; differentiation through the Traffic Class (DSCP + ECN), as in IPv4
A
2001:db8:1::10
B
2001:db8:2::80
flow 0x3a7f1 (HTTPS)
flow 0x9c012 (video)
label 0 (no flow)
Routers doing ECMP use (source, destination, label) to pick the path: each flow always follows the same path.
Version
Traffic class: DSCP (6) + ECN (2)
Flow label (20)
Notes: There may be several active flows from a source to a destination, plus traffic not associated with any flow. A flow is identified by the combination of the source address with a nonzero flow label; packets outside any flow carry a zero label. The current specification (RFC 6437) states that the source assigns pseudorandom labels per flow (typically per transport connection) and that routers must not change them; the main practical use is as input to the ECMP and link-aggregation hash without having to read the transport headers, which is valuable when there are extension headers or encryption (RFC 6438). The original idea of reserving resources per flow (with RSVP) never took off; service differentiation is done through the Traffic Class, which carries DSCP and ECN exactly as IPv4 does.

## Slide 156: Security in IPv6
IPsec built in through extension headers
AH (51, RFC 4302): authentication and integrity, no confidentiality; little used today
ESP (50, RFC 4303): confidentiality + integrity (AES-GCM); transport and tunnel modes; IKEv2 (RFC 7296)
Mandatory? Not anymore
RFC 4294 (2006): IPv6 nodes must implement IPsec
RFC 6434 (2011) → SHOULD; kept in RFC 8504 (2019)
In practice, IPsec in IPv6 is as optional as in IPv4
Specific risks
No NAT: an explicit stateful firewall is mandatory
ND as vulnerable as ARP: rogue RA, forged NS/NA, DAD flooding
Reconnaissance by scanning is unfeasible (/64), but DNS and ND caches leak hosts
Mitigations
RA Guard (RFC 6105), DHCPv6 Guard, ND inspection, SEND (RFC 3971, rare)
Temporary addresses and stable random IDs (RFC 8981, RFC 7217)
Careful ICMPv6 filtering (RFC 4890); filter ULA/link-local at the borders; RPKI for prefixes
Notes: The two built-in options from the original are still there: the Authentication Header, AH (RFC 4302), provides authentication and integrity without confidentiality; ESP (RFC 4303) provides confidentiality and integrity (today ESP with an authenticated cipher, AES-GCM, is the standard and AH is rarely used). What changed was the status: the first IPv6 node requirements (RFC 4294) mandated IPsec; RFC 6434 (2011) downgraded it to SHOULD and RFC 8504 (2019) kept it that way. IPsec in IPv6 is as optional as in IPv4 and uses the same IKEv2 (RFC 7296). The real security of IPv6 lies elsewhere: the absence of NAT requires an explicit stateful firewall; neighbor discovery is as vulnerable as ARP (rogue RAs, forged NS/NA), mitigated by RA Guard (RFC 6105) and ND inspection in switches; privacy extensions (RFC 8981) prevent tracking by interface ID; and over-filtering ICMPv6 breaks PMTUD and ND (RFC 4890).

## Slide 157: IPv4 / IPv6 transition and coexistence
UPDATED
Dual stack (RFC 4213)
Both stacks on hosts and routers
DNS: AAAA preferred; Happy Eyeballs (RFC 8305) picks the fastest connection
Basis of today's Internet; cost: running two networks
Tunnels
IPv6 over IPv4: 6in4 (proto 41), GRE, 6rd (RFC 5969)
IPv4 over IPv6: DS-Lite (RFC 6333), MAP-T/MAP-E
Where one stack does not arrive natively; reduced MTU
Translation
NAT64 (RFC 6146) + DNS64 (RFC 6147): an IPv6-only network reaches IPv4 servers
464XLAT (RFC 6877): IPv4-only apps on IPv6-only phones
Standard at large mobile carriers
Direction in 2026: IPv6-only networks with 'IPv4 as a service' (NAT64/464XLAT), including campuses and data centers; DHCP option 108 (RFC 8925) lets hosts that do not need IPv4 turn it off.
Data: native IPv6 access to Google > 50% since March 28, 2026 (Internet Society Pulse / Google); Brazil ≈ 59% IPv6-capable (APNIC Labs, October 5, 2026). Resource in Portuguese: ipv6.br (NIC.br).
Notes: New slide. Three families of techniques: (1) dual stack (RFC 4213): hosts and routers with both stacks; DNS decides (AAAA first) and the Happy Eyeballs algorithm (RFC 8305) picks the connection that answers first; it is the basis of almost the entire current Internet; (2) tunnels: IPv6 encapsulated in IPv4 (6in4, protocol 41; GRE; 6rd, RFC 5969) or IPv4 in IPv6 (DS-Lite, RFC 6333; MAP-T/MAP-E), used where one of the stacks does not arrive natively; (3) translation: NAT64 (RFC 6146) with DNS64 (RFC 6147) lets IPv6-only networks reach IPv4 servers, and 464XLAT (RFC 6877) takes care of IPv4-only applications on IPv6-only phones, the model adopted by large mobile carriers. Direction for 2026: IPv6-only networks with IPv4 as a service (IPv4aaS), including in data centers and campuses (RFC 8925 lets DHCP tell the host 'do not use IPv4'). Brazilian resource (in Portuguese): IPv6.br from NIC.br.

## Slide 158: IP multicast
MODULE 2 | PART 8
Concept, addresses and mapping to MAC, IGMP and MLD, dense and sparse modes, multicast routing algorithms and protocols (DVMRP, MOSPF, PIM), RSVP
Notes: The original covered multicast on the basis of the MBone and DVMRP; the 2026 edition centers on PIM-SM, SSM, IGMPv3/MLDv2 and IGMP snooping, keeping DVMRP and MOSPF as history.

## Slide 159: Multicast: one sender, many receivers
Unicast
1 → 1
N copies for N receivers
Broadcast
1 → everyone on the link
Interrupts those who do not want it; does not cross routers
Multicast
1 → group (subscribers)
One copy; the network replicates at the branches
Anycast
1 → the nearest member of the group
A single receiver; DNS root, CDN
Source
1 copy
R1
R2
R3
A
B
C
D
not subscribed: no traffic
Applications in 2026
Carrier IPTV; stock market feeds
Video and signaling on campuses; service discovery (mDNS, SSDP)
Routing protocols (OSPF, EIGRP, VRRP)
Public Internet: replaced by unicast CDNs
Notes: The notes of the original recalled that most high-level protocols (TCP, UDP, ISO TP) only offer unicast transmission: a node sends to one other node at a time. To deliver the same content to N receivers, unicast requires N copies at the source; broadcast delivers to everyone, including those who do not want it, and only within the link. Multicast (RFC 1112, 1989) delivers a single copy that the network replicates only at the branching points, and only to those who subscribed to the group (a class D address). Anycast, by contrast, delivers to a single receiver, the nearest one. Applications in 2026: carrier IPTV, distribution of financial market data, videoconferencing and signaling in corporate networks, service discovery (mDNS, SSDP) and, internally, the routing protocols themselves. On the public Internet multicast never became widespread; unicast CDNs took the place of the MBone.

## Slide 160: IPv4 (and IPv6) multicast addresses
1110
Multicast group identifier (28 bits)
Class D: 224.0.0.0 to 239.255.255.255 (224.0.0.0/4)
IPv4 range | Use | Ref.
224.0.0.0/24 | Link-local control (TTL 1): .1 hosts, .2 routers, .5/.6 OSPF, .9 RIPv2, .10 EIGRP, .13 PIM, .18 VRRP, .22 IGMPv3, .251 mDNS | RFC 5771
224.0.1.0/24 | Internetwork control: 224.0.1.1 NTP, .39/.40 Auto-RP | RFC 5771
232.0.0.0/8 | Source-Specific Multicast (SSM) | RFC 4607
233.0.0.0/8 | GLOP: 233.X.Y.0/24 per 16-bit ASN | RFC 3180
239.0.0.0/8 | Administratively scoped (private): organization, site | RFC 2365
IPv6: ff00::/8
ff | flags | scope | group ID (112 bits)
Scopes: 1 interface, 2 link, 4 admin, 5 site, 8 organization, e global
ff02::1 all nodes, ff02::2 all routers, ff02::5/6 OSPFv3, ff02::9 RIPng, ff02::a EIGRP, ff02::d PIM, ff02::12 VRRP, ff02::1:2 DHCPv6
ff02::1:ffxx:xxxx solicited-node (ND)
ff3x::/32 SSM; ff05::/16 site; ff0e::/16 global
Registry: IANA IPv6 Multicast Address Space Registry
Notes: A class D address (1110 + 28 bits of group identifier) designates a multicast group: 224.0.0.0 to 239.255.255.255. IANA reserves ranges: 224.0.0.0/24 (link-local control, TTL 1, never forwarded: 224.0.0.1 all hosts, .2 all routers, .5 and .6 OSPF, .9 RIPv2, .10 EIGRP, .13 PIM, .18 VRRP, .22 IGMPv3, .251 mDNS); 224.0.1.0/24 (internetwork control: 224.0.1.1 NTP, .39 and .40 Auto-RP); 232.0.0.0/8 (SSM, RFC 4607); 233.0.0.0/8 (GLOP, derived from the ASN, RFC 3180); 239.0.0.0/8 (administratively scoped, RFC 2365, the '10.0.0.0/8 of multicast'). In IPv6, ff00::/8 with flags and scope in the second byte: ff02::1 all nodes, ff02::2 routers, ff02::5/6 OSPF, ff02::9 RIPng, ff02::a EIGRP, ff02::d PIM, ff02::12 VRRP, ff05::/16 site scope, ff3x::/32 SSM. Official registry: RFC 5771 and the IANA Multicast Address Space Registry.

## Slide 161: Mapping IP multicast addresses to MAC addresses
IPv4 (RFC 1112): 239.1.1.1 → 01-00-5E-01-01-01
IP address
(class D)
1110
11110 (5 bits dropped)
00000001 00000001 00000001 (23 bits copied)
MAC address
(48 bits)
00000001 00000000 01011110 (01-00-5E)
0
00000001 00000001 00000001
01-00-5E-01-01-01: IANA OUI (01-00-5E) + bit 0 + 23 bits of the group
32-to-1 ambiguity
5 bits of the group do not fit in the MAC: 2^5 = 32 groups share the same MAC
224.1.1.1, 224.129.1.1, 225.1.1.1 ... 239.129.1.1 → all 01-00-5E-01-01-01
The NIC accepts; IP discards the groups not joined (CPU cost)
IPv6 (RFC 2464)
33-33 + the 32 least significant bits of the group
ff02::1 → 33-33-00-00-00-01; ff02::1:ff12:3456 (solicited-node) → 33-33-ff-12-34-56
Switches with MLD snooping filter per group
Notes: So that an Ethernet NIC can filter the groups of interest in hardware, the IP multicast address is mapped to a multicast MAC deterministically (RFC 1112): the 23 least significant bits of the group address are copied into the 23 least significant bits of the MAC 01-00-5E-00-00-00 (the IANA block; bit 24 is always 0). Since the group has 28 bits and only 23 are used, 5 bits are lost: 32 different groups share the same MAC (224.1.1.1, 224.129.1.1, 225.1.1.1, ..., 239.129.1.1 → 01-00-5E-01-01-01), and it is up to IP to filter what the NIC let through. In IPv6 the mapping uses 33-33 followed by the 32 least significant bits of the group (RFC 2464). Switches with IGMP/MLD snooping use these MACs (or rather, the IP groups) to forward multicast only to the ports with members.

## Slide 162: IGMP and MLD: hosts say what they want to receive
Version | RFC | What's new
IGMPv1 | 1112 (1989) | Query and Report; leave by timeout
IGMPv2 | 2236 (1997) | Leave; group-specific query; querier election (lowest IP); 224.0.0.2
IGMPv3 | 3376 (2002) | INCLUDE/EXCLUDE source filters (SSM); reports to 224.0.0.22
MLDv1 | 2710 (1999) | IGMPv2 for IPv6, over ICMPv6 (types 130 to 132)
MLDv2 | 3810 (2004) | IGMPv3 for IPv6; reports to ff02::16 (type 143)
R1
querier
H1
H2
Query → 224.0.0.1 (125 s)
Report: group 239.1.1.1
IGMP / MLD snooping in switches (RFC 4541)
The switch listens to Reports and Leaves and builds a group → ports table
Multicast is forwarded only to the ports with members (and to router ports)
Without snooping, each group floods the whole VLAN as if it were broadcast
Requires a querier on the VLAN (a router or a 'querier' in the switch itself)
Timers (IGMPv2)
Query every 125 s; answer within 10 s
A member expires after 260 s without a report
Leave → group-specific query (2 × 1 s) → fast removal
Notes: IGMP (Internet Group Management Protocol) is used by multicast routers to find out, on each link, whether there are members of a group. Versions: IGMPv1 (RFC 1112): join through a membership report, silent leave (the router finds out by timeout); IGMPv2 (RFC 2236): Leave message, group-specific queries, querier election (lowest IP); IGMPv3 (RFC 3376): reports with source lists (INCLUDE/EXCLUDE), the basis of SSM, sent to 224.0.0.22. In IPv6, MLD does the same over ICMPv6: MLDv1 (RFC 2710) corresponds to IGMPv2 and MLDv2 (RFC 3810) to IGMPv3. The querier router sends periodic Queries (125 s) to 224.0.0.1 / ff02::1; hosts answer with reports. Switches perform IGMP/MLD snooping (RFC 4541): they listen to reports and forward the group only to the ports with members, avoiding flooding the entire VLAN.

## Slide 163: Dense mode vs. sparse mode
Dense mode
Assumes most users belong to the group (receivers everywhere)
Flood and prune: forwards out every port; branches without members send a Prune; the prune expires (3 min) and the flooding starts over
(S,G) state in every router, even without receivers
Protocols: DVMRP, MOSPF, PIM-DM (RFC 3973)
Today: small networks, labs
Sparse mode
Assumes few receivers, scattered across the network
Explicit join: routers with members join the tree; nothing flows without a request
Shared tree around a rendezvous point (RP) or core; optionally a per-source tree (SPT)
Protocols: CBT (RFC 2201, historical), PIM-SM (RFC 7761), SSM (RFC 4607), Bidir-PIM (RFC 5015)
Today: the industry standard
Criterion | Dense | Sparse
Initial traffic | Flooded to everyone | Only after a join
State in routers | In all of them | Only along the receivers' path
Scale | Small networks | Large networks and carriers
Notes: Two distribution models. Dense mode: assumes that most links have receivers; traffic is flooded across the whole network and branches without members are pruned (flood and prune), with the prune expiring periodically and the flooding starting over; simple, but it wastes bandwidth and state; protocols: DVMRP, MOSPF and PIM-DM. Sparse mode: assumes that receivers are few and scattered; nothing is sent until a router with members explicitly joins the tree (explicit join), built around a rendezvous point (RP) or a core; protocols: CBT (historical) and PIM-SM, dominant today, with its SSM and Bidir variants. In 2026 practically only PIM-SM/SSM gets deployed; PIM-DM survives in small networks and labs.

## Slide 164: Multicast routing algorithms and the RPF check
Algorithm | Idea | Status
Flooding | Resends out every interface; memory avoids duplicates | Historical
Spanning tree | One tree for all groups | Historical
RPB | Reverse Path Broadcasting: RPF check + resend out the other interfaces (MBone) | Conceptual basis
TRPB | RPB without sending to leaves without members (IGMP) | Conceptual basis
RPM | TRPB + prunes traveling up the tree; DVMRP, PIM-DM | In use (PIM-DM)
Steiner trees | Minimum total cost tree; NP-hard, unstable | Theoretical
CBT (Core Based Trees) | Shared tree per group around a core | Evolved into PIM-SM
RPF check (Reverse Path Forwarding)
S
source 10.1.1.5
R
R2
if1: RPF OK
if2: RPF fails
R's unicast table | Via
10.1.1.0/24 (source) | if1
Rule: accept the packet from S only if it arrived on the interface the unicast table uses to reach S (if1); copies arriving on another interface (if2) are discarded. Prevents loops without a TTL and is used by DVMRP, PIM-DM and PIM-SM (with the RP in place of the source on the shared tree).
Notes: Evolution of the algorithms (the original's list): flooding (resends out every interface, loops contained by remembering packets); spanning tree (a single tree for all groups, concentrates traffic); RPB, Reverse Path Broadcasting (used on the MBone: forwards a packet only if it arrived on the interface that leads back to the source along the shortest path, the RPF check, and resends it out the others); TRPB, Truncated RPB (does not send to leaf links without members, using IGMP); RPM, Reverse Path Multicasting (TRPB + prunes traveling up the tree: the basis of DVMRP and PIM-DM); Steiner trees (optimal in total cost, but NP-hard and unstable; never used in practice); CBT, Core Based Trees (one shared tree per group, rooted at a core; the conceptual predecessor of PIM-SM). The RPF check is the common element of all current protocols: a router accepts a multicast packet only if it arrives on the interface that the unicast table points to as the path toward the source (or toward the RP); this prevents loops without needing a TTL.

## Slide 165: Multicast routing protocols
Protocol | RFC | Model | How it works | Status in 2026
DVMRP | 1075 (1988) | Dense | Its own distance vector (RIP-like) for RPF; RPM; tunnels between islands; the MBone protocol | Historical
MOSPF | 1584 (1994) | Dense | OSPF extension: group membership LSAs; (S,G) tree computed in the LSDB | Historical
PIM-DM | 3973 (2005) | Dense | Flood and prune; RPF from the existing unicast table; no RP | Small networks
PIM-SM | 7761 (2016) | Sparse | Explicit join; shared tree (*,G) at the RP; switchover to the SPT (S,G) | Industry standard
PIM-SSM | 4607 (2006) | Sparse | Only (S,G); the receiver names the source (IGMPv3/MLDv2); 232/8, ff3x::/32; no RP | IPTV, market data
Bidir-PIM | 5015 (2007) | Sparse | Bidirectional shared tree; many-to-many; no (S,G) state | Niche (finance)
CBT | 2201 (1997) | Sparse | Shared tree around a core | Historical
MBone (1992 to ≈ 2000): a virtual network overlaid on the Internet, with DVMRP tunnels between multicast islands; it carried IETF meetings and NASA missions and reached thousands of subnets in dozens of countries. It disappeared with native multicast and, later, with unicast CDNs.
Notes: DVMRP (RFC 1075, 1988) was the protocol of the MBone: its own distance vector (similar to RIP, 32 hops) used only for RPF, with RPM and tunnels between islands; MOSPF (RFC 1584) extended OSPF with group membership LSAs, computing per-(source, group) trees inside the LSDB; both are historical. The MBone (Multicast Backbone, 1992) was a virtual network overlaid on the Internet to broadcast IETF meetings, space missions and concerts; it reached thousands of subnets and faded away in the late 1990s as native multicast and, later, unicast CDNs took over. The PIM family (Protocol Independent Multicast, developed by the IETF IDMR working group, as the 1999 notes pointed out) uses any unicast table for RPF: PIM-DM (RFC 3973, flood and prune), PIM-SM (RFC 7761, shared tree with an RP and optional SPT), SSM (RFC 4607, only (S,G) trees with 232/8 and IGMPv3, no RP) and Bidir-PIM (RFC 5015, bidirectional trees for many-to-many).

## Slide 166: PIM-SM in operation: RP, shared tree and SPT
S
source
R1
first hop
RP
rendezvous point (RP)
R3
shortest path
R4
last hop
Rx
receiver
1. Join (*,G) → RP
2. Register (unicast)
3. Join (S,G)
4. SPT: Join (S,G) along the shortest path (via R3)
1
Join on the shared tree
The receiver sends an IGMP Report; R4 sends a PIM Join (*,G) hop by hop up to the RP.
2
Source registration
R1 encapsulates the first packets from S in unicast PIM Register messages to the RP, which delivers them down the (*,G) tree.
3
Native path to the RP
The RP sends a Join (S,G) toward S and then a Register-Stop; traffic now flows natively.
4
Switchover to the SPT
R4 sends a Join (S,G) along the shortest path to S (via R3) and prunes the shared tree (Prune (S,G,rpt)).
RP discovery
Static; Auto-RP (Cisco); BSR (RFC 5059); Anycast-RP (RFC 4610) for redundancy
PIM: IP protocol 103; Hello on 224.0.0.13 / ff02::d
Notes: Typical flow: (1) a receiver sends an IGMP Report for group G; its last-hop router sends a PIM Join (*,G) toward the RP (rendezvous point), hop by hop, creating the shared tree; (2) source S starts transmitting; its first-hop router encapsulates the packets in unicast PIM Register messages to the RP; (3) the RP decapsulates, forwards down the shared tree and sends a Join (S,G) toward the source to receive the traffic natively, then a Register-Stop; (4) the last-hop router, on seeing traffic from S, may send a Join (S,G) directly toward the source (switchover to the shortest-path tree, SPT) and prune the shared tree. RP discovery: static, Auto-RP (Cisco), Bootstrap Router (RFC 5059) or Anycast-RP (RFC 4610) for redundancy. PIM uses IP protocol 103, Hello to 224.0.0.13 / ff02::d.

## Slide 167: RSVP: resource reservation (and what is left of it)
LEGACY
Tx
sender
R1
R2
merge
R3
R4
Rx1
receiver 1
Rx2
receiver 2
PATH: the sender describes the flow, hop by hop, down to each receiver
RESV from Rx1 and Rx2 travel up the tree
a single RESV (merged at R2)
Original RSVP (RFC 2205, IntServ)
Receiver-oriented reservations: PATH goes down, RESV goes up and merges at the first reserved branch
Soft per-flow state in every router: did not scale on the Internet
Real QoS went to DiffServ (DSCP) and overprovisioning
What survived: RSVP-TE (RFC 3209)
Signals MPLS traffic-engineering tunnels: explicit path, bandwidth, priority
Fast Reroute protection (RFC 4090)
Losing ground to Segment Routing (no signaling)
Notes: RSVP (Resource Reservation Protocol, RFC 2205, 1997) was designed so that applications could reserve bandwidth and delay along the path, in the integrated services model (IntServ). Its central characteristic, highlighted in the 1999 notes: reservations are receiver-oriented: the sender sends PATH messages describing the flow; each receiver answers with RESV, which travels up the multicast tree and merges with the reservations of other receivers at the first branch already reserved, so that a receiver's reservation does not need to reach the source. State is 'soft' (refreshed periodically). It scaled well in multicast, but requiring per-flow state in every router of the Internet did not scale; service differentiation ended up being done by DiffServ (DSCP). What survived was RSVP-TE (RFC 3209): the same protocol, with extensions, signals MPLS traffic-engineering tunnels with guaranteed bandwidth and explicit paths, including fast protection (FRR, RFC 4090). In 2026 even that is losing ground to Segment Routing, which needs no signaling.

## Slide 168: MPLS and VRRP
MODULE 2 | PART 9
Label switching: concepts, terminology, a LIB/LFIB example and current applications; gateway redundancy with VRRP
Notes: The last two topics of the original were presented in three slides (MPLS in two, VRRP in one, with a single sentence). Here they get the treatment their current importance justifies: MPLS is the foundation of carrier networks and VRRP is ubiquitous in corporate LANs.

## Slide 169: MPLS: label switching
MPLS header ('shim', RFC 3032): 32 bits between the link layer and IP
Ethernet header (EtherType 0x8847)
Label (20 bits)
TC (3)
S
TTL (8)
IP packet
Labels 0 to 15 are reserved (0 IPv4 explicit null, 1 router alert, 2 IPv6 explicit null, 3 implicit null = PHP); S = bottom of stack; the label stack allows nested tunnels
A
10.1.0.0/16
LER
ingress: push 20
LSR
swap 20 → 30
LSR
swap 30 → 40 (or PHP)
LER
egress: pop
C
10.3.0.0/16
IP
[20] IP
[30] IP
[40] IP
IP
LSP (Label Switched Path) for FEC '10.3.0.0/16' from the ingress LER to the egress LER
Operations
Push (ingress): classifies into the FEC and inserts a label
Swap (core): replaces the label using the LFIB, without reading IP
Pop (egress or penultimate hop, PHP): removes it
Why it still exists in 2026
No longer for speed (ASICs route IP at line rate)
For what the label makes possible: L3/L2 VPNs, traffic engineering, multiprotocol transport, Segment Routing
Notes: The 1999 notes explained the motivation: the Internet offered a best-effort service with software routing, little traffic engineering and limited aggregation; MPLS (Multiprotocol Label Switching, RFC 3031, 2001) attacked that by forwarding on short, fixed-length labels instead of IP prefixes. A label is a 32-bit 'shim' header inserted between the link layer and IP (EtherType 0x8847): a 20-bit label, a 3-bit traffic class (formerly EXP, RFC 5462), the S bit (bottom of stack) and an 8-bit TTL. The ingress edge router (ingress LER) classifies the packet into a FEC and pushes a label; the core routers (LSRs) only swap labels by looking up the LFIB, without looking at IP; the egress LER removes (pops) the label, often already at the penultimate hop (PHP). In 2026 the original speed gain is irrelevant (ASICs route IP at line rate); MPLS remains for what labels make possible: VPNs, traffic engineering and transport of any protocol ('multiprotocol').

## Slide 170: MPLS terminology
Term | Definition | Note
FEC | Forwarding Equivalence Class: packets forwarded the same way (e.g., same destination prefix, or prefix + class of service) | One label per FEC on each link
FIB | Forwarding Information Base: IP table with one row per FEC; at the ingress, says which label to push | Derived from the RIB
LSP | Label Switched Path: label-switched path established for each route (or tunnel) through the network | Unidirectional
LDP | Label Distribution Protocol (RFC 5036): distributes labels between neighbors (TCP/UDP 646), following the IGP | Alternatives: RSVP-TE, BGP, Segment Routing
LIB | Label Information Base: every label received from every neighbor, per FEC | Control plane
LFIB | Label Forwarding Information Base: incoming label → action (swap/pop) + outgoing label and interface | Data plane
LER / LSR | Label Edge Router (ingress/egress: push/pop) / Label Switch Router (core: swap) | 'PE' and 'P' in VPNs
PHP | Penultimate Hop Popping: the penultimate hop removes the label (implicit null, 3) | Saves a lookup at the egress
Notes: The five terms of the original, plus the ones that were missing. FEC (Forwarding Equivalence Class): a set of packets treated the same way, for example all those destined to a prefix, or to a prefix with a class of service; FIB: the IP forwarding table with one row per FEC, used at the ingress to decide which label to push; LSP: a label switched path, established for each route through the network; LDP (RFC 5036): the protocol that distributes labels between neighboring routers (TCP/UDP 646), one label per prefix of the IGP table; LIB: the label information base, which stores every label received from every neighbor for each FEC; LFIB: the compact table used by the data plane (incoming label → outgoing label, interface); LER and LSR: edge and core routers; PHP: removal of the label at the penultimate hop, saving a lookup at the egress. Alternatives to LDP for distributing labels: RSVP-TE (traffic engineering), BGP (VPNs, labels per prefix) and Segment Routing (labels advertised by the IGP).

## Slide 171: Example: FIB, LIB and LFIB of router R4
LAN A
R1
LAN B
R2
R4
if1
if2
R3
if3
LAN C
R5
if4
R4's FIB (IP → FEC → outgoing label)
Prefix (FEC) | Next hop | Interface | Outgoing label
10.3.0.0/16 | R3 | if3 | 30
10.1.0.0/16 | R1 | if1 | 10
10.2.0.0/16 | R2 | if2 | 11
R4's LIB (every label learned)
FEC | Neighbor | Its label
10.3.0.0/16 | R3 (if3) | 30
10.3.0.0/16 | R5 (if4) | 55
10.1.0.0/16 | R1 (if1) | 10
10.2.0.0/16 | R2 (if2) | 11
R4's LFIB (data plane)
Label in | If in | Action | Label out | If out
20 | if1 | swap | 30 | if3
21 | if2 | swap | 30 | if3
22 | if3 | swap | 10 | if1
23 | if3 | swap | 11 | if2
LIB = everything LDP learned; LFIB = only the path chosen by the IGP. A → C: arrives [20], leaves [30]; B → C: arrives [21], leaves [30].
Notes: Reproduction of the original's example (slide 182) with modern names. Topology: LAN A (10.1.0.0/16) behind R1, LAN B (10.2.0.0/16) behind R2, LAN C (10.3.0.0/16) behind R3; R4 is the core LSR, with interfaces 1 (to R1), 2 (to R2), 3 (to R3) and 4 (to R5, an alternate path). Through LDP, each router advertises to its neighbors the label it wants to receive for each FEC: R3 tells R4 'for 10.3.0.0/16 use label 30'; R4 chooses its own incoming label for the same FEC (20) and advertises it to R1 and R2. R4's LIB stores every label received (including those from R5, which are not on the best path); the LFIB only contains those on the path chosen by the IGP: label 20 in → swap 30, interface 3. Packets from A to C arrive at R4 with [20] and leave with [30]; those from B to C arrive with [21] (the label R4 advertised to R2) and also leave with [30].

## Slide 172: MPLS applications in 2026
UPDATED
Layer 3 VPN (RFC 4364)
One VRF per customer on the PEs; MP-BGP VPNv4/VPNv6 with route targets
Two-label stack: transport (IGP/LDP/SR) + VPN
The carriers' 'premium' corporate WAN
Layer 2 VPN and EVPN
Pseudowires (RFC 4447), VPLS (RFC 4762)
EVPN (RFC 7432): BGP control plane for MACs/IPs; also over VXLAN in data centers
Traffic engineering
RSVP-TE (RFC 3209): explicit paths, bandwidth, priorities
Fast Reroute (RFC 4090): protection within tens of ms
QoS across the core through the TC field (3 bits)
Segment Routing
No LDP or RSVP: segments advertised by the IGP (OSPF/IS-IS)
SR-MPLS (RFC 8660): label stack at the source; SRv6 (RFC 8986): list of IPv6 addresses
SR Policy with a controller (PCE); TI-LFA for protection
Notes: Four families of applications: (1) Layer 3 VPNs (RFC 4364): the provider carries the private networks of many customers over a common core, with VRF tables on the PEs, MP-BGP distributing VPNv4/VPNv6 prefixes with a label and route targets, and a two-label stack (transport + VPN); (2) Layer 2 VPNs: pseudowires (RFC 4447), VPLS (RFC 4762) and, today, EVPN (RFC 7432) with a BGP control plane, also over VXLAN; (3) traffic engineering: RSVP-TE tunnels (RFC 3209) with explicit paths, reserved bandwidth and FRR protection (RFC 4090) within tens of milliseconds; (4) Segment Routing: eliminates LDP and RSVP; the path is encoded at the source as a stack of segments (labels) advertised by the IGP (SR-MPLS, RFC 8660) or as a list of IPv6 addresses (SRv6, RFC 8986), with controller-driven traffic engineering (SR Policy). The 3-bit traffic class carries QoS across the core. Carrier MPLS remains the 'premium' corporate WAN, even with the advance of SD-WAN over the Internet.

## Slide 173: VRRP: default gateway redundancy
UPDATED
The problem
Hosts have one default gateway: if the router goes down, the LAN is cut off, even with another router available
Old solutions: Proxy ARP, ICMP Router Discovery, RIP on the hosts (all slow or fragile)
The solution: a virtual router
VRID (1 to 255) + virtual IP + virtual MAC 00-00-5E-00-01-{VRID} (IPv6: 00-00-5E-00-02-{VRID})
The hosts use the virtual IP as their gateway; whoever answers is the current master
Parameter | Value | Parameter | Value
Priority | 1 to 254 (255 = IP owner); default 100; highest wins | Advertisements | Master → 224.0.0.18 / ff02::12, IP protocol 112, every 1 s (v3: 100 cs)
Failover | ≈ 3 intervals without advertisements + skew → backup takes over (≈ 3 s; v3 sub-second) | After taking over | Gratuitous ARP / unsolicited NA with the virtual MAC: switches relearn the port
Preemption | Enabled by default (the highest-priority router takes back the role) | Versions | RFC 2338 (1998) → RFC 3768 v2 (2004) → RFC 5798 v3 (2010, IPv4 + IPv6)
Proprietary | HSRP (Cisco, RFC 2281), GLBP (Cisco, load balancing) | Tracking | Object tracking lowers the priority if the master's WAN goes down
Notes: The original summed it up as: 'protocol used as a backup router protocol'. The problem: hosts configured with a single default gateway are cut off if that router fails, even when another router is on the LAN (old solutions: Proxy ARP, ICMP Router Discovery, running RIP on the hosts). VRRP (Virtual Router Redundancy Protocol; RFC 2338 in 1998, RFC 3768 v2 in 2004, RFC 5798 v3 in 2010 with IPv6) creates a virtual router identified by a VRID (1 to 255), with a virtual IP address and a virtual MAC 00-00-5E-00-01-{VRID} (IPv4) or 00-00-5E-00-02-{VRID} (IPv6); the hosts use the virtual IP as their gateway. Among the physical routers, the one with the highest priority (1 to 254; 255 if it owns the IP; default 100) is elected master and sends advertisements to 224.0.0.18 / ff02::12 (IP protocol 112) every 1 s (v3: centiseconds); the others stand by and, if the advertisements stop for about 3 intervals, the highest-priority one takes over, sending a gratuitous ARP with the virtual MAC to update the switches. Preemption is enabled by default. Proprietary equivalents: HSRP (Cisco, informational RFC 2281, 1998) and GLBP (Cisco, with load balancing). Combined with interface tracking (object tracking), VRRP also reacts to the loss of the master's WAN link.

## Slide 174: VRRP in operation: a failover example
WAN
WAN
R1
R2
172.16.20.2
priority 120: MASTER
172.16.20.3
priority 100: backup
Virtual router VRID 10
IP 172.16.20.1
MAC 00-00-5E-00-01-0A
VRRP advertisements every 1 s → 224.0.0.18 (IP protocol 112)
LAN 172.16.20.0/24 (VLAN 20)
H1
gateway 172.16.20.1
H2
gateway 172.16.20.1
H3
gateway 172.16.20.1
H4
gateway 172.16.20.1
R1 fails
R2 gets no advertisements for ≈ 3 s → becomes master → answers for the virtual MAC → gratuitous ARP moves the MAC in the switches. Hosts notice nothing.
Best practices
Track the WAN (tracking); alternate the master per VLAN to use both routers; v3 for IPv6 and centisecond timers.
Notes: LAN 172.16.20.0/24 with two routers: R1 (172.16.20.2, priority 120) and R2 (172.16.20.3, priority 100) share VRID 10 with virtual IP 172.16.20.1 and virtual MAC 00-00-5E-00-01-0A. The hosts have gateway 172.16.20.1 and, when they ARP for it, receive the virtual MAC, answered by the master (R1). R1 sends advertisements every second; R2 listens. When R1 fails (or its WAN link goes down and tracking lowers its priority), R2 stops receiving advertisements, takes over as master after the detection interval, starts answering for the virtual MAC and sends a gratuitous ARP so that the switches move the virtual MAC to its port; the hosts notice nothing (same IP, same MAC in the cache). When R1 comes back, it takes over again through preemption. Design tip: alternate the master between VRIDs on different VLANs to use both routers; in IPv6, the same mechanism covers the default router advertised in RAs.

## Slide 175: Module 2 summary
TCP/IP and addressing
4-layer stack; 20-byte IPv4 header; protocol and port demultiplex
CIDR/VLSM replaced the classes; special addresses (RFC 6890)
Comparison under the mask and longest prefix match
Host behavior
Route determination (local/remote) + ARP/ND resolution
ARP for the destination if local, for the gateway if remote; Proxy ARP
MACs change at every hop; IPs do not; TTL decreases
Dynamic routing
RIP (small), EIGRP (DUAL), OSPF (areas, DR, LSAs), IS-IS
Administrative distance decides between sources; redistribute with care
BGP-4: path vector and policies between ASes
Control and operations
Ordered ACLs with an implicit deny; stateful firewalls
DHCP relay; directed broadcast turned off (RFC 2644)
Secondary addresses and unnumbered interfaces
IPv6
128 bits, 40-byte header, extension headers
ND and SLAAC instead of ARP and DHCP; no broadcast
Dual stack, tunnels, NAT64; > 50% at Google (2026)
Multicast, MPLS, VRRP
IGMP/MLD + PIM-SM/SSM; RPF; 01-00-5E mapping
MPLS: labels, LSP, LDP/SR; VPNs and TE
VRRPv3: virtual IP and MAC; transparent failover
Notes: Final recap. Suggested questions to wrap up: (1) what does a host do before sending the first packet to a destination? (2) what changes and what stays the same in a packet at each router? (3) why does OSPF need a DR on Ethernet but not on point-to-point links? (4) what is the difference between metric and administrative distance? (5) why does IPv6 have neither broadcast nor ARP? (6) what does an MPLS label make possible that plain IP does not? (7) how do hosts survive the failure of the VRRP master router?

## Slide 176: References: RFCs and sources by topic (1 of 2)
Topic | Main references
IPv4, TCP, UDP, ICMP | RFC 791 (IPv4), RFC 9293 (TCP, 2022), RFC 768 (UDP), RFC 792 (ICMP), RFC 1122 (host requirements), RFC 2474 and 3168 (DSCP/ECN), RFC 1191 (PMTUD)
IPv4 addressing | RFC 950 (subnets), RFC 4632 (CIDR), RFC 1918 (private), RFC 6598 (CGNAT), RFC 5737 (documentation), RFC 6890 (special), RFC 3021 (/31), RFC 1878
ARP, DHCP, DNS | RFC 826 (ARP), RFC 1027 (Proxy ARP), RFC 2131 (DHCP), RFC 1542 and 3046 (relay, option 82), RFC 2644 (directed broadcast), RFC 1034/1035 (DNS)
Ports and numbers | RFC 6335 (port ranges) and the IANA port and protocol number registries (successors of RFC 1060 / 1700)
RIP, EIGRP, AD | RFC 1058 (RIPv1), RFC 2453 (RIPv2), RFC 2080 (RIPng), RFC 4822 (authentication), RFC 7868 (EIGRP), RFC 2991/2992 (ECMP)
OSPF, IS-IS | RFC 2328 (OSPFv2), RFC 5340 (OSPFv3), RFC 5838 (AF), RFC 5709 and 7166 (authentication), RFC 5880 (BFD), ISO 10589 and RFC 1195/5308 (IS-IS)
BGP | RFC 4271 (BGP-4), RFC 4760 (MP-BGP), RFC 4456 (route reflectors), RFC 6793 (32-bit ASN), RFC 6996 (private ASN), RFC 1997/8092 (communities), RFC 6811 (ROV), RFC 7938 (BGP in data centers)
Notes: All RFCs are freely available at rfc-editor.org. For each topic, the main reference and the most recent ones.

## Slide 177: References: RFCs and sources by topic (2 of 2)
Topic | Main references
IPv6 | RFC 8200 (IPv6), RFC 4291 (addressing), RFC 5952 (notation), RFC 4193 (ULA), RFC 4861 (ND), RFC 4862 (SLAAC), RFC 7217 and 8981 (interface IDs), RFC 9915 (DHCPv6), RFC 8106 (RDNSS), RFC 4443 (ICMPv6), RFC 6437 (flow label), RFC 8504 (node requirements)
IPv6: security and transition | RFC 4301 to 4303 (IPsec), RFC 6105 (RA Guard), RFC 4890 (ICMPv6 filtering), RFC 4213 (dual stack), RFC 6146/6147 (NAT64/DNS64), RFC 6877 (464XLAT), RFC 8305 (Happy Eyeballs), RFC 8925
Multicast | RFC 1112, RFC 5771 (addresses), RFC 2365 (admin scope), RFC 2236 and 3376 (IGMP), RFC 2710 and 3810 (MLD), RFC 4541 (snooping), RFC 3973 (PIM-DM), RFC 7761 (PIM-SM), RFC 4607 (SSM), RFC 5015 (Bidir), RFC 5059 (BSR), RFC 1075 and 1584 (DVMRP, MOSPF, historical)
RSVP and MPLS | RFC 2205 (RSVP), RFC 3209 (RSVP-TE), RFC 4090 (FRR), RFC 3031/3032 (MPLS), RFC 5462 (TC field), RFC 5036 (LDP), RFC 4364 (L3VPN), RFC 7432 (EVPN), RFC 8660 (SR-MPLS), RFC 8986 (SRv6)
VRRP and redundancy | RFC 5798 (VRRPv3), RFC 3768 (VRRPv2), RFC 2338 (original), RFC 2281 (HSRP, informational)
Layer 2 and history | IEEE 802.1D/802.1Q/802.1w (bridging, VLANs, RSTP), RFC 7042 (documentation MACs), RFC 904 (EGP), RFC 1930 (AS), RFC 1001/1002 (NetBIOS over TCP), RFC 2166 (DLSw)
2026 data | Internet Society Pulse: '18 years later, IPv6 reaches majority' (Google: 50.10% on March 28, 2026); APNIC Labs IPv6 Capability Metrics, Brazil ≈ 59% (October 5, 2026); bgp.potaroo.net (global table)
Notes: Continued. The IPv6 adoption figures cited in the course come from the Internet Society Pulse (Google statistics) and from APNIC Labs; the global routing table figures, from bgp.potaroo.net (Geoff Huston).

## Slide 178: Thank you!
Rodolfo Nützmann | ronutz.com
TCP/IP: Concepts and IP Routing, 2026 edition (US English), based on the March 1999 course
Notes: Closing slide. Leave time for questions and for the final lab (traffic capture with Wireshark: ARP, DHCP, ND/RA, OSPF Hello, VRRP).